## Slide 1: High 4:4:4 16 Intra Profile Specification
JCTVC-R0128
Broadcast & Professional Research Labs
Sony Europe Ltd.
Karl Sharman
Sony Corp.

## Slide 2: Background
At the previous JCT-VC meeting in Valencia it was agreed that a new “High 4:4:4 16 Intra” profile would be planned for inclusion in one of the amendments resulting from this Sapporo meeting.
This profile would be aimed for high end professional content creation.
The profile would enable higher bit rates to be used.
The profile would be based upon Main 4:4:4 16 Intra.

## Slide 3: Changes relative to Main 4:4:4 16 Intra
  profile_idc
    There are no suitable constraint flags that would be interpreted by a version 2 decoder (the unused flags are all 0, and therefore unconstrained), and so the proposed mechanism by which the new profile is signalled is to use a new profile_idc.
HbrFactor is increased by a factor of 12.
  Instead of being equal to either 1 or 2, it would be equal to 12 or 24.
The value of cabac_bypass_alignment_enabled_flag would only be 1.
Decoders supporting this profile would not automatically be required to support any other profile.
Wavefront-parallel processing and tiles may be used simultaneously.

## Slide 4: Bit rates and compression ratios (1)
During RExt development, AHG18 test conditions tested down to 2:1 compression in order to faithfully encode 16-bit source video.
The 2:1 compression ratio is also common for high end content creation
  For example this is used in HDCAM-SR (which uses MPEG4-SStP) [See JCTVC-L0182].
It is proposed to use an HbrFactor 12 times larger than in Main.
  This means the Main tier of this High profile is only 3 or 4 times higher than the corresponding High tier in the Main profile.
This would then yield the following bit rates and compression ratios:

## Slide 5: Bit rates and compression ratios (2)
 | Profile | Tier | Level |  |  |  |  | 
 |  |  | 5 | 5.1 | 5.2 | 6 | 6.1 | 6.2
Maximum bit rate (Mbps) | Main 4:4:4 16 Intra | Main | 200 | 320 | 480 | 480 | 960 | 1920
 |  | High | 800 | 1280 | 1920 | 1920 | 3840 | 6400
 | High 4:4:4 16 Intra | Main | 2400 | 3840 | 5760 | 5760 | 11520 | 23040
 |  | High | 9600 | 15360 | 23040 | 23040 | 46080 | 76800
Compression ratio of 4:4:4 16-bit video at level-targeted sample rate at maximum bit rate | Main 4:4:4 16 Intra | Main | 64.2 | 80.2 | 107.0 | 107.0 | 107.0 | 107.0
 |  | High | 16.0 | 20.1 | 26.7 | 26.7 | 26.7 | 32.1
 | High 4:4:4 16 Intra | Main | 5.3 | 6.7 | 8.9 | 8.9 | 8.9 | 8.9
 |  | High | 1.3 | 1.7 | 2.2 | 2.2 | 2.2 | 2.7

## Slide 6: Bit rates and compression ratios (3)
This combination of Main and High profiles with Main and High tiers provides a wide range of bit rates and compression ratios.
The factor-of-12 increase is particularly important at level 5.2 (i.e. 4K 120P)
  there is no room to create a higher bit rate level 5.3 as the bit-rate must be less than that of level 6.
Of all levels, level 5.2 is of greatest immediate interest to the high end content creation industry (i.e. 4K 120P).

## Slide 7: Conclusion
The planned High 4:4:4 16 Intra profile, targeted for high end professional content creation, has been specified.
The necessary text changes relative to Version 2 are included in the accompanying document.