## Slide 1
Jill Boyce
JCTVC-R0158: Modifications to Scalable Main profile and general and profile-specific level limits

## Slide 2: Introduction
Modifications are proposed to Scalable Main profile and to the profile-specific level limits
Proposal fits within the general framework of JCTVC-Q1008 (output draft from the Valencia meeting)
  Signaling of (profile, tier, level) is done for each output layer set (OLS)
  Imposes stricter conformance limits, to ease burden on decoders

## Slide 3: Framework for discussion
In general, (profile, tier, level) signaling can impose bitstream constraints and decoder conformance requirements, and may impose them on individual layer and/or OLS
This contribution imposes the following:
  Bitstream constraints per OLS
  Bitstream constraints per layer
  Conformance requirements for OLS
In R0352, conformance requirements are imposed for individual layers rather than for the OLS

## Slide 4: Proposed profile-specific level limits
The constraints of the general and profile-specific level limits are unchanged from the design intent of JCTVC-Q1008 (from the adopted JCTVC-P0134), but have some editorial improvements to express the limits:
  Level constraints apply collectively to the OLS, with 2x values compared to the single layer constraints for picture size, sample rate, bit rate
  Level constraints apply individually to each layer, including picture size, sample rate, bit rate
    Avoid the possibility of a bitstream with 0.5x single layer capability in one layer and 1.5x single layer capability in the other

## Slide 5: Framework for discussion
Profile and level constraints for the OLS are primarily affected by 3 parameters
  M: Max number of layers
  N: Max number of layers in a dependency chain
  P: Factor by which bit rate, sample rate, picture size are increased for the OLS vs a single layer at that level

## Slide 6: Background
For AVC’s SVC
  N: Max number of layers in a dependency chain
    N = 3
In Valencia output draft
  M: Max number of layers
    M unconstrained, effectively limited to 63
  N: Max number of layers in a dependency chain
    N = 8
  P: Factor by which bit rate, sample rate, picture size are increased for the OLS vs a single layer at that level
    P = 2

## Slide 7: Proposal
  M: Max number of layers
    M = 4
  N: Max number of layers in a dependency chain
    N = 3
  P: Factor by which bit rate, sample rate, picture size are increase for the OLS vs a single layer at that level
    P = 2