## Slide 1: JCTVC-R0164 Bug fix in SHVC draft specification
P. Bordes (Technicolor), Y.He, Y.Ye (InterDigital Communications Inc)
18th JCT-VC Meeting: Sapporo, 30 June – 11 July 2014

## Slide 2: Current SHVC spec – CGS syntax
  Coding of LUTs residuals: colour_mapping_octants()
    Tree coding of color mapping table
      split_octant_flag : recursive call of colour_mapping_octants()
      locally control the color space sampling resolution in each octant
      reduce the signaling overhead & the number of syntax elements to parse

## Slide 3: Current SHVC spec – CGS syntax
  Example:
    cm_octant_depth=2, cm_y_part_num_log2=1 (YPartNum=2)
      LUT size = (1<<cm_octant_depth+cm_y_part_num_log2) x(1<<cm_octant_depth)x(1<<cm_octant_depth) = 8x4x4
      If depth=1, split_octant_flag=0 : 2 explicitly-encoded vertices/coeffs
      non-explicitly-encoded vertices/coeffs (?) predicted from explicitly-encoded vertices/coeffs (●) with residuals inferred to be 0

## Slide 4: Proposal SHVC spec – CGS syntax
  Proposal:
    Adapt the storage index of explicitly-encoded vertices/coeffs to the octant depth:
      Uniformly arrange the explicitly-encoded vertices/coeffs in the color mapping table
      The relative distance of non-explicitly-encoded vertices/coeffs derivation is reduced (R/8 vs R/4)
      The performance of the SHM encoder is not impacted

## Slide 5: Proposal SHVC spec – CGS syntax
  Proposed SHVC spec change