## Slide 1: JCTVC-R0191: SCCE1 Test 5.1: Combination tests of Test 2.1, Test 2.3 and Test 2.4
Xiaozhong Xu, Shan Liu and Shawmin Lei

## Slide 2: Outlines
Introduction
Test 5.1A: Test 2.1 + Test 2.3
Test 5.1B: Test 2.1 + Test 2.3 + Test 2.4
Simulation results
Conclusion

## Slide 3: SCCE1 Test 2.1, 2.3 and 2.4
Test 2.1: IntraBC as Inter PU (R0190)
Test 2.3: IntraBC merge mode (R0097)
Test 2.4: IntraBC AMP mode (R0241)
  Enabled at 16x16 CU (encoder option)

## Slide 4: 5.1A simulation results (1)
Anchor: SCM-1.0, lossy configuration
 | Test 2.1 |  |  | Test 2.3 |  |  | Test 5.1A |  | 
 | AI | RA | LD | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -3.9% | -2.0% | -1.6% | -7.2% | -4.3% | -3.3% | -9.3% | -5.8% | -4.9%
RGB, text & graphics with motion,720p | -2.0% | -1.5% | -0.9% | -4.0% | -2.7% | -1.0% | -5.2% | -3.8% | -2.1%
RGB, mixed content, 1440p | -1.6% | -1.2% | -0.7% | -2.9% | -1.8% | -1.0% | -4.2% | -2.6% | -2.0%
RGB, mixed content, 1080p | -1.9% | -1.3% | -0.9% | -2.9% | -1.9% | -1.3% | -4.5% | -3.0% | -1.7%
RGB, Animation, 720p | -0.1% | -0.1% | 0.1% | -0.1% | -0.1% | 0.0% | -0.3% | -0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | 0.1%
YUV, text & graphics with motion, 1080p | -4.6% | -1.8% | -1.2% | -7.4% | -4.4% | -3.2% | -9.7% | -5.6% | -4.4%
YUV, text & graphics with motion,720p | -2.4% | -1.5% | -0.5% | -4.3% | -2.8% | -1.2% | -5.7% | -3.8% | -1.4%
YUV, mixed content, 1440p | -1.8% | -0.9% | -0.3% | -3.1% | -1.9% | -1.2% | -4.1% | -2.4% | -1.4%
YUV, mixed content, 1080p | -2.1% | -1.3% | -0.5% | -3.2% | -2.3% | -0.8% | -4.6% | -3.2% | -1.6%
YUV, Animation, 720p | -0.1% | 0.1% | 0.2% | -0.2% | -0.1% | -0.1% | -0.2% | 0.1% | 0.3%
YUV, camera captured, 1080p | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.3%
Enc Time[%] | 100% | 98% | 97% | 110% | 99% | 99% | 120% | 101% | 98%
Dec Time[%] | 98% | 97% | 99% | 98% | 97% | 98% | 94% | 99% | 101%

## Slide 5: 5.1A simulation results (2)
Anchor: SCM-1.0, lossless configuration
 | Test 2.1 |  |  | Test 2.3 |  |  | Test 5.1A |  | 
 | AI | RA | LD | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | 1.8% | 0.8% | 1.0% | 5.6% | 3.8% | 3.9% | 6.8% | 4.7% | 5.0%
RGB, text & graphics with motion,720p | 0.2% | 0.1% | 0.1% | 1.1% | 0.3% | 0.2% | 1.3% | 0.4% | 0.2%
RGB, mixed content, 1440p | 0.2% | 0.0% | 0.0% | 2.1% | 0.4% | 0.2% | 2.1% | 0.4% | 0.3%
RGB, mixed content, 1080p | 0.2% | 0.0% | 0.0% | 2.1% | 0.4% | 0.2% | 2.3% | 0.4% | 0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 2.0% | 0.8% | 1.0% | 5.4% | 3.8% | 3.7% | 6.9% | 4.7% | 4.9%
YUV, text & graphics with motion,720p | 0.3% | 0.1% | 0.0% | 1.1% | 0.3% | 0.2% | 1.4% | 0.4% | 0.2%
YUV, mixed content, 1440p | 0.2% | 0.0% | 0.0% | 2.1% | 0.4% | 0.2% | 2.2% | 0.4% | 0.2%
YUV, mixed content, 1080p | 0.3% | 0.0% | 0.0% | 1.8% | 0.4% | 0.1% | 2.2% | 0.4% | 0.2%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 104% | 97% | 98% | 111% | 100% | 101% | 123% | 100% | 100%
Dec Time[%] | 100% | 98% | 101% | 103% | 104% | 99% | 96% | 97% | 100%

## Slide 6: 5.1B Simulation results (1)
Anchor: SCM-1.0 , lossy configuration
 | Test 5.1A |  |  | Test 2.4 |  |  | Test 5.1B |  | 
 | AI | RA | LD | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -9.3% | -5.8% | -4.9% | -0.8% | -0.6% | -0.4% | -9.9% | -6.4% | -5.4%
RGB, text & graphics with motion,720p | -5.2% | -3.8% | -2.1% | -0.5% | -0.6% | -0.4% | -5.7% | -4.2% | -2.2%
RGB, mixed content, 1440p | -4.2% | -2.6% | -2.0% | -0.5% | -0.5% | -0.4% | -4.6% | -3.0% | -2.2%
RGB, mixed content, 1080p | -4.5% | -3.0% | -1.7% | -0.6% | -0.4% | -0.4% | -4.8% | -3.2% | -2.0%
RGB, Animation, 720p | -0.3% | -0.1% | 0.0% | -0.2% | -0.2% | -0.1% | -0.4% | -0.2% | -0.1%
RGB, camera captured, 1080p | -0.1% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% | -0.1% | 0.2% | 0.2%
YUV, text & graphics with motion, 1080p | -9.7% | -5.6% | -4.4% | -1.1% | -0.8% | -0.6% | -10.6% | -6.2% | -4.9%
YUV, text & graphics with motion,720p | -5.7% | -3.8% | -1.4% | -0.7% | -0.5% | -0.2% | -6.2% | -4.3% | -1.9%
YUV, mixed content, 1440p | -4.1% | -2.4% | -1.4% | -0.5% | -0.3% | -0.4% | -4.5% | -2.6% | -1.5%
YUV, mixed content, 1080p | -4.6% | -3.2% | -1.6% | -0.6% | -0.5% | 0.2% | -5.0% | -3.5% | -1.8%
YUV, Animation, 720p | -0.2% | 0.1% | 0.3% | -0.2% | -0.1% | -0.2% | -0.5% | -0.1% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.1% | 0.3% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.3%
Enc Time[%] | 120% | 101% | 98% | 140% | 110% | 108% | 166% | 116% | 112%
Dec Time[%] | 94% | 99% | 101% | 100% | 101% | 101% | 95% | 101% | 101%

## Slide 7: 5.1B Simulation results (2)
Anchor: SCM-1.0 , lossless configuration
 | Test 5.1A |  |  | Test 2.4 |  |  | Test 5.1B |  | 
 | AI | RA | LD | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | 6.8% | 4.7% | 5.0% | 0.3% | 0.2% | 0.2% | 7.1% | 4.8% | 5.2%
RGB, text & graphics with motion,720p | 1.3% | 0.4% | 0.2% | 0.1% | 0.0% | 0.0% | 1.4% | 0.4% | 0.3%
RGB, mixed content, 1440p | 2.1% | 0.4% | 0.3% | 0.0% | 0.0% | 0.0% | 2.1% | 0.4% | 0.2%
RGB, mixed content, 1080p | 2.3% | 0.4% | 0.2% | 0.0% | 0.0% | 0.0% | 2.3% | 0.4% | 0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 6.9% | 4.7% | 4.9% | 0.2% | 0.2% | 0.2% | 7.2% | 4.9% | 5.0%
YUV, text & graphics with motion,720p | 1.4% | 0.4% | 0.2% | 0.1% | 0.0% | 0.0% | 1.5% | 0.4% | 0.2%
YUV, mixed content, 1440p | 2.2% | 0.4% | 0.2% | 0.0% | 0.0% | 0.0% | 2.2% | 0.4% | 0.2%
YUV, mixed content, 1080p | 2.2% | 0.4% | 0.2% | 0.1% | 0.0% | 0.0% | 2.2% | 0.4% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 123% | 100% | 100% | 170% | 107% | 105% | 196% | 115% | 110%
Dec Time[%] | 96% | 97% | 100% | 98% | 99% | 99% | 95% | 101% | 99%

## Slide 8: Conclusion
  The gains from Test 2.1, 2.3 and 2.4 are additive
  Test 2.4 (IntraBC AMP) is naturally enabled when IntraBC is coded as Inter PU
  Thank Canon for cross-checking (R0246)!