## Slide 1: JCTVC-R0203: Non-SCCE1: Default vector selection for intra block copy BV prediction
Xiaozhong Xu, Tzu-Der Chuang, Shan Liu and Shawmin Lei

## Slide 2: Outlines
Introduction
Proposed methods
  Method A: last two BVs
  Method B: last one BV + one preset BV
Changes in decoding process
Simulation results
Conclusion

## Slide 3: BV prediction in SCCE1
In SCM-1.0:
  Use last coded BV as predictor
  Use (-w, 0) when it is not available
In SCCE1 Test 3.1(R0185):
  Use left and above BV as predictors
  Use (-2w, 0) and (2w, 0) when candidates are not available
In SCCE1 Test 3.2(R0240):
  Use last 2 coded BV as predictors
  Use (-2w, 0) and (0, -2w) when candidates are not available
In SCCE1 Test 3.3(R0081):
  Use last 3 coded BV as predictors
  Use (-w, 0), (-2w, 0) and (-3w, 0) when candidates are not available
In SCCE1 Test 3.4(R0061):
  Use AMVP-like spatial prediction
  Use (-2w, 0) and (-w, 0) when candidates are not available

## Slide 4: Proposed method A:
Two BV candidates are derived from top and left spatial neighbors
Last two coded BVs are appended after that
  In case spatial candidates are not available or the same
Two default vectors (-2w, 0) and (-w, 0) are used at the beginning of each CTU

## Slide 5: Proposed method B:
Two BV candidates are derived from top and left spatial neighbors
Last one coded BVs is appended after that
  In case spatial candidates are not available or the same
Two default vectors (-2w, 0) and (-w, 0) are used to fill the candidate list

## Slide 6: Simulation results (1)
Platform: Test 3.4 without further optimization
 | Last 2 BV w/o OPT. |  |  | Last 1 BV w/o OPT. |  | 
 | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -3.9% | -1.8% | -1.2% | -4.0% | -1.8% | -1.0%
RGB, text & graphics with motion,720p | -1.8% | -1.1% | -0.5% | -2.0% | -1.3% | -0.6%
RGB, mixed content, 1440p | -1.4% | -0.9% | -0.6% | -1.4% | -0.9% | -0.5%
RGB, mixed content, 1080p | -1.7% | -1.0% | -0.4% | -1.8% | -1.0% | -0.6%
RGB, Animation, 720p | -0.1% | -0.1% | 0.0% | -0.1% | -0.2% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -4.6% | -2.0% | -1.1% | -4.8% | -2.0% | -1.0%
YUV, text & graphics with motion,720p | -2.3% | -1.5% | -0.7% | -2.5% | -1.6% | -0.6%
YUV, mixed content, 1440p | -1.8% | -1.0% | -0.7% | -1.8% | -0.9% | -0.4%
YUV, mixed content, 1080p | -2.1% | -1.4% | -0.4% | -2.1% | -1.5% | -0.3%
YUV, Animation, 720p | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% | 96% | 96% | 99% | 96% | 95%
Dec Time[%] | 100% | 101% | 100% | 100% | 103% | 99%

## Slide 7: Simulation results (2)
Platform: Test 3.4 with encoder optimization (as in JCTVC-R0081, config. 2)
 | Last 2 BV with OPT. |  |  | Last 1 BV with OPT. |  | 
 | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -7.7% | -3.9% | -2.6% | -7.5% | -3.6% | -2.3%
RGB, text & graphics with motion,720p | -4.4% | -2.9% | -1.1% | -4.4% | -2.8% | -1.1%
RGB, mixed content, 1440p | -3.1% | -2.0% | -1.1% | -3.0% | -1.8% | -0.7%
RGB, mixed content, 1080p | -3.7% | -2.3% | -1.1% | -3.6% | -2.2% | -0.9%
RGB, Animation, 720p | -0.2% | -0.2% | 0.0% | -0.2% | -0.1% | -0.1%
RGB, camera captured, 1080p | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
YUV, text & graphics with motion, 1080p | -8.3% | -3.8% | -2.3% | -8.2% | -3.6% | -2.0%
YUV, text & graphics with motion,720p | -5.2% | -3.3% | -1.2% | -5.1% | -3.3% | -1.0%
YUV, mixed content, 1440p | -3.6% | -2.1% | -1.2% | -3.5% | -2.0% | -0.9%
YUV, mixed content, 1080p | -4.0% | -2.8% | -0.8% | -3.9% | -2.7% | -1.0%
YUV, Animation, 720p | -0.3% | 0.0% | 0.0% | -0.2% | -0.1% | -0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 96% | 96% | 96% | 97% | 97% | 96%
Dec Time[%] | 99% | 101% | 99% | 100% | 99% | 100%

## Slide 8: Conclusion
Use previously coded BV(s) in addition to spatial neighbor predictors
Experimental results showed in method A
  BD rate reduction of 3.9%/4.6%, 1.8%/2.0%, 1.2%/1.1% in 1080p TGM class, for AI, RA and LD configurations
  Encoding and decoding time changes are negligible
With more encoder optimization (as in R0081, Canon’s encoder config. 2)
  BD rate reduction of 7.7%/8.3%, 3.9%/3.8%, 2.6%/2.3% in 1080p TGM class, for AI, RA and LD configurations
  Encoding and decoding time changes are negligible
Recommend to adopt or further study in CE
  Thank MERL for cross-checking (R0243)!