## Slide 1: JCTVC-R0204: Non-SCCE1: PU intra block copy with flipping mode
Xiaozhong Xu, Shan Liu, Jing Ye, Kai Zhang and Shawmin Lei

## Slide 2: Outlines
Introduction
Proposed method
Changes in syntax and semantics
Simulation results
Conclusion

## Slide 3: IntraBC with flipping
Proposed in the previous meeting
  JCTVC-Q0116 (SCCE1 test4.1)
  JCTVC-Q0097 (SCCE1 test4.2)
  IntraBC flipping for 2Nx2N CU/PU

## Slide 4: Proposed method
The use of IntraBC is signaled at PU
The use of IntraBC with flipping mode is signaled at PU
  One flag to signal the flipping direction (vertical or horizontal)

## Slide 5: Syntax changes
In coding_unit()
  intra_bc_flag is moved from CU to PU
  pred_mode_flag is signaled in intra slice
    pred_mode_flag = MODE_INTER in intra slice infers IntraBC mode
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if( transquant_bypass_enabled_flag ) | 
cu_transquant_bypass_flag | ae(v)
if( slice_type != I ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
nCbS = ( 1 << log2CbSize ) | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( intra_block_copy_enabled_flag ) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( slice_type != I && !intra_bc_flag[ x0 ][ y0 ] intra_block_copy_enabled_flag) | 
pred_mode_flag | ae(v)
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ intra_bc_flag[ x0 ][ y0 ] ¦ ¦ log2CbSize = = MinCbLog2SizeY ) | 
part_mode | ae(v)

## Slide 6: Syntax changes
In prediction_unit()
prediction_unit( x0, y0, nPbW, nPbH ) { | Descriptor
if( cu_skip_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
if(slice_type != I && intra_block_copy_enabled_flag) | 
intra_bc_flag | ae(v)
if( intra_bc_flag ) { | 
symmetric_ibc_flag | ae(v)
if(symmetric_ibc_flag) | 
symmetric_ibc_type | ae(v)
mvd_coding( 0, 0, 2 ) | 
} else { | 
merge_flag[ x0 ][ y0 ] | ae(v)
if( merge_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { | 
... | 
} | 
} | 

## Slide 7: Syntax changes
In mvd_coding()
mvd_coding( x0, y0, refList ) { | Descriptor
if(!symmetric_ibc_flag[x0][y0]¦¦ symmetric_ibc_type[x0][y0]!=1) | 
abs_mvd_greater0_flag[ 0 ] | ae(v)
if(!symmetric_ibc_flag[x0][y0]¦¦ symmetric_ibc_type[x0][y0]!=0) | 
abs_mvd_greater0_flag[ 1 ] | ae(v)
if( abs_mvd_greater0_flag[ 0 ] ) | 
abs_mvd_greater1_flag[ 0 ] | ae(v)
if( abs_mvd_greater0_flag[ 1 ] ) | 
abs_mvd_greater1_flag[ 1 ] | ae(v)
if( abs_mvd_greater0_flag[ 0 ] ) { | 
if( abs_mvd_greater1_flag[ 0 ] ) | 
abs_mvd_minus2[ 0 ] | ae(v)
mvd_sign_flag[ 0 ] | ae(v)
} | 
if( abs_mvd_greater0_flag[ 1 ] ) { | 
if( abs_mvd_greater1_flag[ 1 ] ) | 
abs_mvd_minus2[ 1 ] | ae(v)
mvd_sign_flag[ 1 ] | ae(v)
} | 
} | 

## Slide 8: Simulation results (1)
Anchor: SCM-1.0, lossy coding
 | PU IBC with flipping |  |  | SCCE1 Test 4.1 |  | 
 | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -2.6% | -2.2% | -2.0% | -1.3% | -0.9% | -0.5%
RGB, text & graphics with motion,720p | -1.4% | -1.2% | -1.1% | -0.8% | -0.6% | -0.4%
RGB, mixed content, 1440p | -1.5% | -1.1% | -0.5% | -1.0% | -0.4% | -0.3%
RGB, mixed content, 1080p | -1.2% | -0.9% | -1.0% | -0.8% | -0.4% | -0.5%
RGB, Animation, 720p | -0.1% | -0.2% | -0.1% | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -2.4% | -1.6% | -1.3% | -1.2% | -0.7% | -0.5%
YUV, text & graphics with motion,720p | -1.4% | -1.0% | -0.6% | -0.9% | -0.6% | -0.3%
YUV, mixed content, 1440p | -1.4% | -0.6% | -0.3% | -1.0% | -0.4% | -0.3%
YUV, mixed content, 1080p | -1.3% | -1.0% | -0.3% | -0.8% | -0.5% | 0.1%
YUV, Animation, 720p | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% | 97% | 96% | 102% | 99% | 98%
Dec Time[%] | 99% | 97% | 97% | 99% | 99% | 99%

## Slide 9: Simulation results (2)
Anchor: SCM-1.0, lossless coding
 | PU IBC with flipping |  |  | SCCE1 Test 4.1 |  | 
 | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | 2.4% | 1.4% | 1.5% | 1.8% | 1.0% | 1.0%
RGB, text & graphics with motion,720p | 0.7% | 0.3% | 0.3% | 0.5% | 0.2% | 0.2%
RGB, mixed content, 1440p | 0.3% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.4% | 0.1% | 0.0% | 0.2% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 2.7% | 1.5% | 1.5% | 1.9% | 1.0% | 0.9%
YUV, text & graphics with motion,720p | 0.7% | 0.3% | 0.3% | 0.5% | 0.3% | 0.2%
YUV, mixed content, 1440p | 0.3% | 0.1% | 0.0% | 0.3% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.4% | 0.1% | 0.0% | 0.3% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 102% | 97% | 96% | 104% | 98% | 99%
Dec Time[%] | 99% | 98% | 98% | 99% | 100% | 101%

## Slide 10: Conclusion
In this proposal
  IntraBC on/off is signaled for each PU
  IntraBC flipping on/off is signaled for each PU
    2.6%/2.4% gain for AI, 2.2%/1.6% gain for RA, 2.0%/1.3% gain for LD, for TGM 1080p sequences in lossy configuration
Recommend for adoption or further study in CE
Thank Microsoft for cross-checking (R0291)!