## Slide 1
Xingyu Zhang, Robert Cohen
Mitsubishi Electric Research Laboratories
July 2014
JCTVC-R0218
trType for Intra Block Copy for screen content coding

## Slide 2: Introduction
Currently the DST-like (trType=1) transform is used for 4x4 intra block copy and for the directional, DC, and Planar intra prediction modes. The DCT-like transform (trType=0) is used for larger TUs.
Concept behind DST: prediction error is small near boundary of prediction; becomes larger moving away from boundary.
IBC, however, predicts using a displaced block. The residual is more like an inter-predicted block.
Proposal: use the existing DCT-like transform for 4x4 IBC
No other changes to IBC, i.e. it is still an intra mode

## Slide 3: Changes to text
8.6.4 Transformation process for scaled transform coefficients
8.6.4.1 General
…
Depending on the values of CuPredMode[ xTbY ][ yTbY ], nTbS, intra_bc_flag[ xTbY ][ yTbY ] and cIdx, the variable trType is derived as follows:
– If CuPredMode[ xTbY ][ yTbY ] is equal to MODE_INTRA, nTbS is equal to 4, intra_bc_flag[ xTbY ][ yTbY ] is equal to 0, and cIdx is equal to 0, trType is set equal to 1.
– Otherwise, trType is set equal to 0.
…

## Slide 4: Lossy compression performance (AI), anchor SCM 1.0
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
RGB, text & graphics with motion,720p | -0.1% | -0.1% | -0.1%
RGB, mixed content, 1440p | -0.2% | -0.1% | -0.1%
RGB, mixed content, 1080p | -0.2% | -0.1% | -0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.1% | 0.0% | 0.0%
YUV, text & graphics with motion,720p | -0.1% | 0.0% | -0.2%
YUV, mixed content, 1440p | -0.1% | 0.0% | 0.0%
YUV, mixed content, 1080p | -0.1% | -0.1% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  | 
Dec Time[%] | 94% |  | 

## Slide 5: Lossy compression performance (RA,LB), anchor SCM 1.0
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
RGB, text & graphics with motion,720p | -0.1% | 0.0% | 0.0%
RGB, mixed content, 1440p | -0.2% | -0.1% | -0.1%
RGB, mixed content, 1080p | -0.2% | -0.1% | -0.1%
RGB, Animation, 720p | 0.0% | -0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.1% | 0.0% | 0.0%
YUV, text & graphics with motion,720p | -0.1% | 0.0% | 0.0%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | -0.1% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | -0.1% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.1% | 0.2%
Enc Time[%] | 99% |  | 
Dec Time[%] | 82% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.1%
RGB, text & graphics with motion,720p | -0.1% | -0.1% | 0.1%
RGB, mixed content, 1440p | -0.1% | -0.4% | -0.1%
RGB, mixed content, 1080p | -0.1% | 0.4% | -0.3%
RGB, Animation, 720p | 0.1% | 0.0% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | 0.1% | 0.4% | 0.1%
YUV, mixed content, 1440p | 0.0% | -0.4% | -0.1%
YUV, mixed content, 1080p | -0.1% | -0.3% | 0.3%
YUV, Animation, 720p | 0.0% | -0.2% | -0.3%
YUV, camera captured, 1080p | 0.0% | -0.1% | -0.1%
Enc Time[%] | 99% |  | 
Dec Time[%] | 76% |  | 

## Slide 6: Method 2 lossy compression performance (AI), anchor SCM 1.0 (trType=0 for all 4x4 intra-coded TUs)
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.4% | -0.3% | -0.3%
RGB, text & graphics with motion,720p | -0.2% | 0.0% | 0.0%
RGB, mixed content, 1440p | -0.3% | 0.0% | 0.0%
RGB, mixed content, 1080p | -0.3% | 0.0% | -0.1%
RGB, Animation, 720p | -0.5% | 0.0% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.3% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | -0.3% | -0.1% | -0.3%
YUV, mixed content, 1440p | -0.1% | 0.1% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.2% | 0.2%
YUV, Animation, 720p | 0.0% | 0.0% | 0.1%
YUV, camera captured, 1080p | 0.3% | -0.2% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 98% |  | 

## Slide 7: Method 2: Lossy compression performance (RA,LB), anchor SCM 1.0 (trType=0 for all 4x4 intra-coded TUs)
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.2% | -0.1% | -0.1%
RGB, text & graphics with motion,720p | -0.2% | 0.0% | 0.0%
RGB, mixed content, 1440p | -0.4% | -0.1% | 0.0%
RGB, mixed content, 1080p | -0.1% | 0.2% | -0.1%
RGB, Animation, 720p | -0.4% | -0.2% | -0.1%
RGB, camera captured, 1080p | 0.0% | -0.1% | -0.1%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | -0.2% | -0.2% | -0.1%
YUV, mixed content, 1440p | -0.1% | 0.1% | -0.1%
YUV, mixed content, 1080p | -0.2% | 0.0% | 0.2%
YUV, Animation, 720p | 0.1% | -0.3% | 0.1%
YUV, camera captured, 1080p | 0.1% | -0.3% | -0.2%
Enc Time[%] | 99% |  | 
Dec Time[%] | 82% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.1% | -0.1% | 0.0%
RGB, text & graphics with motion,720p | -0.1% | 0.0% | 0.0%
RGB, mixed content, 1440p | -0.4% | -0.3% | -0.2%
RGB, mixed content, 1080p | -0.2% | 0.0% | -0.2%
RGB, Animation, 720p | 0.0% | -0.1% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | -0.1%
YUV, text & graphics with motion, 1080p | -0.1% | 0.0% | -0.1%
YUV, text & graphics with motion,720p | -0.2% | 0.6% | -0.3%
YUV, mixed content, 1440p | -0.1% | -0.3% | 0.0%
YUV, mixed content, 1080p | 0.0% | -0.1% | 0.9%
YUV, Animation, 720p | 0.1% | -0.4% | -0.3%
YUV, camera captured, 1080p | 0.0% | 0.0% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 78% |  | 

## Slide 8: Conclusions
For screen content sequences, the nature of the prediction residual does not have the characteristics that residuals with camera-captured material had, making them less of a match to the DST
Intra block copy produces a residual from a translated block, again not matched to the DST
Propose to use the DCT for all IBC block sizes
Thanks to MediaTek for performing a cross-check (JCTVC-R0199)