## Slide 1: On reference position calculation (JCTVC-R0220)
Tomoyuki Yamamoto, Takeshi Tsukuba, Tomohiro Ikai
SHARP Corporation

## Slide 2: Introduction
  AHG13 recommended several modifications including
    Reference layer offset
    Luma/chroma phase
    Moving reference position information from SPS to PPS
  Three proposals on top of AHG 13 recommendation
    Reference position calculation for pixels outside of scaled ref offset window
    Signalling of ref offset, scaled ref offset, and luma/chroma phase
    Infer ref offset from scaled ref offset

## Slide 3: Proposal 1: reference position info signalling
pps_multilayer_extension( ) { | Descriptor
... | 
num_scaled_ref_layer_offsets | ue(v)
for( i = 0; i < num_scaled_ref_layer_offsets; i++) { | 
scaled_ref_layer_id[ i ] | u(6)
scaled_ref_layer_left_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_top_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_right_offset[ scaled_ref_layer_id[ i ] ] | se(v)
scaled_ref_layer_bottom_offset[ scaled_ref_layer_id[ i ] ] | se(v)
} | 
num_ref_layer_offsets | ue(v)
for( i = 0; i < num_ ref_layer_offsets; i++) { | 
ref_offset_layer_id[ i ] | u(6)
ref_layer_offset_present_flag[ i ] | u(1)
if ( ref_layer_offset_present_flag[ i ] ) { | 
ref_layer_left_offset[ scaled_ref_layer_id[ i ] ] | se(v)
ref_layer_top_offset[ scaled_ref_layer_id[ i ] ] | se(v)
ref_layer_right_offset[scaled_ref_layer_id[ i ] ] | se(v)
ref_layer_bottom_offset[ scaled_ref_layer_id[ i ] ] | se(v)
} | 
} | 
num_resample_phase | ue(v)
for( i = 0; i < num_resample_phase; i++) { | 
resample_phase_layer_id[ i ] | u(6)
resample _phase_present_flag[ i ] | u(1)
if ( resample_phase_present_flag[ i ]) { | 
phase_hor_luma[ scaled_ref_layer_id [ i ] ] | ue(v)
phase_ver_luma[ scaled_ref_layer_id [ i ] ] | ue(v)
phase_hor_chroma[ scaled_ref_layer_id [ i ] ] | ue(v)
phase_ver_chroma[ scaled_ref_layer_id [ i ] ] | ue(v)
} | 
} | 
} | 
... | 
} | 
Benefit: (1) avoid sending the same reference layer id three times in typical situation
(2) less syntax elements
Signal ref offset, scaled ref offset, phase in a single loop with common ref layer id instead of independent loops

## Slide 4: Proposal 2: Infer reference layer offset
Benefit: - avoid signalling same offset values for scaled ref offset and ref offset in SNR cases
RefLayerLeftOffset = (((RefPicWidthInSamplesY * scaled_ref_layer_left_offset[rLIdx]) / CurPicWidthInSamplesY) + (ref_layer_left_offset[rLIdx])) * RefLayerSubWidthC
Proposal:
- Referece layer offsets are predicted with scaled ref offset

## Slide 5: Proposal 3: clipping in ref position calculation
Motivation: - allow utilizing pixels outside of “RefRegion” in reference picture
Proposal: Clipping in EL domain is omitted in reference layer position calculation process
EL clip
BL clip

## Slide 6: Comparison of clip position options
Possible options for reference position constraints: Option A1: "restrict within reference offset window extended with filter tap length" (AHG 13 text)
Option A2: "restrict within reference offset window"
Option B: "restrict within reference layer picture“ (proposal in the contribution)
 | EL Clip | BL Clip | ref pos restriction | prediction note | complexity note
A1 | scaled ref window boundary | ref pic boundary | “ref offset window” + “filter tap length” |  | most friendly for “BL padding” implementation
A2 | scaled ref window boundary | ref window boundary | “ref offset window” | good when outside of ref offset window contains meaningless pixel values | 
B | no clip | ref pic boundary | “ref layer picture” | good when outside of ref offset window contains meaningful pixel values | Less clip operation

## Slide 7: Text change for option A2
The sample value tempArray[ n ] with n = 0 … 7, is derived as follows:
refH = RefLayerPicHeightInSamplesY
refW = RefLayerPicWidthInSamplesY
offT = Clip3( 0, refH − 1, refLayerTopOffset ) offB = Clip3( 0, refH − 1, refH− 1− refLayerBottomOffset ) offL = Clip3( 0, refW − 1, refLayerLeftOffset ) offR = Clip3( 0, refW − 1, refW− 1− refLayerRightOffset )
yPosRL = Clip3( offT, offB, yRef + n − 3 ) (H‑47) tempArray[ n ] = ( fL[ xPhase, 0 ] * rlPicSampleL[ Clip3( offL, offR, xRef − 3), yPosRL ] + fL[ xPhase, 1 ] * rlPicSampleL[ Clip3( offL, offR, xRef − 2), yPosRL ] + fL[ xPhase, 2 ] * rlPicSampleL[ Clip3( offL, offR, xRef − 1), yPosRL ] + fL[ xPhase, 3 ] * rlPicSampleL[ Clip3( 0, offL, offR, xRef ), yPosRL ] + fL[ xPhase, 4 ] * rlPicSampleL[ Clip3( 0, offL, offR, xRef + 1), yPosRL ] + (H‑49) fL[ xPhase, 5 ] * rlPicSampleL[ Clip3( 0, offL, offR, xRef + 2), yPosRL ] + fL[ xPhase, 6 ] * rlPicSampleL[ Clip3( 0, offL, offR, xRef + 3), yPosRL ] + fL[ xPhase, 7 ] * rlPicSampleL[ Clip3( 0, offL, offR, xRef + 4), yPosRL ] ) >> shift1
H.8.1.4.1.3 Luma sample interpolation process

## Slide 8: Text change for option B
Input to this process is the reference luma sample array rlPicSampleL.
Output of this process is the resampled luma sample array rsPicSampleL.
The variables leftStartL, rightEndL, topStartL, and bottomEndL are derived as follows:
leftStartL = ScaledRefLayerLeftOffset rightEndL = CurPicWidthInSamplesY − ScaledRefLayerRightOffset (H‑36) topStartL = ScaledRefLayerTopOffset bottomEndL = CurPicHeightInSamplesY − ScaledRefLayerBottomOffset (H‑37)
The luma samples rsPicSampleL[ xP ][ yP ] with ( xP = 0 ... CurPicWidthInSamplesY − 1, yP = 0 ... CurPicHeightInSamplesY − 1) are derived by invoking the luma sample interpolation process specified in subclause H.8.1.4.1.3 with rlPicSampleL and luma sample location (xP, yP) ( Clip3( leftStartL, rightEndL − 1, xP ), Clip3( topStartL, bottomEndL − 1, yP ) ) given as inputs and rsPicSampleL[ xP ][ yP ] as output.
H.8.1.4.1.1 Resampling process of luma sample values.