## Slide 1: Palette Table Prediction by the Nearest Palette Table JCTVC-R0266
C. –H. Hung, C. –L. Lin, Y. –J. Chang, C. –C. Lin, J. –S. Tu
ITRI International

## Slide 2: Contents
Introduction
  Palette Table Prediction
Proposed Algorithms
Experimental Results
Conclusion

## Slide 3: Palette Table Prediction
Current predictor for palette tables
  Last decoded palette table
  May be far away from current CU
  Need to reset predictor when processing next row of LCUs
LCU
LCU
LCU
LCU
LCU
LCU
LCU
LCU
LCU
LCU
LCU
LCU
Far away
Low correlation
Reset predictor
Current
palette-coded CU
Last
palette-coded CU
Last
palette-coded CU
Current
palette-coded CU
The Nearest
palette-coded CU
The Nearest
palette-coded CU

## Slide 4: Contents
Introduction
Proposed Algorithms
  Adopting neighboring palette tables as predictor
Experimental Results
Conclusion

## Slide 5: Proposed Algorithms (1)
For a palette-coded CU
  Storing its palette table and center coordinates
  These two information will be propagated together by other non-palette-coded Cus
  Adopt the palette table stored in the nearest CU as predictor
For a non-palette-coded CU
  Propagating above two information from the nearest CU

## Slide 6: Proposed Algorithms (2)
The Nearest CU
  Selecting from current CU’s above and left CUs
  Center coordinate of current CU (XC, YC)
  Center coordinate stored in left CU (XL, YL)
  Center coordinate stored in above CU (XA, YA)
  Left distance DL = abs(XC - XL) + abs(YC - YL)
  Above distance DA = abs(XC - XA) + abs(YC - YA)
  The nearest CU is the CU resulting in minimum distance
Current CU
Above CU
Left CU
  (XC, YC)
  (XL, YL)
  (XA, YA)
  DL
  DA
  If left CU is palette-coded, (XL, YL) is its center
  Otherwise, (XL, YL) is propagated from the nearest CU
  (XA, YA) is processed similarly as above

## Slide 7: Contents
Introduction
Proposed Algorithms
Experimental Results
Conclusion

## Slide 8: Experimental Results
Anchor
  Anchor 1: SCM-1.0
  Anchor 2: SCCE3 = SCM-1.0 + JCTVC-Q0094 + bug-fixes of JCTVC-Q0047
Test condition
  JCTVC-Q1015
  JCTVC-Q1123

## Slide 9: Anchor = SCCE3, Lossy
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
IBC searches 2 left CTUs | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -1.2% | -1.2% | -1.2% | -0.8% | -0.7% | -0.7% | -0.5% | -0.5% | -0.5%
RGB, text & graphics with motion,720p | -1.0% | -1.0% | -1.0% | -0.8% | -0.8% | -0.9% | -0.4% | -0.5% | -0.4%
RGB, mixed content, 1440p | -0.2% | -0.1% | -0.2% | -0.1% | -0.2% | -0.2% | -0.1% | 0.0% | -0.1%
RGB, mixed content, 1080p | -0.2% | -0.2% | -0.2% | -0.1% | -0.2% | -0.2% | -0.3% | -0.3% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -1.1% | -1.1% | -1.1% | -0.6% | -0.7% | -0.7% | -0.4% | -0.4% | -0.4%
YUV, text & graphics with motion,720p | -0.9% | -1.0% | -1.0% | -0.7% | -0.7% | -0.8% | -0.3% | 0.0% | -0.1%
YUV, mixed content, 1440p | -0.2% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | 0.0%
YUV, mixed content, 1080p | -0.3% | -0.4% | -0.3% | -0.2% | -0.3% | -0.3% | -0.2% | -0.9% | -0.2%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 96% |  |  | 97% |  |  | 96% |  | 
Dec Time[%] | 112% |  |  | 103% |  |  | 103% |  | 
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
IBC searches full frame | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.8% | -0.8% | -0.8% | -0.5% | -0.5% | -0.5% | -0.3% | -0.4% | -0.3%
RGB, text & graphics with motion,720p | -0.7% | -0.7% | -0.7% | -0.6% | -0.6% | -0.6% | -0.3% | -0.5% | -0.4%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.2% | -0.1% | -0.1%
RGB, mixed content, 1080p | -0.1% | -0.1% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | -0.3% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.8% | -0.8% | -0.8% | -0.5% | -0.5% | -0.5% | -0.3% | -0.4% | -0.4%
YUV, text & graphics with motion,720p | -0.6% | -0.7% | -0.8% | -0.5% | -0.5% | -0.6% | 0.0% | -0.1% | 0.0%
YUV, mixed content, 1440p | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | -0.3% | -0.3% | -0.2%
YUV, mixed content, 1080p | -0.2% | -0.2% | -0.1% | -0.1% | -0.3% | -0.1% | -0.4% | -0.8% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.2% | -0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 93% |  |  | 96% |  |  | 142% |  | 
Dec Time[%] | 110% |  |  | 100% |  |  | 173% |  | 

## Slide 10: Anchor = SCM 1.0, Lossy
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
IBC searches full frame | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -11.1% | -11.1% | -11.0% | -6.7% | -6.9% | -7.1% | -4.2% | -4.7% | -4.7%
RGB, text & graphics with motion,720p | -6.3% | -5.6% | -6.0% | -6.2% | -5.2% | -5.7% | -4.3% | -3.9% | -4.2%
RGB, mixed content, 1440p | -1.2% | -1.1% | -1.s0% | -1.4% | -1.1% | -1.0% | -1.5% | -1.4% | -1.2%
RGB, mixed content, 1080p | -2.3% | -2.4% | -2.2% | -2.2% | -2.4% | -2.2% | -2.0% | -2.4% | -2.1%
RGB, Animation, 720p | 0.1% | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1%
YUV, text & graphics with motion, 1080p | -11.3% | -12.8% | -11.9% | -7.0% | -9.1% | -8.7% | -3.7% | -5.9% | -5.7%
YUV, text & graphics with motion,720p | -5.3% | -7.4% | -9.5% | -5.2% | -7.3% | -9.1% | -3.3% | -5.2% | -6.7%
YUV, mixed content, 1440p | -0.9% | -2.5% | -2.3% | -1.1% | -3.6% | -3.1% | -1.1% | -4.0% | -3.4%
YUV, mixed content, 1080p | -2.4% | -3.5% | -3.3% | -2.4% | -5.0% | -4.6% | -1.5% | -4.5% | -2.9%
YUV, Animation, 720p | 0.1% | 0.0% | 0.0% | 0.0% | -0.2% | 0.1% | 0.1% | -0.1% | -0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | -0.1%
Enc Time[%] | 99% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 134% |  |  | 106% |  |  | 106% |  | 
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
IBC searches 2 left CTUs | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -14.2% | -14.4% | -14.3% | -8.5% | -9.1% | -9.1% | -5.3% | -5.9% | -5.9%
RGB, text & graphics with motion,720p | -7.9% | -7.3% | -7.6% | -7.7% | -6.9% | -7.3% | -5.8% | -5.5% | -5.8%
RGB, mixed content, 1440p | -1.5% | -1.4% | -1.3% | -1.8% | -1.5% | -1.5% | -1.8% | -1.5% | -1.4%
RGB, mixed content, 1080p | -3.1% | -3.4% | -2.9% | -2.9% | -3.3% | -2.7% | -2.7% | -3.3% | -2.6%
RGB, Animation, 720p | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -13.4% | -15.5% | -14.7% | -8.6% | -11.2% | -10.7% | -4.5% | -7.2% | -6.8%
YUV, text & graphics with motion,720p | -5.7% | -8.2% | -10.2% | -5.8% | -8.3% | -10.3% | -4.1% | -6.2% | -8.1%
YUV, mixed content, 1440p | -1.1% | -3.3% | -3.0% | -1.3% | -4.3% | -4.0% | -1.5% | -4.7% | -4.0%
YUV, mixed content, 1080p | -2.7% | -5.1% | -4.8% | -2.8% | -6.5% | -6.2% | -2.0% | -5.2% | -4.9%
YUV, Animation, 720p | 0.1% | -0.1% | 0.0% | 0.1% | -0.1% | 0.1% | 0.0% | -0.3% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0%
Enc Time[%] | 102% |  |  | 101% |  |  | 100% |  | 
Dec Time[%] | 135% |  |  | 108% |  |  | 109% |  | 

## Slide 11: Anchor = SCCE3, Lossless
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
IBC searched 2 left CTUS | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 1.0% | 0.9% | 0.3% | 2.0% | 0.2% | 0.6% | 0.2% | 1.5% | 0.2% | 0.5% | 0.2% | 1.0%
RGB, text & graphics with motion,720p | 0.6% | 0.7% | 0.0% | 1.6% | 0.1% | 0.4% | 0.0% | 1.3% | 0.1% | 0.2% | 0.0% | 0.6%
RGB, mixed content, 1440p | 0.2% | 0.1% | 0.1% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 1.1% | 1.1% | 0.3% | 2.3% | 0.3% | 0.7% | 0.2% | 1.6% | 0.2% | 0.5% | 0.2% | 0.9%
YUV, text & graphics with motion,720p | 0.7% | 0.8% | 0.0% | 1.7% | 0.1% | 0.5% | 0.0% | 1.4% | 0.1% | 0.3% | 0.0% | 0.8%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 96% |  |  |  | 98% |  |  |  | 99% |  |  | 
Dec Time[%] | 108% |  |  |  | 102% |  |  |  | 103% |  |  | 
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
IBC searched full frame | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.7% | 0.7% | 0.2% | 1.6% | 0.2% | 0.4% | 0.1% | 1.0% | 0.1% | 0.3% | 0.1% | 0.6%
RGB, text & graphics with motion,720p | 0.5% | 0.6% | 0.0% | 1.2% | 0.1% | 0.3% | 0.0% | 0.8% | 0.0% | 0.2% | 0.0% | 0.4%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.8% | 0.8% | 0.2% | 1.8% | 0.2% | 0.5% | 0.1% | 1.1% | 0.1% | 0.3% | 0.1% | 0.7%
YUV, text & graphics with motion,720p | 0.6% | 0.7% | 0.0% | 1.4% | 0.1% | 0.4% | 0.0% | 1.0% | 0.0% | 0.2% | 0.0% | 0.6%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 97% |  |  |  | 99% |  |  |  | 100% |  |  | 
Dec Time[%] | 109% |  |  |  | 103% |  |  |  | 102% |  |  | 

## Slide 12: Anchor = SCM 1.0, Lossless
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
IBC searched 2 left CTUS | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 13.8% | 13.1% | 4.6% | 23.9% | 3.1% | 7.5% | 2.3% | 17.7% | 2.4% | 5.0% | 1.3% | 11.3%
RGB, text & graphics with motion,720p | 9.9% | 9.7% | 0.2% | 20.3% | 1.4% | 5.5% | 0.1% | 13.9% | 0.8% | 3.4% | 0.1% | 8.0%
RGB, mixed content, 1440p | 1.6% | 1.5% | 1.0% | 1.9% | 0.2% | 0.2% | 0.1% | 0.4% | 0.0% | 0.0% | 0.0% | 0.1%
RGB, mixed content, 1080p | 1.1% | 1.1% | 1.1% | 1.1% | 0.2% | 0.2% | 0.2% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 17.6% | 16.1% | 3.7% | 31.3% | 3.1% | 9.7% | 2.2% | 23.7% | 2.1% | 6.5% | 1.9% | 15.8%
YUV, text & graphics with motion,720p | 9.0% | 10.3% | 0.2% | 23.5% | 1.3% | 6.7% | 0.1% | 20.0% | 0.7% | 4.0% | 0.0% | 11.4%
YUV, mixed content, 1440p | 0.6% | 0.7% | 0.3% | 1.2% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.6% | 0.6% | 0.6% | 0.6% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 107% |  |  |  | 100% |  |  |  | 99% |  |  | 
Dec Time[%] | 123% |  |  |  | 106% |  |  |  | 107% |  |  | 
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
IBC searched full frame | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 8.3% | 8.5% | 3.5% | 13.5% | 2.2% | 4.4% | 1.8% | 9.4% | 1.8% | 2.9% | 1.0% | 5.9%
RGB, text & graphics with motion,720p | 8.7% | 6.8% | 0.2% | 19.4% | 1.2% | 3.3% | 0.1% | 7.5% | 0.7% | 2.3% | 0.1% | 5.1%
RGB, mixed content, 1440p | 0.5% | 0.5% | 0.4% | 0.6% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.5% | 0.5% | 0.5% | 0.5% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 10.2% | 10.2% | 2.7% | 17.8% | 2.0% | 5.5% | 1.5% | 12.6% | 1.5% | 3.6% | 1.3% | 8.2%
YUV, text & graphics with motion,720p | 7.3% | 6.6% | 0.1% | 15.8% | 1.0% | 3.7% | 0.0% | 8.4% | 0.6% | 2.5% | 0.0% | 6.0%
YUV, mixed content, 1440p | 0.3% | 0.3% | 0.1% | 0.6% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.3% | 0.3% | 0.3% | 0.3% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 106% |  |  |  | 99% |  |  |  | 98% |  |  | 
Dec Time[%] | 124% |  |  |  | 104% |  |  |  | 104% |  |  | 

## Slide 13: Contents
Introduction
Proposed Algorithms
Experimental Results
Conclusion

## Slide 14: Conclusion
Predicting major color table by the nearest one
Coding gain
  Anchor is SCCE3, IBC searches full frame, All Intra
    RGB, text & graphics with motion, 1080p, -0.8%
    YUV, text & graphics with motion, 1080p, -0.8%
  Anchor is SCCE3, IBC searches 2 left CTUs , All Intra
    RGB, text & graphics with motion, 1080p, -1.2%
    YUV, text & graphics with motion, 1080p, -1.1%
Recommending for further studying

## Slide 15: Acknowledgement
We thank Sharp for crosscheck on our proposal

## Slide 16: Thank you for your attention!
Any questions?