## Slide 1
Jill Boyce, Ye-Kui Wang, Miska Hannuksela
JCTVC-R0352: Proposed Profile, Tier, Level Conformance

## Slide 2: Introduction
Modifications are proposed to Scalable Main and Scalable Main 10 profiles and to the generic level limits and profile-specific level limits
A multi-layer bitstream partition decoding (MBPD) capability is proposed

## Slide 3: Design Goals
Enable reuse of single layer decoders for multilayer profiles
  Simple repurposing to decode a single layer
  Flexible repurposing to decode multiple layers which do not exceed single layer resource requirements
Avoid overprovisioning of decoder resources
Describe conformance in an understandable way

## Slide 4: Background
Current definition of Scalable Main profile in JCTVC-Q1008
  Allows a chain of dependent layers with up to 8 layers
  Has no explicit limit on the total number of layers
    Inherent limit in the number of layers which can be signaled is 63
  Profile, tier, level (PTL) conformance is signaled for an output layer set (OLS)
  In Valencia, it was recognized that the conformance language in the design was inadequate and identified as an area for encouraged further study
    AHG10 held 9 phone conferences to study
AVC’s SVC profiles constrained 3 layers in a chain of dependent layers

## Slide 5: Proposal
Scalable Main and Scalable Main 10 profiles
  Bitstream conformance point (profile, tier, level - PTL) constraints required to be signaled per layer in an OLS
    Additional PTL bitstream constraints may be signaled for partitions in one or more partitionings
    Decoder conformance based upon per layer PTL signaling
Motivations
  Enables simple re-purposing of single layer cores
    Each core only required to decode a single layer
  Simple definition of conformance
  Avoids overprovisioning that could be needed with conformance points defined for OLS (combined layers)
  Allows any number of layers, selectable by decoder

## Slide 6: Scalable Main profile examples
2 layer spatial scalable, 3840x2160p60 and 1920x1080p60
  Layer 0: Level 4.1
  Layer 1: Level 5.1
2 layer SNR scalable, both 1920x1080p60
  Layer 0: Level 4.1
  Layer 1: Level 4.1
3 layer SNR scalable, all 1920x1080p60
  Layer 0: Level 4.1
  Layer 1: Level 4.1
  Layer 2: Level 4.1

## Slide 7: Partitionings Description
Each OLS has one or more partitioning schemes
For each partitioning scheme
  The OLS is split into one or more partitions
  Each partition contains one or more layers
  For each partitioning, each layer in the OLS is allocated to a partition
The 0-th partitioning scheme allocates one layer per partition, and is inferred rather than directly signaled

## Slide 8: Partitionings Example
Example, 4 layer bitstream (L0, L1, L2, L3), with 3 partitioning schemes defined
  Partioning scheme 0 has 4 partitions (Default)
    P0 contains L0
    P1 contains L1
    P2 contains L2
    P3 contains L3
  Partitioning scheme 1 has 2 partitions
    P0 contains L0, L1
    P2 contains L2, L3
  Partitioning scheme 2 has 1 partition
    P0 contains L0, L1, L2, L3

## Slide 9: Multi-layer bitstream partitioning decoding (MBPD) capability
Decoders may indicate a capability to decode multiple layers within a repurposed single-layer decoder
  Bitstream conformance point PTL constraints signalled for each partition of one or more partitionings
  Decoder conformance based upon conformance point per partition PTL signalling constraints of any conforming partitioning
Motivations
  Enables re-purposing of a single layer core to decode multiple layers when total requirements (bitrate, sample rate, pictures size) fit within a level
  Particularly beneficial with many layers
  Advantageous when each layer does not utilize full capabilities of a level

## Slide 10: Indication of MBPD capability
A new Scalable High profile could be defined which requires this decoding capability
Alternatively, a capability could be defined without a new profile
  Decoders could either support or not support the capability
  When the capability supported, decoder conformance would be defined using the multi-layer partitioning parameters
  A reserved bit in the profile_tier_level( ) syntax structure would be used to indicate that a bitstream contains multi-layer partitioning information

## Slide 11: Scalable High examples
See Figure 2 in JCTVC-R0043.