## Slide 1: JCTVC-R0356: PU level IntraBC on/off and signalling
Xiaozhong Xu, Shan Liu
MediaTek Inc.
JCTVC-R0356

## Slide 2: Outline
Results for two IBC related scenarios
  PU level IBC decision
  IBC signalling using ibc_flag vs. ref_idx

## Slide 3: CU level IBC (as in SCM1/RExt6, JCTVC-P1005)
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if( transquant_bypass_enabled_flag ) | 
cu_transquant_bypass_flag | ae(v)
if( slice_type != I ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
nCbS = ( 1 << log2CbSize ) | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( intra_block_copy_enabled_flag ) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( slice_type != I && !intra_bc_flag[ x0 ][ y0 ] ) | 
pred_mode_flag | ae(v)
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ intra_bc_flag[ x0 ][ y0 ] ¦ ¦ log2CbSize = = MinCbLog2SizeY ) | 
part_mode | ae(v)
if( CuPredMode[ x0 ][ y0 ] = = MODE_INTRA ) { | 
if( PartMode = = PART_2Nx2N && pcm_enabled_flag && !intra_bc_flag[ x0 ][ y0 ] && log2CbSize >= Log2MinIpcmCbSizeY && log2CbSize <= Log2MaxIpcmCbSizeY ) | 
pcm_flag[ x0 ][ y0 ] | ae(v)
if( pcm_flag[ x0 ][ y0 ] ) { | 
...... | 
} else if( intra_bc_flag[ x0 ][ y0 ] ) { | 
mvd_coding( x0, y0, 2) | 
if( PartMode = = PART_2NxN ) | 
mvd_coding( x0, y0 + ( nCbS / 2 ), 2) | 
else if( PartMode = = PART_Nx2N ) | 
mvd_coding( x0 + ( nCbS / 2 ), y0, 2) | 
else if( PartMode = = PART_NxN ) { | 
mvd_coding( x0 + ( nCbS / 2 ), y0, 2) | 
mvd_coding( x0, y0 + ( nCbS / 2 ), 2) | 
mvd_coding( x0 + ( nCbS / 2 ), y0 + ( nCbS / 2 ), 2) | 
} | 
} else { | 
...... | 
} | 

## Slide 4: Proposed PU level IBC
coding_unit( x0, y0, log2CbSize ) { | Descriptor
...... | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( slice_type != I ¦ ¦ intra_block_copy_enabled_flag )) | 
pred_mode_flag | ae(v)
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ log2CbSize = = MinCbLog2SizeY ) | 
part_mode | ae(v)
…… | 
} | 
prediction_unit( x0, y0, nPbW, nPbH ) { | Descriptor
if( cu_skip_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
intra_bc_flag | ae(v)
if( intra_bc_flag ) | 
mvd_coding( 0, 0, 2 ) | 
else { | 
... | 
} | 
} | 

## Slide 5: Result 1 – ibc_flag
Anchor: SCM1.0, lossy
 | PU IBC |  |  | w/ inter deblock & dct |  | 
 | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | 0.0% | -0.5% | -0.7% | -0.1% | -0.8% | -1.2%
RGB, text & graphics with motion,720p | 0.1% | -0.2% | -0.4% | -0.1% | -0.5% | -0.7%
RGB, mixed content, 1440p | 0.0% | -0.1% | -0.2% | -0.2% | -0.3% | -0.5%
RGB, mixed content, 1080p | 0.0% | -0.1% | -0.5% | -0.2% | -0.3% | -0.6%
RGB, Animation, 720p | 0.0% | -0.1% | -0.2% | 0.0% | -0.2% | -0.1%
RGB, camera captured, 1080p | 0.0% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | -0.3% | -0.5% | -0.1% | -0.5% | -0.9%
YUV, text & graphics with motion,720p | 0.0% | -0.1% | -0.2% | -0.1% | -0.2% | -0.3%
YUV, mixed content, 1440p | 0.0% | 0.2% | -0.1% | -0.1% | 0.0% | -0.2%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | -0.2% | 0.0% | 0.0% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
Enc Time[%] |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  | 
Note: current encoder mode decision algorithm is not optimal. No noticeable encoding time increase.

## Slide 6: Supplemental Results
When PU level IBC decision is combined with other tools (e.g. IBC flipping)
 | PU IBC with flipping |  |  | CU IBC with PU flipping |  |  | SCCE1 Test 4.1 |  | 
 | AI | RA | LD | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -2.6% | -2.2% | -2.0% | -2.6% | -1.5% | -1.1% | -1.3% | -0.9% | -0.5%
RGB, text & graphics with motion,720p | -1.4% | -1.2% | -1.1% | -1.4% | -1.1% | -0.6% | -0.8% | -0.6% | -0.4%
RGB, mixed content, 1440p | -1.5% | -1.1% | -0.5% | -1.5% | -0.9% | -0.3% | -1.0% | -0.4% | -0.3%
RGB, mixed content, 1080p | -1.2% | -0.9% | -1.0% | -1.2% | -0.8% | -0.6% | -0.8% | -0.4% | -0.5%
RGB, Animation, 720p | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -2.4% | -1.6% | -1.3% | -2.4% | -1.1% | -0.6% | -1.2% | -0.7% | -0.5%
YUV, text & graphics with motion,720p | -1.4% | -1.0% | -0.6% | -1.4% | -0.8% | -0.2% | -0.9% | -0.6% | -0.3%
YUV, mixed content, 1440p | -1.4% | -0.6% | -0.3% | -1.4% | -0.6% | -0.2% | -1.0% | -0.4% | -0.3%
YUV, mixed content, 1080p | -1.3% | -1.0% | -0.3% | -1.3% | -0.9% | 0.1% | -0.8% | -0.5% | 0.1%
YUV, Animation, 720p | -0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | -0.1% | 0.0% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% | 97% | 96% | 100% | 97% | 96% | 102% | 99% | 98%
Dec Time[%] | 99% | 97% | 97% | 100% | 99% | 99% | 99% | 99% | 99%

## Slide 7: PU level IBC using ref_idx signalling
CU syntax same as ibc_flag signalling
PU syntax same as HEVC version 1
coding_unit( x0, y0, log2CbSize ) { | Descriptor
...... | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( slice_type != I ¦ ¦ intra_block_copy_enabled_flag )) | 
pred_mode_flag | ae(v)
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ log2CbSize = = MinCbLog2SizeY ) | 
part_mode | ae(v)
…… | 
} | 

## Slide 8: Result 2 – ref_idx
Test2.1: ref_idx IBC signalling with AMVP (spatial) BV prediction, inter deblocking and DCT
Test2.1_ibc_flag: Test2.1 using ibc_flag to replace ref_idx signalling
Test2.1_PU_off: Test2.1 with PU level IBC turned off at encoder

## Slide 9: Result 2 – ref_idx
Anchor: SCM1.0, lossy
 | Test 2.1 |  |  | Test 2.1_ibc_flag |  |  | Test 2.1_PU_off |  | 
 | AI | RA | LD | AI | RA | LD | AI | RA | LD
RGB, text & graphics with motion, 1080p | -3.9% | -2.0% | -1.6% | -4.0% | -2.4% | -2.0% | -3.9% | -1.2% | -0.6%
RGB, text & graphics with motion,720p | -2.0% | -1.5% | -0.9% | -2.0% | -1.6% | -1.0% | -2.0% | -1.3% | -0.4%
RGB, mixed content, 1440p | -1.6% | -1.2% | -0.7% | -1.6% | -1.2% | -0.8% | -1.6% | -1.0% | -0.3%
RGB, mixed content, 1080p | -1.9% | -1.3% | -0.9% | -1.9% | -1.2% | -1.1% | -1.9% | -1.1% | -0.4%
RGB, Animation, 720p | -0.1% | -0.1% | 0.1% | -0.2% | -0.3% | -0.2% | -0.1% | 0.1% | 0.2%
RGB, camera captured, 1080p | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | 0.1%
YUV, text & graphics with motion, 1080p | -4.6% | -1.8% | -1.2% | -4.6% | -2.2% | -1.5% | -4.6% | -1.2% | -0.3%
YUV, text & graphics with motion,720p | -2.4% | -1.5% | -0.5% | -2.4% | -1.6% | -0.5% | -2.4% | -1.3% | -0.1%
YUV, mixed content, 1440p | -1.8% | -0.9% | -0.3% | -1.8% | -0.9% | -0.5% | -1.8% | -0.7% | -0.2%
YUV, mixed content, 1080p | -2.1% | -1.3% | -0.5% | -2.1% | -1.4% | -0.5% | -2.1% | -1.2% | 0.0%
YUV, Animation, 720p | -0.1% | 0.1% | 0.2% | -0.1% | -0.1% | -0.1% | -0.1% | 0.2% | 0.3%
YUV, camera captured, 1080p | 0.0% | 0.1% | 0.2% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.2%
Enc Time[%] | 100% | 98% | 97% |  |  |  |  |  | 
Dec Time[%] | 98% | 97% | 99% |  |  |  |  |  | 

## Slide 10: Discussions
PU level IBC decision interacts with other IBC tools
  Only applies to 8x4 and 4x8 in current implementation
  Encoder can be improved
The penalty of using ref_idx signalling (in current implementation)
  merge_flag
  inter_pred_idc
  ref_idx_l0 (4x4, I_SLICE)
Some features may be easily enabled if using ref_idx signalling
  Merge
  Bi-prediction
  AMP …
Recommend to further study in CE