## Slide 1: JCTVC-S0050 Non-CE8: Combination of CE8 Test A and CE8 Test B for Screen Content Coding
Yao-Jen Chang, Ching-Chieh Lin, Chun-Lung Lin, Jih-Sheng Tu, and Chao-Hsiung Hung
Strasbourg, France
October 2014
Notes: <number>

## Slide 2: Background
CE8 Test A: Bi-color mode
  Select two neighboring colors to smooth the CU
CE8 Test B: Uni-color mode
  Select one neighboring color to smooth the CU
Two modes can be integrated to improve the coding gain.
  This contribution shows the combination of two CE tests.
<number>
Notes: <number>

## Slide 3: Combination
Combination: uni-color mode & bi-color mode
The most frequently occurring colors are selected from the neighboring block: N1, N2
There are two color modes:
  Uni-color mode: N1 (transmit one-bit flag “0”)
  Bi-color mode: N1, N2 (transmit one-bit flag “1”)
    A bi-index map is established to represent each pixel in the CU by a binary index.
The best mode will be selected by RDO to code the CU
<number>
Notes: <number>

## Slide 4: Parser
A CU-level flag is parsed first to enable/disable the combination mode
If the combination mode is enabled, a mode flag is further parsed to indicate which color mode is selected. Ex: 0/1 for uni-/bi- color mode
If the bi-color mode is selected, the parser of palette mode is used to parse index map, but skips the escape parsing, adaptive scan parsing, and table-related parsing (sharing, major color prediction, major colors).
<number>
Notes: <number>

## Slide 5: Results of AI-Lossy: Proposed vs. Test A, Test B
<number>
 | All Intra |  | 
 | Proposed: Test A + Test B | Bi-color: CE8 Test A | Uni-color CE8 Test B
RGB, text & graphics with motion, 1080p | -0.7% | -0.4% | -0.6%
RGB, text & graphics with motion,720p | -0.9% | -0.4% | -0.8%
RGB, mixed content, 1440p | -0.3% | -0.2% | -0.3%
RGB, mixed content, 1080p | -0.3% | -0.2% | -0.3%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.4% | -0.2% | -0.1%
YUV, text & graphics with motion,720p | -0.7% | -0.1% | -0.5%
YUV, mixed content, 1440p | -0.3% | -0.1% | -0.3%
YUV, mixed content, 1080p | -0.3% | -0.1% | -0.3%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | -0.1% | 0.0% | -0.1%
Notes: <number>

## Slide 6: Conclusion
This proposal shows effectiveness of the combined CE8 Test A and CE8 Test B:
  Compared with uni-color mode (CE8 Test B), up to 0.3% BD-rate saving is gained for Lossy condition, and no additional hardware complexity is required for parser
  Compared with bi-color mode (CE8 Test A), up to 0.6% BD-rate saving is gained for Lossy condition, and no additional hardware complexity is required for parser
<number>
Notes: <number>

## Slide 7: Recommendation
Recommend to adopt the combination of CE8 Test A and CE8 Test B for SCC.
<number>
Notes: <number>

## Slide 8: Acknowledgement
Thank MediaTek for cross check
<number>
Notes: <number>

## Slide 9: Thank you!
<number>