## Slide 1: Non-CE2: On Intra block copy JCTVC-S0112
Chao Pang, Vadim Seregin, Marta Karczewicz

## Slide 2: Current Intra block copy (Intra BC)
Above spatial neighbors outside the current CTU are considered unavailable in BV predictor derivation.
Deblocking as Intra with Bs value set equal to 2.
Use DST for 4x4 luma block.

## Slide 3: Proposed changes to Intra BC
Improved BV prediction
  Enable BV prediction with spatial neighbors outside the current CTU
  Share with the MV line buffer for AMVP or merge
Use Inter-like deblocking process
  Bs value is set equal to 1 or 0
  Treat Intra BC block as uni-predicted Inter block with MV being BV and the reference picture being the current picture
  Reuse HEVC blocking module without changes
Use DCT for Intra BC 4x4 luma block
  The Intra BC prediction is similar to Inter prediction

## Slide 4: Encoder improvements
To align with CE2 tests, encoder is improved as follows:
Method 1
  Full RD check for 2Nx2N partition mode with BV being one of the spatial merge candidates in HEVC (merge mode is not used).
  For all the CU sizes, including 64x64 and 32x32.
Method 2
  Enable RD check for 2NxN and Nx2N partition modes for 16x16 CU.

## Slide 5: Results
Improved BV prediction
Improved BV prediction with encoder method 1 (20% complexity increase for AI)

## Slide 6: Results
Inter-like deblocking
DCT for Intra BC4x4 luma block

## Slide 7: Results
Proposed changes without encoder changes
Proposed changes with encoder method 1 & 2 (20% complexity increase for AI)

## Slide 8: Conclusions
Proposed changes to Intra BC
Improved BV prediction
Use Inter-like deblocking process
Use DCT for Intra BC 4x4 luma block
Recommend for adoption in SCM 2.0

## Slide 9: Non-CE2: On Intra block copy JCTVC-S0112
Chao Pang, Vadim Seregin, Marta Karczewicz