## Slide 1: JCTVC-S0121: CE2 Test 2 Intra BC Signalled at PU level
Xiaozhong Xu, Shan Liu
and Shawmin Lei
MediaTek Inc.
JCTVC-S0121

## Slide 2: Outline
Intra BC is signalled at PU level
  Intra_bc_flag is moved from coding_unit() syntax to prediction_unit() syntax
Results for two Intra BC scenarios
  Intra BC coded as an INTRA mode
  Intra BC coded as an INTER mode

## Slide 3: CU Syntax Changes
coding_unit( x0, y0, log2CbSize ) { | Descriptor
if( transquant_bypass_enabled_flag ) | 
cu_transquant_bypass_flag | ae(v)
if( slice_type != I ) | 
cu_skip_flag[ x0 ][ y0 ] | ae(v)
nCbS = ( 1 << log2CbSize ) | 
if( cu_skip_flag[ x0 ][ y0 ] ) | 
prediction_unit( x0, y0, nCbS, nCbS ) | 
else { | 
if( intra_block_copy_enabled_flag ) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( slice_type != I && !intra_bc_flag[ x0 ][ y0 ] ¦ ¦ intra_block_copy_enabled_flag ) | 
pred_mode_flag | ae(v)
if( palette_enabled_flag && ChromaArrayType = = 3 && CuPredMode[ x0 ][ y0 ] = = MODE_INTRA && !intra_bc_flag[ x0 ][ y0 ]) | 
palette_mode_flag[ x0 ][ y0 ] | ae(v)
if( palette_mode_flag[ x0 ][ y0 ] ) | 
palette_coding( x0, y0, nCbS ) | 
else { | 
if( CuPredMode[ x0 ][ y0 ] != MODE_INTRA ¦ ¦ intra_bc_flag[ x0 ][ y0 ] ¦ ¦ log2CbSize = = MinCbLog2SizeY ) | 
part_mode | ae(v)
if( CuPredMode[ x0 ][ y0 ] = = MODE_INTRA && !intra_bc_flag[ x0 ][ y0 ]) { | 
if( PartMode = = PART_2Nx2N && pcm_enabled_flag && log2CbSize >= Log2MinIpcmCbSizeY && log2CbSize <= Log2MaxIpcmCbSizeY ) | 
… | 

## Slide 4: PU Syntax Changes
prediction_unit( x0, y0, nPbW, nPbH ) { | Descriptor
if( cu_skip_flag[ x0 ][ y0 ] ) { | 
if( MaxNumMergeCand > 1 ) | 
merge_idx[ x0 ][ y0 ] | ae(v)
} else {if( intra_bc_flag[ x0 ][ y0 ] ) /* Intra BC*/ | 
if( intra_block_copy_enabled_flag && slice_type != I && ( PartMode < PART_NxN ¦ ¦ MinCbLog2SizeY > 3 && PartMode = = PART_NxN ))) | 
intra_bc_flag[ x0 ][ y0 ] | ae(v)
if( intra_bc_flag[ x0 ][ y0 ] ) { /* Intra BC*/ | 
bvd_coding( x0, y0, 2 ) | 
bvp_flag[ x0 ][ y0 ] | ae(v)
} else { /* MODE_INTER */ | 
merge_flag[ x0 ][ y0 ] | ae(v)
…… | 

## Slide 5: Results
Anchor: SCM2.0, lossy
 | Intra BC as INTRA mode |  |  | Intra BC as INTER mode |  | 
 | AI | RA | LB | AI | RA | LB
RGB, text & graphics with motion, 1080p | 0.0% | -1.4% | -1.7% | -0.1% | -1.7% | -2.0%
RGB, text & graphics with motion,720p | 0.0% | -0.3% | -0.6% | -0.2% | -0.7% | -0.8%
RGB, mixed content, 1440p | 0.0% | -0.3% | -0.3% | -0.1% | -0.6% | -0.5%
RGB, mixed content, 1080p | 0.0% | -0.3% | -0.6% | -0.1% | -0.6% | -1.0%
RGB, Animation, 720p | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | -1.3% | -1.6% | -0.2% | -1.6% | -1.8%
YUV, text & graphics with motion,720p | 0.1% | -0.2% | -0.7% | 0.0% | -0.4% | -0.7%
YUV, mixed content, 1440p | 0.0% | -0.3% | -0.4% | 0.0% | -0.3% | -0.5%
YUV, mixed content, 1080p | 0.0% | -0.2% | -0.6% | -0.1% | -0.4% | -0.8%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 94% | 101% | 97% | 95% | 102% | 98%
Dec Time[%] | 92% | 99% | 96% | 94% | 98% | 95%

## Slide 6: Conclusion
IntraBC signalled at PU level allows a PU to be selected from IntraBC or Inter mode
0.1%/1.7%/2.0% BD rate reduction for RGB TGM 1080p class; 0.2%/1.6%/1.8% BD rate reduction for YUV TGM 1080p class (Inter mode)
Recommend for adoption into next SCM
Thanks Intel & Qualcomm for cross-checking!