## Slide 1: JCTVC-S0134 Non-CE6: Simplified palette size coding

## Slide 2: Background
This proposal is a continuation of our proposal JCTVC-R0161 in last meeting, in which we proposed to use FLC binarization to replace the TR code to signal Palette_num_signalled_entries
Recommendation in previous BOG report JVCVC-R0346 is: Re-test on proposed common platform to verify that there is no loss, then consider for addition to proposed common platform.
However, at that time impact on coding performance could not be properly evaluated before the meeting due to the bug in common software. It showed loss in the new common platform.
This new proposal fixes the coding performance issue, reduces worst case number of coded bins without coding loss.

## Slide 3: Proposed Method
Palette_num_signalled_entries
  Is currently binarized by TR code with riceparameter equal to 0 (same as TU binarization)
Proposes a concatenated binarization based on TR code and fixed length code.
  When the palette_num_signalled_entries is less than 16 there is no change to the binarization
The benefit of the proposed method is that it reduces the worst case coded bins from 31 to 20 bins (35.5% reduction)
It has no coding loss for both lossy and lossless coding conditions

## Slide 4: Proposed Binarization for palette size coding
Concatenated binarization between TU and FLC
Threshold = 16
Length of FLC =4
Maximum palette size =31
Input | Truncated Unary | Fixed Length
0 | 1 | 
1 | 10 | 
2 | 110 | 
3 | 1110 | 
… | 111 … 0 | 
15 | 1111111111111110 | 
16 | 1111111111111111 | 0000
17 | 1111111111111111 | 0001
18 | 1111111111111111 | 0010
19 | 1111111111111111 | 0011
20 | 1111111111111111 | 0100
21 | 1111111111111111 | 0101
… | 1111111111111111 | …
31 | 1111111111111111 | 1111

## Slide 5: Results (lossy)
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & grap. with mot,1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, text & grap. with mot,720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & grap. with mot, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & grap. with mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 6: Results (Lossless)
 | All Intra |  |  |  |  | Random Access |  |  |  | Low delay B |  |  | 
 | Bit-rate Savings |  |  |  |  | Bit-rate Savings |  |  |  | Bit-rate Savings |  |  | 
 | Total | Ave. |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Min | Max |  | Total | Ave. | Min | Max | Total | Ave. | Min | Max
RGB, T & G. with mot.,1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, T & G. w/mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera cap., 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV T & G. w/mot., 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, T & G. w/mot.,720p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 7: Conclusion
Proposed a simple change to the binarization of Palette_num_signalled_entries
Reduces the worst case coded bins from 31 to 20 bins (35.5% reduction)
It has no coding loss for both lossy and lossless coding conditions
Propose to adopt this into the SCM draft text and software.