## Slide 1: JCTVC-S0138 Non-CE6: Exponential Golomb binarization for Palette Run

## Slide 2: Improved Palette Run Coding
Current Palette_run coding | Proposed
Code significant flag (context coded) if(significant flag ==1) Code GR_1 flag (context coded) if (GR_1 flag ==1) Code GR_2 flag (context coded) if(GR_2 flag ==1) Code Remaining level (‘Run-3’) (bypass coded with TR code with riceparameter ==3) | Code significant flag (context coded) if(significant flag ==1) Code GR_1 flag (context coded) if (GR_1 flag ==1) Code GR_5 flag (context coded) if(GR_5 flag ==0) Code Fixed Length Code (‘Run-2’) else Code Remaining level (‘Run-6’) (bypass coded with 3rd order of Exp-Golomb binarization)
- Current Palette run coding can be improved by simply changing the binarization
Notes: 2

## Slide 3: Results (lossy)
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & grap. with mot,1080p | -0.3% | -0.3% | -0.3% | -0.2% | -0.2% | -0.2% | -0.2% | -0.3% | -0.2%
RGB, text & grap. with mot,720p | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | -0.2% | -0.3% | -0.3% | -0.2%
RGB, mixed content, 1440p | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1% | 0.1% | -0.1% | -0.1%
RGB, mixed content, 1080p | -0.1% | -0.1% | -0.1% | 0.0% | -0.2% | -0.1% | -0.2% | 0.2% | 0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | -0.1%
YUV, text & grap. with mot, 1080p | -0.4% | -0.3% | -0.3% | -0.1% | -0.2% | -0.2% | -0.2% | -0.3% | -0.2%
YUV, text & grap. with mot.,720p | -0.1% | -0.2% | -0.3% | -0.1% | -0.1% | -0.1% | -0.2% | -0.1% | -0.7%
YUV, mixed content, 1440p | -0.1% | -0.1% | -0.2% | 0.0% | 0.0% | 0.0% | -0.1% | -0.2% | 0.0%
YUV, mixed content, 1080p | -0.1% | -0.2% | -0.2% | 0.0% | -0.2% | -0.2% | -0.1% | -0.7% | -0.8%
YUV, Animation, 720p | 0.0% | 0.0% | -0.1% | 0.1% | -0.2% | -0.2% | 0.0% | -0.2% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.2% | 0.0%
Notes: 3

## Slide 4: Results (Lossless)
 | All Intra |  |  |  |  | Random Access |  |  |  | Low delay B |  |  | 
 | Bit-rate Savings |  |  |  |  | Bit-rate Savings |  |  |  | Bit-rate Savings |  |  | 
 | Total | Ave. |  |  |  |  |  |  |  |  |  |  | 
 |  |  | Min | Max |  | Total | Ave. | Min | Max | Total | Ave. | Min | Max
RGB, T & G. with mot.,1080p | 0.1% | 0.1% | 0.0% | 0.2% |  | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.2%
RGB, T & G. w/mot.,720p | 0.0% | 0.0% | 0.0% | 0.1% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera cap., 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV T & G. w/mot., 1080p | 0.1% | 0.1% | 0.0% | 0.2% |  | 0.0% | 0.1% | 0.0% | 0.2% | 0.0% | 0.1% | 0.0% | 0.2%
YUV, T & G. w/mot.,720p | 0.0% | 0.0% | 0.0% | 0.1% |  | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% |  | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 5: Conclusion
The proposed concatenated binarization is based on fixed length code and exponential golomb code.
The proposed approach provides bit rate reductions of 0.3 %, 0.4% for All Intra 1080p text and graphics RGB and YUV categories.