## Slide 1: JCTVC-S0139 Using flat scaling lists for escape coded palette pixels

## Slide 2: Palette coding and scaling lists
When using ESCAPE mode in palette coding the existing HEVC dequantizer is used
Proposal
  Reuse the dequantization process as defined in section 8.6.3
  When palette coding mode is used then scaling lists is set to a flat scaling factor array

## Slide 3: Experimental Results
Original
(a) Flat Scaling List (Proposed)
(b) Default Scaling List Enabled
A 16x16 template was repeated to generate a frame and was processed using:
Flat scaling list
Default scaling list enabled

## Slide 4: Experimental Results
(a) Flat Scaling List (Proposed)
(b) Default Scaling List Enabled
Artifacts caused from using non-flat scaling list

## Slide 5: Conclusion
The proposed change would:
  Remove repetition of the dequantization process within the draft
  Prevent artifacts that may arise due to use of non-flat scaling list
It is recommended to adopt the proposed change in HEVC screen content coding draft