## Slide 1: JCTVC-S0140 On transform coefficient scaling for adaptive colour transform

## Slide 2: Introduction
Last meeting adaptive color transform (JCTVC-R0147) was adopted in the HEVC-screen content coding (SCC) design
In the HEVC-SCC draft, the scaling associated with adaptive color transform (ACT) is carried out by the transform coefficient scaling process
However, the ACT related modifications result in negative qP values. This makes the output of the transform coefficient scaling process undefined

## Slide 3: Negative qP values in adaptive colour transform
For Qp’Y<5 or Qp’Cb<5 or Qp’Cr<3, bug fix required to handle negative qP values
No problem for lossless because dequantization is bypassed in lossless coding
8.6.2 Scaling and transformation process
…
– If cIdx is equal to 0,
qP = Qp′Y + (cu_residual_csc_flag [ xTbY ][ yTbY ] ? -5 : 0) (8‑267)
– Otherwise, if cIdx is equal to 1,
qP = Qp′Cb + (cu_residual_csc_flag [ xTbY ][ yTbY ] ? -5 : 0) (8‑268)
– Otherwise (cIdx is equal to 2),
qP = Qp′C + (cu_residual_csc_flag [ xTbY ][ yTbY ] ? -3 : 0) (8‑269)
…
8.6.3 Scaling process for transform coefficients
…
d[ x ][ y ] = Clip3( coeffMin, coeffMax, ( ( TransCoeffLevel[ xTbY ][ yTbY ][ cIdx ][ x ][ y ] * m[ x ][ y ] * levelScale[ qP%6 ] << (qP / 6 ) ) + ( 1 << ( bdShift − 1 ) ) ) >> bdShift ) (8-279)

## Slide 4: Inverse colour transform bug fix - Proposed
Proposed Methods
  Option (a): Disable inverse color transform for (Qp’Y<5 or Qp’Cb<5 or Qp’Cr<3)
  Option (b): Clip qP so it is always non-negative
coding_unit( x0, y0, log2CbSize ) { | Descriptor
… | 
if( rqt_root_cbf ) { | 
if(!( Qp′Y < 5 ¦¦ Qp′Cb < 5 ¦¦ Qp′Cr < 3) && residual_adaptive_colour_transform_enabled_flag && ( CuPredMode[ x0 ][ y0 ] = = MODE_INTER ¦ ¦ intra_bc_flag[ x0 ][ y0 ] ¦ ¦ intra_chroma_pred_mode[ x0 ][ y0 ] = = 4 ) ) | 
cu_residual_act_flag | 
… | 
} | 
… | 
} | 
– If cIdx is equal to 0,
qP = Max(0,Qp′Y + (cu_residual_act_flag[ xTbY ][ yTbY ] ? −5 : 0)) (8‑261)
– Otherwise, if cIdx is equal to 1,
qP = Max(0,Qp′Cb + (cu_residual_act_flag[ xTbY ][ yTbY ] ? −5 : 0)) (8‑262)
– Otherwise (cIdx is equal to 2),
qP = Max(0,Qp′Cr + (cu_residual_act_flag[ xTbY ][ yTbY ] ? −3 : 0)) (8‑263)

## Slide 5: Results
 | SCM 2.0 |  | Option (a) |  | Option (b) | 
Quantization parameter | Bitrates | PSNR (G) | Bitrates | PSNR (G) | Bitrates | PSNR (G)
1 | 204865.4700 | 33.6777 | 228095.8500 | 84.9411 | 284879.5200 | 78.8354
2 | 377669.5800 | 39.7507 | 218379.3000 | 80.4757 | 257264.1600 | 77.0936
3 | 326218.4100 | 63.2395 | 202108.1400 | 77.1090 | 225076.8900 | 75.0776
4 | 208964.7000 | 69.4524 | 178521.4200 | 71.6991 | 189562.9800 | 70.6202
Thank you Interdigital for cross-check
Bitrates and PSNR comparison “FlyingGraphics_RGB” in all-intra, 16 frames:
(a) Disable inverse color transform for (Qp’Y<5 or Qp’Cb<5 or Qp’Cr<3)
(b) Clip qP so it is always non-negative