## Slide 1: [JCTVC-S0149] Fast intra coding mode decision for screen contents coding
Yong-Jo Ahn, Xiangjian Wu, Woong Lim, Jonghyun Ma, and Donggyu Sim
Kwangwoon University (KWU)

## Slide 2: Introduction
Intra block copy (IBC) was adopted as a new intra coding mode for HEVC RExt
  It leads to large bitrate saving for screen contents
A fast IBC encoding methods have been proposed in JCTVC-N0256 and JCTVC-O0245
  Disable IBC search for 32x32 and 64x64 CUs
  1-D search for 16x16 CUs and 2-D search enabled only for 8x8 CUs
  Early skipping decision methods of IBC search using intra mode cost and CU activities for 8x8 CUs
In this contribution, early termination of intra coding mode decision is proposed to reduce an encoding complexity of the screen contents coding (SCC) extensions

## Slide 3: Mode decision process of SCM 2.0
In order to decide best mode, SCM 2.0 encoder computes the RD-cost of all the possible modes
SKIP mode
Inter 2Nx2N mode
Inter NxN mode
Inter Nx2N mode
Inter 2NxN mode
Inter AMP mode
Intra 2Nx2N mode
Intra NxN mode
Intra PCM mode
IBC 2Nx2N mode
IBC Nx2N mode
IBC 2NxN mode
IBC NxN mode
PLT mode
xCompressCU
xCompressCU
xCompressCU
xCompressCU

## Slide 4: The proposed method
Several coding information are widely used for fast encoding
  Coded block flag (CBF) of luma and chroma
  Motion vector
  RD-cost
In SCM encoder, coding information of intra prediction modes aren’t enough to terminate additional intra coding modes
  Coded block flag (CBF) of luma and chroma
  Motion vector
  RD-cost
In this contribution, changing of decision order of intra coding mode to use more coding information of coded mode
  IBC 2Nx2N mode is checked before checking the intra 2Nx2N mode

## Slide 5: The proposed method
After encoding the IBC 2Nx2N mode, the proposed method checks the condition of early termination
  Block vector difference
  CBF of luma and chroma
If BVD and CBF of the IBC 2Nx2N mode are respectively equal to (0, 0) and zero (Table I)
  The encoding process of the next intra coding modes (e.g., intra 2Nx2N, intra NxN, IBC 2NxN, IBC Nx2N, IBC NxN, and Intra PCM) is terminated
BVD == (0, 0) CBF of luma and chroma == 0
Table I. The condition of early termination for intra coding modes

## Slide 6: Mode decision process of the proposed method
SKIP mode
Inter 2Nx2N mode
Inter NxN mode
Inter Nx2N mode
Inter 2NxN mode
Inter AMP mode
Intra 2Nx2N mode
Intra PCM mode
IBC NxN mode
Intra NxN mode
IBC 2NxN mode
IBC Nx2N mode
PLT mode
xCompressCU
xCompressCU
xCompressCU
xCompressCU
Early termination conditions?
IBC 2Nx2N mode
No
Yes

## Slide 7: Performance evaluation
10% encoding time reduction with 0.28% BD-BR gain in All Intra (AI) case
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -2.3% | -2.1% | -2.1%
RGB, text & graphics with motion,720p | -0.3% | -0.4% | -0.4%
RGB, mixed content, 1440p | -0.3% | -0.2% | -0.3%
RGB, mixed content, 1080p | -0.4% | -0.4% | -0.4%
RGB, Animation, 720p | 0.1% | 0.1% | 0.1%
RGB, camera captured, 1080p | 0.1% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | 0.0%
YUV, text & graphics with motion,720p | 0.3% | 0.1% | 0.0%
YUV, mixed content, 1440p | 0.1% | -0.1% | -0.2%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.3% | 0.1% | 0.0%
YUV, camera captured, 1080p | 0.2% | 0.0% | 0.1%
Enc Time[%] | 90% |  | 
Dec Time[%] | 97% |  | 

## Slide 8: Performance evaluation
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.6% | -0.5% | -0.6%
RGB, text & graphics with motion,720p | -0.2% | -0.3% | -0.2%
RGB, mixed content, 1440p | -0.2% | -0.1% | -0.2%
RGB, mixed content, 1080p | -0.2% | -0.1% | -0.2%
RGB, Animation, 720p | 0.1% | 0.1% | 0.0%
RGB, camera captured, 1080p | 0.1% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p | 0.0% | -0.4% | 0.0%
YUV, text & graphics with motion,720p | 0.1% | -0.1% | 0.0%
YUV, mixed content, 1440p | 0.1% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.2% | -0.2% | 0.0%
YUV, Animation, 720p | 0.2% | 0.2% | -0.1%
YUV, camera captured, 1080p | 0.1% | 0.1% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 

## Slide 9: Performance evaluation
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.3% | -0.2% | -0.2%
RGB, text & graphics with motion,720p | -0.1% | -0.2% | 0.0%
RGB, mixed content, 1440p | -0.1% | -0.3% | -0.1%
RGB, mixed content, 1080p | -0.2% | 0.5% | 0.1%
RGB, Animation, 720p | 0.0% | 0.1% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p | 0.0% | -0.1% | 0.0%
YUV, text & graphics with motion,720p | 0.0% | 0.3% | 0.1%
YUV, mixed content, 1440p | 0.1% | -0.3% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.1% | 0.1%
YUV, Animation, 720p | 0.0% | -0.1% | 0.2%
YUV, camera captured, 1080p | 0.0% | -0.1% | 0.2%
Enc Time[%] | 99% |  | 
Dec Time[%] | 100% |  | 

## Slide 10: Conclusion
This contribution proposes a fast intra coding mode decision for SCC in SCM 2.0
The proposed method has a reduction of encoding time by about 10% on average with 0.28% BD-BR gain compared to SCM 2.0 in AI case with already adopted fast encoding methods for IBC
The proposed method needs to change only 20 lines of SCM 2.0