## Slide 1: Non-CE6: Index Coding Group (ICG) for 8x8 CU of Palette Mode in HEVC SCC
JCTVC-S0152

## Slide 2: Summary
Index Coding Group
  2x8 groups for 8x8 Cus
    Flag introduced to indicate full RUN group
  Simplified palette mode
    Escape coding + reduced context
Performance and complexity (loss)
  Negligible BD-Rate loss (averaged 0.2%/0.1%/0.0% of AI/RA/LB)
    Palette mode itself provides averaged 6.7%/4.1%/5.8% BD gains for all
  Small Gains observed for Lossless mode
  Potential parallel processing at encoder (4x as shown)

## Slide 3: Motivation
Palette mode brings impressive gains for coding screen contents.
  Averaged 6.7% BD Gains for All Intra (15.3% for text/graphics 1080p)
  Instead of conventional block based processing, it is basically a pixel-level processing  throughput will be key issue especially for small CU size (such as 8x8).

## Slide 4: Index Coding Group
It suggests parallel processing index coding groups to improve the 8x8 CU processing throughput.
  Each 8x8 Index Map  4 Parallel 2x8 Index Coding Group
  COPY_ABOVE enabled across different group
  A flag indicates current group is a “full RUN” group, i.e., RUN = 2x8 = 16.

## Slide 5: Palette Simplification
Simplified Escape Coding
  The same as the JCTVC-S0150: parallel index map and Escape color processing by treating Escape index as normal color index
Contexts reduction of SPoint
  2 contexts in current design, depending on SPoint of upper line
  Reduced to 1 only without any dependency

## Slide 6: Performance Evaluation
Anchor: SCM 2.0; Negligible loss!
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.4% | 0.4% | 0.3%
RGB, text & graphics with motion,720p | 0.3% | 0.3% | 0.3%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.1%
RGB, mixed content, 1080p | 0.1% | 0.2% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.6% | 0.6% | 0.6%
YUV, text & graphics with motion,720p | 0.4% | 0.4% | 0.4%
YUV, mixed content, 1440p | 0.2% | 0.3% | 0.2%
YUV, mixed content, 1080p | 0.2% | 0.3% | 0.3%
YUV, Animation, 720p | 0.0% | 0.2% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.2% | 0.3% | 0.2%
0.2% | 0.1% | 0.1%
0.1% | 0.1% | 0.0%
0.1% | 0.1% | 0.1%
0.0% | 0.1% | 0.0%
0.0% | 0.0% | 0.0%
0.3% | 0.3% | 0.3%
0.3% | 0.2% | 0.4%
0.1% | 0.3% | 0.3%
0.2% | 0.2% | 0.2%
0.0% | 0.0% | 0.0%
0.0% | 0.1% | -0.1%
100% |  | 
100% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.1% | 0.2% | 0.2%
0.0% | -0.1% | 0.1%
-0.2% | 0.0% | -0.1%
0.0% | 0.2% | 0.3%
0.0% | 0.1% | 0.1%
0.1% | -0.1% | 0.0%
0.2% | 0.2% | 0.2%
0.0% | 0.3% | 0.0%
0.0% | 0.0% | 0.2%
0.1% | 0.6% | 0.7%
0.1% | -0.1% | -0.2%
0.0% | -0.2% | 0.1%
100% |  | 
100% |  | 
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.5% | 0.4% | -0.2% | 0.8%
RGB, text & graphics with motion,720p | 0.1% | 0.0% | -0.1% | 0.3%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.2%
RGB, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.2% | 0.2% | -0.3% | 0.5%
YUV, text & graphics with motion,720p | 0.0% | 0.0% | -0.2% | 0.1%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 97% |  |  | 
Lossy: 0.2%/0.1%/0.0%
Lossless: 0.1%/0.0%/0.0%
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.3% | 0.2% | -0.2% | 0.4%
0.0% | 0.0% | -0.1% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.2% | 0.0% | -0.3% | 0.3%
0.0% | 0.0% | -0.2% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
99% |  |  | 
95% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.3% | 0.1% | -0.2% | 0.3%
0.0% | 0.0% | -0.1% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.1% | 0.0% | -0.2% | 0.2%
0.0% | 0.0% | -0.1% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
92% |  |  | 
100% |  |  | 

## Slide 7: Impact on overall palette mode efficiency
Anchor: SCM 2.0 w/o Palette
  Camera-captured and Animation are excluded.
  Averaged over same category regardless of resolution and format
  AI and LB are presented
  Almost negligible loss from S0152 (especially for LB)!
AI | SCM 2.0 | S0152
Text/graphics | -15.3% | -14.9%
Mixed | -4.9% | -4.8%
LB | SCM 2.0 | S0152
Text/graphics | -6.2% | -6.1%
Mixed | -2.1% | -2.1%

## Slide 8: Additional Results (1) – Palette Simplification Impact
Anchor: SCM 2.0; on average, no loss for lossy! Gains for lossless
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.0%
RGB, text & graphics with motion,720p | 0.1% | 0.1% | 0.1%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | 0.1% | 0.1%
YUV, text & graphics with motion,720p | 0.2% | 0.1% | 0.1%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.1%
YUV, mixed content, 1080p | 0.1% | 0.2% | 0.2%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 101% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | -0.1% | 0.0%
-0.1% | -0.1% | 0.1%
0.0% | 0.0% | -0.1%
0.0% | -0.1% | 0.0%
0.0% | 0.0% | 0.0%
0.1% | 0.0% | 0.1%
0.1% | 0.3% | 0.3%
0.1% | 0.0% | 0.1%
0.0% | -0.1% | -0.1%
0.0% | 0.1% | -0.2%
100% |  | 
102% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-0.1% | 0.0% | 0.0%
0.0% | -0.1% | 0.1%
0.1% | -0.1% | -0.2%
0.1% | 0.5% | 0.5%
-0.1% | 0.0% | 0.2%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.2% | -0.2%
-0.1% | -0.2% | -0.3%
-0.3% | -0.1% | 0.2%
0.0% | -0.4% | 0.0%
0.0% | 0.0% | -0.1%
100% |  | 
104% |  | 
Lossy: 0.0%/0.0%/0.0%
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.7% | 0.7% | 0.2% | 0.9%
RGB, text & graphics with motion,720p | 0.2% | 0.1% | 0.0% | 0.4%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.2%
RGB, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.5% | 0.5% | 0.1% | 0.9%
YUV, text & graphics with motion,720p | 0.1% | 0.1% | 0.0% | 0.2%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.2%
YUV, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 100% |  |  | 
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.5% | 0.3% | 0.1% | 0.5%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.3% | 0.2% | 0.0% | 0.5%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
100% |  |  | 
102% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.4% | 0.3% | 0.0% | 0.4%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.2% | 0.2% | 0.0% | 0.4%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
100% |  |  | 
102% |  |  | 
Lossless:
0.2%/0.1%/0.1%

## Slide 9: Additional Results (2) – Impact of removing “full-RUN” flag
Anchor: SCM 2.0; Small BD-loss for lossy! No loss for lossless.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.8% | 0.8% | 0.7%
RGB, text & graphics with motion,720p | 0.6% | 0.6% | 0.6%
RGB, mixed content, 1440p | 0.2% | 0.4% | 0.3%
RGB, mixed content, 1080p | 0.2% | 0.4% | 0.3%
RGB, Animation, 720p | 0.0% | 0.1% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 1.2% | 1.1% | 1.1%
YUV, text & graphics with motion,720p | 0.7% | 0.8% | 1.0%
YUV, mixed content, 1440p | 0.4% | 0.8% | 0.8%
YUV, mixed content, 1080p | 0.5% | 0.6% | 0.7%
YUV, Animation, 720p | 0.0% | 0.4% | 0.3%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.4% | 0.5% | 0.4%
0.4% | 0.4% | 0.4%
0.1% | 0.1% | 0.1%
0.1% | 0.3% | 0.1%
0.0% | 0.1% | 0.0%
0.0% | 0.0% | 0.0%
0.6% | 0.5% | 0.6%
0.5% | 0.3% | 0.7%
0.3% | 0.4% | 0.5%
0.4% | 0.5% | 0.5%
0.0% | 0.3% | 0.2%
0.0% | 0.2% | 0.0%
100% |  | 
100% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.3% | 0.3% | 0.3%
0.2% | 0.2% | 0.3%
0.2% | 0.1% | 0.0%
-0.1% | 0.7% | 0.3%
0.0% | 0.1% | 0.1%
0.0% | 0.0% | 0.0%
0.4% | 0.5% | 0.5%
0.3% | 0.5% | 0.6%
0.0% | 0.1% | 0.5%
0.1% | 0.9% | 0.9%
0.0% | -0.1% | 0.1%
0.0% | -0.1% | 0.1%
100% |  | 
102% |  | 
Lossy: 0.4%/0.2%/0.1%
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.2% | 0.2% | -0.6% | 0.7%
RGB, text & graphics with motion,720p | 0.0% | -0.1% | -0.4% | 0.2%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.2%
RGB, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.8% | 0.2%
YUV, text & graphics with motion,720p | -0.1% | -0.2% | -0.5% | 0.1%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.1%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 97% |  |  | 
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.2% | 0.0% | -0.5% | 0.3%
0.0% | -0.1% | -0.3% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | -0.2% | -0.6% | 0.1%
0.0% | -0.1% | -0.4% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
99% |  |  | 
95% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.2% | 0.0% | -0.5% | 0.2%
0.0% | -0.1% | -0.2% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | -0.1% | -0.5% | 0.1%
0.0% | -0.1% | -0.3% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
91% |  |  | 
100% |  |  | 
Lossless: 0.0%/0.0%/0.0%

## Slide 10: Conclusion
Index Coding Group
  Provides parallel index processing at encoder to improve the system throughput
  Palette simplification further reduces contexts for coding index mode on top of JCTVC S0150 (Escape Coding)
  Negligible performance loss
Recommendation
  Adopt it into HEVC SCC WD and SCM 3.0