## Slide 1: JCTVC-S0179 On inter-component de-correlation for screen content coding
Xiaoyu Xiu, Yan Ye, Yuwen He
InterDigital Communications, Inc.
Oct. 2014

## Slide 2
Introduction
Two inter-component de-correlation methods are supported in HEVC SCC draft 1
  The inverse CCP is performed on TU-level.
  The inverse ACT is performed on CU-level for CUs coded with inter mode, and on PU-level for CUs coded with intra and intraBC modes.
  Complicates pipeline design and parallel processing

## Slide 3
Proposal (1)
TU-level inverse ACT (editorial change to the spec.)
  Represents a more efficient decoder implementation for pipeline and parallel processing.
  Make ACT more consistent with CCP as both modules are located at TU-level.

## Slide 4
Proposal (2)
Combined inverse CCP and inverse ACT
  Combine inverse CCP and inverse ACT to one single decoding process.
  Reduce the decoding latency.
  Combined decoding process in lossy coding:
  Combined decoding process in lossless coding:

## Slide 5
Simulation
TU-level inverse ACT (editorial change to the spec.)
  No coding performance difference.
  Reduced decoding time as TU-level CBF flags could be utilized to skip unnecessary inverse ACT operations.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.0%
RGB, text & graphics with motion,720p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion,720p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 93% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
94% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
94% |  | 

## Slide 6
Simulation
TU-level inverse ACT (editorial change to the spec.)
  No coding performance difference.
  Reduced decoding time as TU-level CBF flags could be utilized to skip unnecessary inverse ACT operations.
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, text & graphics with motion,720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion,720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 
Dec Time[%] | 95% |  |  | 
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
100% |  |  | 
94% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
100% |  |  | 
97% |  |  | 

## Slide 7
Simulation
Combined inverse CCP and inverse ACT
  No coding performance loss.
  Similar encoding and decoding times to the anchor.
  Reduced decoding latency.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | 0.0% | 0.0% | -0.1%
RGB, text & graphics with motion,720p | -0.1% | -0.1% | 0.0%
RGB, mixed content, 1440p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1080p | -0.1% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.1% | -0.1% | 0.2%
YUV, text & graphics with motion, 1080p | 0.0% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1440p | 0.0% | -0.1% | -0.1%
YUV, mixed content, 1080p | 0.0% | -0.2% | -0.1%
YUV, Animation, 720p | 0.1% | -0.2% | 0.0%
YUV, camera captured, 1080p | 0.0% | -0.1% | 0.0%
Enc Time[%] | 105% |  | 
Dec Time[%] | 97% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | -0.1% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | -0.1%
0.0% | 0.0% | -0.2%
0.0% | -0.2% | 0.1%
0.0% | 0.0% | -0.1%
0.1% | -0.4% | 0.0%
0.1% | -0.1% | -0.2%
0.0% | -0.5% | -0.4%
0.1% | -0.2% | 0.0%
0.0% | -0.4% | -0.1%
104% |  | 
100% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.0% | -0.1% | 0.0%
-0.2% | -0.1% | 0.1%
-0.1% | 0.0% | -0.1%
-0.1% | 0.2% | 0.5%
-0.1% | -0.1% | -0.1%
0.0% | -0.3% | 0.0%
0.0% | -0.1% | 0.0%
-0.2% | -0.1% | -0.3%
-0.2% | -0.3% | -0.1%
0.0% | -0.3% | 0.0%
0.0% | -1.1% | -0.1%
0.0% | -0.7% | -0.2%
103% |  | 
100% |  | 

## Slide 8
Simulation
Thanks to Microsoft for the cross-check!
Combined inverse CCP and inverse ACT
  No coding performance loss.
  Similar encoding and decoding times to the anchor.
  Reduced decoding latency.
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, text & graphics with motion,720p | 0.1% | 0.0% | 0.0% | 0.1%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.1% | 0.1%
RGB, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p | 0.1% | 0.1% | 0.0% | 0.1%
YUV, text & graphics with motion,720p | 0.1% | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  | 
Dec Time[%] | 103% |  |  | 
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.1% | 0.0% | 0.0% | 0.1%
0.2% | 0.1% | 0.0% | 0.2%
0.1% | 0.1% | 0.1% | 0.1%
0.1% | 0.1% | 0.1% | 0.1%
0.1% | 0.1% | 0.1% | 0.1%
0.0% | 0.0% | 0.0% | 0.1%
0.1% | 0.1% | 0.0% | 0.1%
0.1% | 0.1% | 0.0% | 0.2%
0.2% | 0.2% | 0.0% | 0.4%
0.0% | 0.0% | 0.0% | 0.0%
0.1% | 0.1% | 0.1% | 0.1%
0.0% | 0.0% | 0.0% | 0.0%
101% |  |  | 
101% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.1% | 0.0% | 0.0% | 0.1%
0.2% | 0.1% | 0.0% | 0.3%
0.1% | 0.1% | 0.1% | 0.1%
0.2% | 0.2% | 0.2% | 0.2%
0.1% | 0.1% | 0.1% | 0.1%
0.0% | 0.0% | 0.0% | 0.1%
0.1% | 0.1% | 0.0% | 0.1%
0.2% | 0.1% | 0.0% | 0.2%
0.3% | 0.3% | 0.0% | 0.5%
0.0% | 0.0% | 0.0% | 0.0%
0.1% | 0.1% | 0.1% | 0.1%
0.0% | 0.0% | 0.0% | 0.0%
102% |  |  | 
103% |  |  | 

## Slide 9
Closing Remarks
The proposed methods
  TU-level inverse ACT (editorial change to the spec.)
  Combined inverse CCP and inverse ACT
There is no coding performance loss while pipeline design and parallel processing are simplified.
Reduced decoding latency of inverse CCP and inverse ACT.