## Slide 1
JCTVC-S0180 Adaptive color transform for different luma and chroma bit-depth
Xiaoyu Xiu, Yuwen He, Yan Ye (InterDigital)
Bin Li, Ji-zheng Xu (Microsoft)
Oct. 2014

## Slide 2
Introduction
The ACT design in SCM-2.0
  It was found that the current ACT design is not optimal when the luma and chroma components are coded with different bit-depths.
  Other encoder issues when SCM-2.0 is used for different luma and chroma bit-depths
  For hash-based inter search, luma bit-depth is used to derive the CRC value of chroma component.
  For palette-based coding, the threshold used to derive palette table and palette indices are defined by assuming luma and chroma are 8-bit.

## Slide 3
Proposal
Encoder bug fixes
  For inter hash, use the chroma bit-depth to calculate the chroma CRC values.
  For palette-based coding, use 8-bit distortion to generate the palette table and the palette indices.
The proposed solution
  For lossy coding, align the luma and chroma bit-depths by left-shift before ACT. The scaled component is converted to its original bit-depth by right-shift after ACT.
  For lossless coding, ACT is disabled.

## Slide 4
Simulation
Three methods are evaluated under the CTC with the modified bit-depths
  SCM-2.0 anchor
  SCM-2.0 + encoder bug fixes
  SCM-2.0 + encoder bug fixes + proposed bit-depth alignment solution
  Two settings
  Setting one: InterBitDepth = 10 and InterBitDepthC = 8
  Setting two: InterBitDepth = 12 and InterBItDepthC = 8
Thanks to Qualcomm for the cross-check!

## Slide 5
Results of encoder bug fixes (1)
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -2.4% | -3.8% | -3.6%
RGB, text & graphics with motion,720p | -2.7% | -4.3% | -4.3%
RGB, mixed content, 1440p | -1.8% | -2.8% | -3.0%
RGB, mixed content, 1080p | -2.2% | -4.0% | -3.8%
RGB, Animation, 720p | -0.3% | -0.9% | -1.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | -0.1%
YUV, text & graphics with motion, 1080p | -2.6% | -6.3% | -5.6%
YUV, text & graphics with motion,720p | -1.4% | -6.4% | -6.6%
YUV, mixed content, 1440p | -2.4% | -8.1% | -8.2%
YUV, mixed content, 1080p | -3.0% | -9.0% | -8.7%
YUV, Animation, 720p | 0.1% | -1.5% | -1.4%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 96% |  | 
Dec Time[%] | 97% |  | 
Random Access |  | 
G/Y | B/U | R/V
-0.9% | -2.0% | -1.9%
0.2% | -2.1% | -2.0%
0.0% | -1.0% | -1.0%
-0.6% | -2.3% | -2.1%
1.2% | -0.3% | -0.2%
0.5% | 0.2% | 0.5%
-0.8% | -3.4% | -2.8%
0.6% | -4.3% | -4.2%
-0.8% | -7.1% | -7.1%
-1.4% | -7.6% | -6.9%
0.1% | -1.2% | -1.3%
0.0% | 0.0% | 0.0%
94% |  | 
98% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-1.0% | -1.9% | -1.7%
-1.7% | -3.0% | -3.2%
0.9% | -0.9% | -1.0%
2.2% | 0.5% | -0.1%
2.8% | 0.2% | 0.0%
1.9% | 0.8% | 1.5%
-1.3% | -3.3% | -2.9%
-0.4% | -3.9% | -4.8%
-0.1% | -6.3% | -6.7%
-0.5% | -7.2% | -5.8%
0.0% | -0.4% | -0.3%
0.0% | 0.0% | 0.0%
96% |  | 
98% |  | 
  Testing configuration
  Anchor: SCM-2.0
  Tested: SCM-2.0 + encoder bug fixes
  Setting one: InterBitDepth = 10 and InterBitDepthC = 8
  Coding performance
  RGB coding: BD-rate savings 1.6%, 0.1% and 0.8% for AI, RA and LB.
  YUV coding: BD-rate savings 1.6%, 0.4% and 0.4% for AI, RA and LB.

## Slide 6
Results of encoder bug fixes (2)
  Testing configuration
  Anchor: SCM-2.0
  Tested: SCM-2.0 + encoder bug fixes
  Setting two: InterBitDepth = 12 and InterBitDepthC = 8
  Coding performance
  RGB coding: BD-rate savings 5.6%, 4.8% and 2.5% for AI, RA and LB.
  YUV coding: BD-rate savings 3.4%, 2.4% and 1.9% for AI, RA and LB.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -8.8% | -10.1% | -9.8%
RGB, text & graphics with motion,720p | -9.5% | -10.3% | -10.6%
RGB, mixed content, 1440p | -6.6% | -7.6% | -7.9%
RGB, mixed content, 1080p | -8.0% | -9.1% | -9.3%
RGB, Animation, 720p | -0.6% | -1.6% | -1.8%
RGB, camera captured, 1080p | -0.1% | -0.2% | -0.3%
YUV, text & graphics with motion, 1080p | -7.1% | -9.9% | -9.4%
YUV, text & graphics with motion,720p | -5.5% | -9.7% | -12.2%
YUV, mixed content, 1440p | -3.5% | -8.7% | -9.1%
YUV, mixed content, 1080p | -4.5% | -9.5% | -9.8%
YUV, Animation, 720p | 0.1% | -1.4% | -1.3%
YUV, camera captured, 1080p | 0.0% | 0.0% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 96% |  | 
Random Access |  | 
G/Y | B/U | R/V
-11.9% | -12.9% | -12.5%
-7.9% | -9.4% | -8.7%
-3.2% | -5.0% | -5.9%
-7.1% | -6.1% | -6.7%
1.4% | -11.3% | -7.8%
0.0% | -8.1% | -3.6%
-4.0% | -6.3% | -6.0%
-3.9% | -6.6% | -10.0%
-3.1% | -8.1% | -8.7%
-3.5% | -8.7% | -8.6%
0.1% | -1.1% | -1.0%
0.0% | 0.0% | -0.1%
102% |  | 
99% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-11.1% | -14.2% | -13.2%
-8.9% | -12.6% | -11.5%
3.9% | -1.3% | -2.7%
-3.3% | -7.0% | -8.8%
1.9% | -18.1% | -13.5%
2.3% | -15.8% | -6.7%
-3.0% | -4.9% | -4.9%
-3.1% | -6.4% | -9.1%
-2.5% | -7.8% | -8.2%
-2.7% | -7.5% | -7.1%
0.0% | -0.6% | -0.7%
0.0% | -0.1% | -0.1%
101% |  | 
98% |  | 

## Slide 7
Results of bit-depth alignment (1)
  Testing configuration
  Anchor: SCM-2.0 + encoder bug fixes
  Tested: SCM-2.0 + encoder bug fixes + bit-depth alignment
  Setting one: InterBitDepth = 10 and InterBitDepthC = 8
  Coding performance
  RGB coding: BD-rate savings 15.4%, 20.1% and 23.6% for AI, RA and LB.
  YUV coding: BD-rate savings 0.1%, 0.3% and 0.3% for AI, RA and LB.
  Fully restore the coding gain of ACT.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -5.9% | -3.4% | -3.4%
RGB, text & graphics with motion,720p | -11.4% | -6.3% | -8.3%
RGB, mixed content, 1440p | -18.3% | -11.8% | -11.2%
RGB, mixed content, 1080p | -14.6% | -7.8% | -8.4%
RGB, Animation, 720p | -23.0% | -23.1% | -20.3%
RGB, camera captured, 1080p | -19.5% | -8.1% | -12.8%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.2%
YUV, text & graphics with motion,720p | -0.4% | -0.5% | -0.5%
YUV, mixed content, 1440p | 0.1% | -0.7% | -0.7%
YUV, mixed content, 1080p | 0.0% | -0.2% | -0.3%
YUV, Animation, 720p | -0.1% | -6.3% | -3.4%
YUV, camera captured, 1080p | 0.0% | -0.1% | -0.1%
Enc Time[%] | 98% |  | 
Dec Time[%] | 109% |  | 
Random Access |  | 
G/Y | B/U | R/V
-8.4% | -5.2% | -5.4%
-14.4% | -7.2% | -10.0%
-24.5% | -15.8% | -14.6%
-17.3% | -8.5% | -8.5%
-27.3% | -24.6% | -22.9%
-28.6% | -18.1% | -24.2%
-0.1% | -0.1% | -0.2%
-1.2% | -1.0% | -2.0%
0.0% | -0.6% | -0.6%
0.1% | -0.2% | -0.3%
-0.6% | -6.8% | -3.2%
0.0% | -0.1% | -0.2%
113% |  | 
107% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-7.8% | -4.9% | -4.9%
-14.0% | -9.0% | -11.6%
-27.6% | -19.2% | -17.8%
-22.0% | -14.7% | -16.0%
-34.2% | -32.5% | -31.5%
-36.1% | -28.5% | -33.2%
-0.1% | -0.1% | -0.1%
-1.6% | -1.4% | -2.1%
0.0% | -0.5% | -0.3%
0.3% | -0.7% | -0.6%
-0.2% | -4.8% | -3.1%
0.0% | -0.1% | 0.0%
113% |  | 
105% |  | 

## Slide 8
Results of bit-depth alignment (2)
  Testing configuration
  Anchor: SCM-2.0 + encoder bug fixes
  Tested: SCM-2.0 + encoder bug fixes + bit-depth alignment
  Setting two: InterBitDepth = 12 and InterBitDepthC = 8
  Coding performance
  RGB coding: BD-rate savings 15.4%, 20.1% and 23.6% for AI, RA and LB.
  YUV coding: BD-rate savings 0.1%, 0.3% and 0.3% for AI, RA and LB.
  Fully restore the coding gain of ACT.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -16.8% | -13.4% | -13.4%
RGB, text & graphics with motion,720p | -17.9% | -13.0% | -14.8%
RGB, mixed content, 1440p | -26.5% | -20.7% | -19.9%
RGB, mixed content, 1080p | -24.9% | -18.6% | -18.8%
RGB, Animation, 720p | -25.8% | -26.6% | -24.2%
RGB, camera captured, 1080p | -20.4% | -10.1% | -14.9%
YUV, text & graphics with motion, 1080p | -0.1% | -0.1% | -0.1%
YUV, text & graphics with motion,720p | -0.4% | -0.5% | -0.5%
YUV, mixed content, 1440p | 0.0% | -0.8% | -0.8%
YUV, mixed content, 1080p | 0.0% | -0.2% | -0.4%
YUV, Animation, 720p | -0.1% | -6.4% | -3.5%
YUV, camera captured, 1080p | 0.0% | -0.1% | -0.1%
Enc Time[%] | 93% |  | 
Dec Time[%] | 110% |  | 
Random Access |  | 
G/Y | B/U | R/V
-32.0% | -25.3% | -25.7%
-31.1% | -23.6% | -25.8%
-43.1% | -36.5% | -35.4%
-38.5% | -29.4% | -30.4%
-44.1% | -40.8% | -39.9%
-51.3% | -46.2% | -50.4%
-0.2% | -0.1% | -0.2%
-1.2% | -1.2% | -2.0%
-0.1% | -1.0% | -0.8%
-0.1% | -0.5% | -0.7%
-0.5% | -6.8% | -3.4%
0.0% | -0.1% | 0.0%
108% |  | 
103% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-30.4% | -23.8% | -24.1%
-40.8% | -32.4% | -34.8%
-51.7% | -44.0% | -42.5%
-45.2% | -32.5% | -32.6%
-56.0% | -51.7% | -51.6%
-60.0% | -58.1% | -60.8%
-0.1% | -0.2% | -0.2%
-1.5% | -1.3% | -2.0%
-0.1% | -1.1% | -0.9%
0.2% | -1.3% | -1.3%
-0.4% | -5.3% | -3.1%
0.0% | 0.0% | 0.1%
110% |  | 
104% |  | 

## Slide 9
Closing Remarks
Two encoder bug fixes
  For inter hash, use the chroma bit-depth to calculate the chroma CRC values.
  For palette-based coding, use 8-bit distortion to generate the palette table and the palette indices.
The proposed solution
  The bit-depth alignment is proposed to improve the ACT performance with different luma and chroma bit-depths for lossy coding.
  Disable ACT for lossless coding.
Significant coding performance gains are observed.