## Slide 1: JCTVC-S0181 Removal of parsing dependency in palette-based coding
Xiaoyu Xiu, Yuwen He, Yan Ye
InterDigital Communications, Inc.
Oct. 2014

## Slide 2
Palette-based Coding (1)
The current palette design in SCM-2.0
  Palette indices are coded by run mode and copy-above mode.
  Palette indices are binarized using truncated binary code (TBC) that needs to know the maximum level as input.
  Parsing of indices needs to check the index of compared palette index (CPI) position.
  The palette index indicating escape colors are coded independently, i.e. not used in either run mode or copy-above mode.

## Slide 3: Palette-based Coding (2)
Parsing dependency that needs to identify escape colors
  TBC maximum level is dependent on whether the CPI position is escape color or not.
  Escape color triplets (palette_escape_val) or run-length (palette_run) is signaled depending on whether the current position is escape color or not.
Localize CPI position
  Case 1: The left neighbor uses run mode. The left neighbor is the CPI position.
  Case 2: The left neighbor uses copy-above mode. The above neighbor is the CPI position.
  The maximum level of TBC
  When CPI is escape color, the maximum TBC level is equal to the maximum palette index.
  When CPI is major color, the maximum TBC level is equal to the maximum palette index minus one.

## Slide 4
Parsing Dependency Removal
The proposed solution
  Treat the palette index indicating escape colors as a normal palette index as part of run mode and copy-above mode.
  Separate the parsing of escape color triplets from the parsing of palette indices.
    The benefits
  Removing parsing dependency: no need to check the Spoint of the left neighbor and whether the CPI position is escape or not.
  Improving coding efficiency: enable run mode and copy mode to code the palette index of escape colors.
  Unified design: unify the palette index coding of escape color and major color.

## Slide 5
Lossy Coding Performance
The average BD-rate savings of text & graphics with motion 1080p both in RGB and YCbCr formats are 0.4%, 0.2% and 0.2% for AI, RA and LB, respectively.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.4% | -0.4% | -0.4%
RGB, text & graphics with motion,720p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1440p | -0.1% | -0.1% | -0.1%
RGB, mixed content, 1080p | -0.1% | -0.1% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.5% | -0.4% | -0.4%
YUV, text & graphics with motion,720p | -0.2% | -0.3% | -0.3%
YUV, mixed content, 1440p | -0.1% | -0.1% | -0.2%
YUV, mixed content, 1080p | -0.1% | -0.1% | -0.2%
YUV, Animation, 720p | 0.0% | -0.1% | -0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 103% |  | 
Dec Time[%] | 99% |  | 
Random Access |  | 
G/Y | B/U | R/V
-0.2% | -0.2% | -0.2%
-0.2% | -0.2% | -0.2%
0.0% | 0.0% | 0.0%
-0.1% | -0.2% | -0.1%
-0.1% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
-0.2% | -0.2% | -0.2%
-0.1% | -0.3% | -0.3%
-0.1% | -0.3% | -0.2%
-0.1% | -0.5% | -0.1%
0.0% | 0.0% | -0.1%
0.0% | 0.1% | 0.0%
104% |  | 
99% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-0.2% | -0.2% | -0.1%
-0.2% | -0.3% | -0.3%
0.0% | -0.1% | -0.1%
-0.1% | 0.3% | 0.6%
-0.1% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
-0.1% | -0.3% | -0.2%
0.0% | 0.0% | -0.2%
-0.2% | -0.2% | 0.0%
-0.4% | 0.1% | -0.8%
0.0% | 0.0% | 0.1%
0.1% | 0.0% | 0.1%
103% |  | 
98% |  | 
Thanks to Qualcomm for the cross-check!

## Slide 6
Lossless Coding Performance
The average bit-rate savings of text & graphics with motion 1080p both in RGB and YCbCr formats are 0.8%, 0.4% and 0.4% for AI, RA and LB, respectively.
Thanks to Qualcomm for the cross-check!
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.5% | 0.5% | 0.4% | 0.5%
0.0% | 0.1% | 0.0% | 0.1%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.3% | 0.4% | 0.3% | 0.6%
0.0% | 0.1% | 0.0% | 0.1%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
98% |  |  | 
97% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.5% | 0.4% | 0.3% | 0.5%
0.0% | 0.0% | 0.0% | 0.1%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.3% | 0.4% | 0.2% | 0.5%
0.0% | 0.0% | 0.0% | 0.1%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
98% |  |  | 
95% |  |  | 
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.9% | 0.9% | 0.5% | 1.1%
RGB, text & graphics with motion,720p | 0.3% | 0.2% | 0.0% | 0.4%
RGB, mixed content, 1440p | 0.1% | 0.2% | 0.1% | 0.3%
RGB, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.7% | 0.7% | 0.4% | 1.2%
YUV, text & graphics with motion,720p | 0.2% | 0.2% | 0.0% | 0.4%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.1% | 0.2%
YUV, mixed content, 1080p | 0.1% | 0.1% | 0.1% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 102% |  |  | 
Dec Time[%] | 98% |  |  | 

## Slide 7
Closing Remarks
Two proposed changes to remove parsing dependencies
  Code the palette index indicating escape colors using run mode and copy-above mode
  Separately parse palette indices and escape colors
Coding performance
  Average BD-rate savings of 0.4%, 0.2% and 0.2% for AI, RA and LB in lossy coding.
  Average bit-rate savings of 0.8%, 0.4% and 0.4% for AI, RA and LB in lossless coding.