## Slide 1: Non-CE5: CU dependent color palette maximum size
JCTVC-S0201

## Slide 2: Summary
CU Dependent Palette Size
  Smaller size for smaller CU
  Improve system throughput
Performance
  On average, 0.5%/0.3%/0.1% BD-Rate loss for AI/RA/LB
  8x8/16x16 CU requires nearly 25% operations of current table processing in SCM 2.0

## Slide 3: Motivation
Palette mode brings impressive gains for coding screen contents.
  Averaged 6.7% for All Intra (15.3% for text/graphics 1080p)
  Current table size is not practical for implementation
    It requires 1984 operations even for 8x8 CU
    It is also aware that small CU is the bottle neck for overall system throughput!

## Slide 4: CU Dependent Palette Size
It suggests CU dependent palette size
CU Size | Max. Palette Size | Max. Palette Predictor Size
64x64 | 31 | 32
32x32 | 31 | 32
16x16 | 15 | 32
8x8 | 15 | 32

## Slide 5: Performance Evaluation
Anchor: SCM 2.0
Lossy: 0.5%/0.3%/0.1%
Lossless: -0.8%/-0.2%/-0.1%

## Slide 6: Performance Comparison with fixed palette size
Anchor: SCM 2.0 + MaxPaletteSize = 15 + MaxPalettePredictorSize = 32
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p | -0.4% | -0.6% | -0.5%
RGB, text & graphics with motion,720p | -0.5% | -0.7% | -0.7%
RGB, mixed content, 1440p | -0.1% | -0.1% | -0.1%
RGB, mixed content, 1080p | -0.2% | -0.1% | -0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | -0.5% | -0.9% | -0.7%
YUV, text & graphics with motion,720p | -0.3% | -0.6% | -0.8%
YUV, mixed content, 1440p | -0.1% | -0.3% | -0.2%
YUV, mixed content, 1080p | -0.3% | -0.7% | -0.5%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 97% |  | 
Random Access |  | 
G/Y | B/U | R/V
-0.2% | -0.4% | -0.3%
-0.6% | -0.7% | -0.7%
0.0% | -0.1% | -0.1%
-0.2% | -0.3% | -0.2%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | -0.1%
-0.3% | -0.5% | -0.4%
-0.4% | -0.6% | -0.9%
-0.2% | -0.5% | -0.5%
-0.2% | -1.0% | -0.7%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
100% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-0.2% | -0.3% | -0.2%
-0.4% | -0.5% | -0.5%
-0.3% | -0.1% | 0.0%
0.0% | -0.2% | 0.2%
0.0% | 0.0% | 0.1%
0.0% | 0.0% | 0.0%
-0.2% | -0.4% | -0.3%
0.0% | -0.3% | 0.0%
-0.4% | -0.6% | -0.2%
-0.5% | -0.6% | -1.2%
0.0% | 0.1% | -0.1%
0.0% | 0.0% | -0.1%
100% |  | 
100% |  | 
 | All Intra |  |  | 
 | Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, text & graphics with motion, 1080p | 0.4% | 0.5% | 0.2% | 0.9%
RGB, text & graphics with motion,720p | 0.7% | 0.6% | 0.0% | 1.9%
RGB, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.1%
RGB, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p | 0.7% | 0.8% | 0.3% | 1.1%
YUV, text & graphics with motion,720p | 0.8% | 0.7% | 0.0% | 2.0%
YUV, mixed content, 1440p | 0.1% | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  | 
Dec Time[%] | 100% |  |  | 
Random Access |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.1% | 0.3% | 0.1% | 0.7%
0.1% | 0.3% | 0.0% | 0.7%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.2% | 0.4% | 0.1% | 0.8%
0.1% | 0.3% | 0.0% | 0.8%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
100% |  |  | 
100% |  |  | 
Low Delay B |  |  | 
Bit-rate saving (Total) | Bit-rate saving (Average) | Bit-rate saving (Min) | Bit-rate saving (Max)
0.1% | 0.2% | 0.0% | 0.6%
0.1% | 0.2% | 0.0% | 0.4%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.1% | 0.3% | 0.1% | 0.6%
0.1% | 0.2% | 0.0% | 0.4%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
100% |  |  | 
99% |  |  | 

## Slide 7: Conclusion
CU dependent Palette Size
  Provide decent trade-off between performance and complexity
  Resolve throughput issue with small CU size
  Gains observed over the case that MaxPaletteSize = 15, MaxPalettePredictorSize = 32
Recommendation
  Adopt it into HEVC SCC WD and SCM 3.0