## Slide 1: JCTVC-T0021 CE6: Summary report of CE on improvements of palette mode
20th JCTVC Meeting, Geneva, CH. Feb.2015
Presenter: PoLin Lai
<number>

## Slide 2: CE1 Tests and Cross-checks
Test A.1 - Extended copy_above mode to the first line
  JCTVC-T0036/T0037
  Cross-check: JCTVC-T0151
Test A.2 – Generalized copy_above mode
  JCTVC-T0038
  Cross-check: JCTVC-T0131
Test B.1 – Modified palette run coding
  JCTVC-T0034
  Cross-check: JCTVC-T0180
Test C.1 – 2D index map coding for palette mode
  JCTVC-T0124
  Cross-check: JCTVC-T0032
Test D.1 – Encoder modification of palette coding for escape pixels
  JCTVC-T0044
  Cross-check: JCTVC-T0033
<number>
Notes: <number>

## Slide 3: Test A.1 (JCTVC-T0036/T0037)
Extended copy_above mode to the first line
Convert neighbouring CU pixels (NCP) into palette indices
Minimum SAD, between pixel value and a colour in palette
  Min-SAD search over all colours in palette (max = 31)
  Min-SAD search over the first 8 colours in palette
  SAD computed using 3 or 1 components
  Index redundancy removal (in SCM3.0): From parsed index, need to know the “reference index”, to reconstruct the current index
    If “reference index” is from NCP  Known only at reconstruction-stage (Index cannot be reconstructed in parsing-stage)
    Solution, “Partial Redundancy Removal”: If the reference index is from the NCP, skips index redundancy removal (reconstructed index = parsed index)
Directly copy pixel value of NCP
  No SAD comparison
  “Partial Redundancy Removal”
<number>

## Slide 4: Test A.1 (JCTVC-T0036/T0037): Results
Partial redundancy removal: 0.1%~0.2% loss, no need to decouple parsing and reconstruction
Directly copy pixel: Comparable results , with no need for SAD comparisons.
<number>

## Slide 5: Test A.2 (JCTVC-T0038)
Generalized copy_above mode
For copy_above mode, signal T: The offset between the current row R and the reference row R-T where the indices are copied from.
Neighbouring CU pixels (NCP) are also used, as described in Test A.1
<number>

## Slide 6: Test A.2 (JCTVC-T0038): Results
Partial redundancy removal: 0.1%~0.2% loss, no need to decouple parsing and reconstruction
Directly copy pixel: Comparable results, with no need for SAD comparisons.
<number>

## Slide 7: Category A: Summary
<number>

## Slide 8: Test B.1 (JCTVC-T0034)
Modified palette run coding
A bypass coded flag is used to indicates whether the current palette run reaches the end of the CU.
<number>

## Slide 9: Test C.1 (JCTVC-T0124)
2D index map coding for palette mode
If 2D_flag = 1:
  WxH palette indices copy from a reference area indicated using (mvx,mvy)
  Signal W, H, mvx, mvy
  If reference area is outside the current CU: Convert samples to indices (Test A.1, A.2)
  Large reference area tested: 1x4 CTU, 2x4 CTU, 3x5 CTU
If 2D_flag = 0:
  SCM3.0
  COPY_INDEX_MODE
  COPY_ABOVE_MODE
<number>

## Slide 10: Test C.1 (JCTVC-T0124): Results
<number>

## Slide 11: Test D.1 (JCTVC-T0044)
Encoder modification of palette coding for escape pixels
Encoder conducts RD checks by removing least occurring palette colours
Method 1 , for current CU
  RD check #1: Encoder derives palette with M colours
  If “previous palette size S” < M – 2
    RD check #2: M-1 colours (remove the least occurring colour, those samples become Escape)
  Else
    RD check #2: Use previous palette (Sharing mode)
Method 2 , for current CU
  RD check #1: Encoder derive palette, with M colours
  If “previous palette size S” < M – 2
    RD check #2: M-1 colours
    RD check #3: M-2 colours
  Else
    RD check #2: Use previous palette (Sharing mode)
    RD check #3: M-1 colours
<number>

## Slide 12: Test D.1 (JCTVC-T0044): Results
<number>