## Slide 1: Non-CE1: On intra mode MPM derivation for SCC JCTVC-T0049
C. Gisquet, G. Laroche, P. Onno
20th Meeting: Geneva, CH, 10–18 Feb. 2015

## Slide 2: Basic idea
Screen Content has strong directional features
  Textures, patterns, windows edges are often vertical and vertical
This is in contrast to natural content that is smoother
  Intra mode coding is biased towards PLANAR and DC
For SCC, HOR/VER would be better
  But what is SCC ? When should this be done
  Neighbor CU coding mode is a good indication of it

## Slide 3: Proposal
Current CU
Top CU
Left CU
Current CU is likely SCC-like if its neighbors are coded using a SCC mode
  If left CU is IBC or palette, use HOR
  If top CU is IBC or palette, use VER
Corresponding normative changes
  Otherwise, if CuPredMode[ xNbX ][ yNbX ] is equal to MODE_INTER or pcm_flag[ xNbX ][ yNbX ] is equal to 1, candIntraPredModeX is set equal to INTRA_DC,
  […]
  Otherwise, if intra_bc_flag[ xNbX ][ yNbX ] is equal to 1 or palette_mode_flag[ xNbX ][ yNbX ] is equal to 1, candIntraPredModeA and candIntraPredModeB are respectively set to INTRA_ANGULAR10 and INTRA_ANGULAR26;
  […]

## Slide 4: Further observations: specifications
Palette and IBC modes are intra modes (section 7.3.8.5):
Section 8.4.2, “Derivation process for luma intra prediction mode”:
  […]
  Otherwise, if CuPredMode[ xNbX ][ yNbX ] is equal to MODE_INTER or pcm_flag[ xNbX ][ yNbX ] is equal to 1, candIntraPredModeX is set equal to INTRA_DC
  […]
  Otherwise, candIntraPredModeX is set equal to IntraPredModeY[ xNbX ][ yNbX ]
What’s the value of IntraPredModeY for IBC and palette modes?
coding_unit( x0, y0, log2CbSize ) { | Descriptor
[…] | 
if( palette_mode_enabled_flag && ChromaArrayType = = 3 && CuPredMode[ x0 ][ y0 ] = = MODE_INTRA && !intra_bc_flag[ x0 ][ y0 ] ) | 
palette_mode_flag[ x0 ][ y0 ] | ae(v)

## Slide 5: Further observations: code
In the code:
  isIntra is (mode == MODE_INTRA) but IBC is MODE_INTRA_BC…
    Is not Intra, get DC as default value
  Palette does get IntraPredModeY, which is initialized to DC…
What actually happens:
  Otherwise, if CuPredMode[ xNbX ][ yNbX ] is equal to MODE_INTER or or intra_bc_flag[ xNbX ][ yNbX ] is equal to 1, or palette_mode_flag[ xNbX ][ yNbX ] is equal to 1 or pcm_flag[ xNbX ][ yNbX ] is equal to 1, candIntraPredModeX is set equal to INTRA_DC
Some clarification needed?

## Slide 6: Results
Thanks ITRI for cross-checking
CTC, 4:4:4 lossy:
CTC, 4:2:0 lossy
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | 0.0%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 0.2% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | -0.2%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.3% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.2% | -0.2% | -0.2% | -0.1% | 0.1% | -0.2% | -0.5% | -0.3%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | 0.1% | 0.0% | 0.0% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
Text & graphics with motion, 720p | -0.5% | -0.5% | -0.3% | -0.4% | -0.4% | -0.2% | -0.2% | -0.6% | -1.5%
Mixed content, 480p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.2% | 0.1%
Animation, 768p | -0.4% | -0.3% | -0.3% | -0.1% | 0.0% | 0.0% | 0.0% | 0.2% | 0.1%
Average of all sequences | -0.3% | -0.3% | -0.2% | -0.2% | -0.2% | -0.1% | -0.1% | -0.3% | -0.7%

## Slide 7: Conclusion
Intra mode coding may have room for some potential improvements
  Text-wise?
  Coding efficiency-wise
It is suggested therefore to consider the current normative changes for inclusion