## Slide 1: JCTVC-T0066/JCTVC-T0067 CE1-related: Bypassing the context-based coding for CU-level transpose flag / CE1-related: Bypassing the context-based coding for CU-level share flag
Geneva Feb. 2015

## Slide 2: JCTVC-T0066 CE1-related: Bypassing the context-based coding for CU-level transpose flag
Yao-Jen Chang, Chun-Lung Lin, Ching-Chieh Lin, Jih-Sheng Tu, and Chao-Hsiung Hung,
Geneva Feb. 2015

## Slide 3: Issue in the current palette coding design
There are three main CU-level syntax elements coded with context models in the current palette coding:
  palette_mode_flag
  palette_share_flag
  palette_transpose_flag
Context coded syntax elements need a context update process, which slows down the system throughput.
Notes: <number>

## Slide 4: Current syntax for palette_transpose_flag
Palette_transpose_flag needs to update two contexts during coding in the current design
<number>
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
palette_share_flag | 0 | na | na | na | na | na
palette_escape_val_present_flag | bypass | na | na | na | na | na
palette_transpose_flag | 0, 1 | na | na | na | na | na
Notes: <number>

## Slide 5: Our proposed solution (T0066)
Using bypass mode to code the CU-level transpose flag
  Reduce two contexts for updating
<number>
Notes: <number>

## Slide 6: Results of lossy test condition
Common Test Condition:
Coding time for RA & LB is not reliable
<number>
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | -0.1% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1% | 0.1% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | -0.1% | 0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1% | 0.1% | 0.1% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 102% |  |  | 101% |  | 

## Slide 7: Results of lossless test condition
Common Test Condition:
Coding time for RA & LB is not reliable
<number>
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  |  | 100% |  |  |  | 100% |  |  | 
Dec Time[%] | 101% |  |  |  | 103% |  |  |  | 102% |  |  | 

## Slide 8: Conclusions for JCTVC-T0066
Bypassing two contexts for CU-level “palette_transpose_flag” is proposed to improve the data throughput.
There is no gain loss with our proposed simplification under CTC.
<number>
Notes: Still need some improvements for the third bullet.
<number>

## Slide 9: JCTVC-T0067 CE1-related: Bypassing the context-based coding for CU-level share flag
Yao-Jen Chang, Chun-Lung Lin, Ching-Chieh Lin, Chao-Hsiung Hung, and Jih-Sheng Tu
Geneva Feb. 2015

## Slide 10: Issue in the current palette coding design
There are three main CU-level syntax elements coded with context models in the current palette coding:
  palette_mode_flag
  palette_share_flag
  palette_transpose_flag
More context coded syntax elements, lower data throughput

## Slide 11: Current syntax for palette_share_flag
Palette_share_flag needs to update one context during coding in the current design
<number>
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
palette_share_flag | 0 | na | na | na | na | na
palette_escape_val_present_flag | bypass | na | na | na | na | na
palette_transpose_flag | 0, 1 | na | na | na | na | na
Notes: <number>

## Slide 12: Our proposed solution (T0067)
Replacing the context mode with bypass mode for “palette_share_flag”
    Reduce one context for updating
<number>
Notes: <number>

## Slide 13: Results of lossy test condition
Common Test Condition:
Coding time for RA & LB is not reliable
<number>
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | -0.1% | 0.1% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.2%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.1% | 0.1% | 0.1% | 0.2% | 0.2% | 0.0% | 0.2% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.0% | 0.0% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 102% |  |  | 101% |  | 
Notes: <number>

## Slide 14: Results of lossless test condition
Common Test Condition:
Coding time for RA & LB is not reliable
<number>
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  |  | 100% |  |  |  | 100% |  |  | 
Dec Time[%] | 101% |  |  |  | 103% |  |  |  | 102% |  |  | 

## Slide 15: Combination of JCTVC-T0066 and JCTVC-T0067
The “palette_share_flag” and the “palette_transpose_flag” are coded by bypass mode
      Reduce three contexts for updating
<number>
Notes: <number>

## Slide 16: Lossy results for the combination of T0066 and T0067
<number>
Bypassing 1 context model for “palette_share_flag” | G/Y |  | 
+ Bypassing 2 context models for “palette_transpose_flag” | AI | RA | LB
RGB, text & graphics with motion, 1080p & 720p | 0.01% | 0.06% | -0.05%
RGB, mixed content, 1440p & 1080p | 0.02% | 0.02% | 0.05%
RGB, Animation, 720p | 0.01% | 0.02% | 0.02%
RGB, camera captured, 1080p | -0.02% | 0.02% | 0.07%
YUV, text & graphics with motion, 1080p & 720p | 0.02% | 0.06% | 0.01%
YUV, mixed content, 1440p & 1080p | 0.01% | 0.05% | -0.14%
YUV, Animation, 720p | 0.02% | 0.02% | 0.07%
YUV, camera captured, 1080p | -0.01% | 0.01% | -0.06%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Common Test Condition:
Coding time for RA & LB is not reliable

## Slide 17: Lossless results for the combination of T0066 and T0067
Common Test Condition:
Coding time for RA & LB is not reliable
<number>
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  |  | 101% |  |  |  | 100% |  |  | 
Dec Time[%] | 100% |  |  |  | 101% |  |  |  | 100% |  |  | 

## Slide 18: Conclusions for JCTVC-T0067
Bypassing 1 context in the coding of “palette_share_flag” for higher data throughput.
  No gain loss under CTC
Bypassing 3 contexts in the coding of “palette_share_flag” and “palette_transpose_flag” for higher data throughput.
  No gain loss under CTC
<number>
Notes: Still need some improvements for the third bullet.
<number>

## Slide 19: Recommendations
Recommend to adopt the proposed combination (JCTVC-T0066 & JCTVC-T0067) for Screen Content Coding.
<number>

## Slide 20: Acknowledgements
Thank Qualcomm for crosschecking JCTVC-T0066
Thank Microsoft for crosschecking JCTVC-T0067
<number>

## Slide 21: Thank You
<number>