## Slide 1: JCTVC-T0068 Non-CE1: Binarization modification for CU-level palette flags
Yao-Jen Chang, Chun-Lung Lin, Ching-Chieh Lin, Jih-Sheng Tu, and Chao-Hsiung Hung
Geneva, Switzerland
February, 2015
Notes: <number>

## Slide 2: Current design in SCM3.0
  palette_escape_val_present_flag: indicate if the CU contains the escape coded pixels
palette_transpose_flag: indicate the scan of the pixels is horizontal scan or vertical scan
A fixed-length coding is used in the SCM3.0 to sequentially binarize the two flags:
<number>
Case | palette_escape_val_present_flag | palette_transpose_flag | binarization
0 | 0 | 0 | ‘00’
1 | 0 | 1 | ‘01’
2 | 1 | 0 | ‘10’
3 | 1 | 1 | ‘11’
Notes: <number>

## Slide 3: Observation
The probability of Case 0 is high.
<number>
Case | palette_escape_val_present_flag | palette_transpose_flag | binarization
0 | 0 | 0 | ‘00’
1 | 0 | 1 | ‘01’
2 | 1 | 0 | ‘10’
3 | 1 | 1 | ‘11’
Notes: <number>

## Slide 4: Proposed binarization
A simple variable-length coding is proposed.
<number>
Case | palette_escape_val_present_flag | palette_transpose_flag | binarization
0 | 0 | 0 | ‘0’
1 | 0 | 1 | ‘10’
2 | 1 | 0 | ‘110’
3 | 1 | 1 | ‘111’
Notes: <number>

## Slide 5: Two versions for simulations
There are two versions of the proposed binarization for simulations
  Current method in SCM 3.0: Two contexts are allowed to be updated
  Proposed method
    Version 1: No context updated
    Version 2: One context updated
  Version 1 can achieve higher data throughput.
    Fewer updating contexts, higher data throughput.
<number>
Notes: <number>

## Slide 6: Results of AI, Lossy, G/Y
<number>
 | All Intra, G/Y | 
 | Version 1 - No updated Context model | Version 2 - One updated Context model
RGB, text & graphics with motion, 1080p & 720p | -0.1% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.2%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0%
Enc Time[%] | 100% | 100%
Dec Time[%] | 100% | 100%
Notes: <number>

## Slide 7: Results of RA, Lossy, G/Y
<number>
 | All Intra, G/Y | 
 | Version 1 - No updated Context model | Version 2 - One updated Context model
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0%
YUV, Animation, 720p | -0.1% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0%
Enc Time[%] | 100% | 100%
Dec Time[%] | 101% | 101%
Notes: <number>

## Slide 8: Results of LB, Lossy, G/Y
<number>
 | All Intra, G/Y | 
 | Version 1 - No updated Context model | Version 2 - One updated Context model
RGB, text & graphics with motion, 1080p & 720p | -0.1% | 0.0%
RGB, mixed content, 1440p & 1080p | -0.1% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.0%
YUV, mixed content, 1440p & 1080p | -0.1% | 0.0%
YUV, Animation, 720p | -0.1% | 0.0%
YUV, camera captured, 1080p | -0.1% | -0.1%
Enc Time[%] | 100% | 100%
Dec Time[%] | 101% | 101%
Notes: <number>

## Slide 9: Conclusion
A binarization method is proposed based on a simple variable-length coding for
  palette_escape_val_present_flag
  palette_transpose_flag
Compared with SCM3.0:
  0.2% gain with less updating contexts
  0.1% gain with no updating context
  Less updating contexts result in higher throughput
<number>
Notes:   ag
<number>

## Slide 10: Recommendation
Recommend to adopt the proposed binarization for Screen Content Coding.
<number>
Notes: <number>

## Slide 11: Acknowledgement
Thank Sharp for cross check
<number>
Notes: <number>

## Slide 12: Thank you!
<number>

## Slide 13: Appendix
<number>

## Slide 14: Results of Lossy in CTC
<number>
Version 1 (No updated context models) | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | 0.0% | -0.1% | -0.1% | -0.1% | 0.1% | 0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1% | 0.0% | 0.0% | 0.1% | -0.1% | -0.1% | 0.2% | -0.1%
YUV, Animation, 720p | 0.0% | -0.1% | -0.1% | -0.1% | -0.1% | 0.1% | -0.1% | 0.0% | -0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.1%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  |  | 101% |  | 
Version 2 (One updated context models) | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.2% | -0.1% | -0.1% | 0.0% | 0.0% | -0.2% | 0.0% | -0.1% | -0.2%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.2% | 0.0% | 0.0% | -0.2% | 0.0% | -0.2% | -0.2%
YUV, Animation, 720p | 0.0% | -0.1% | -0.1% | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | -0.1% | -0.1% | 0.0% | 0.2%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  |  | 101% |  | 

## Slide 15: Results of Lossless in CTC
<number>
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
Version 2 (One updated context models) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  |  | 100% |  |  |  | 100% |  |  | 
Dec Time[%] | 100% |  |  |  | 101% |  |  |  | 100% |  |  | 
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
Version 1 (No updated context models) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  |  |  | 100% |  |  |  | 99% |  |  | 
Dec Time[%] | 101% |  |  |  | 101% |  |  |  | 100% |  |  |