## Slide 1: CE2-related: on the initialization of block vector prediction for intra block copy
Xiaozhong Xu, Tzu-Der Chuang,
Shan Liu and Shawmin Lei
JCTVC-T0081

## Slide 2: Proposal Summary
Two methods are proposed to fix/simplify the initialization of block vector predictor at the beginning of each CTU.
The impacts on coding performance for both methods are negligible

## Slide 3: Problem statement (1)
The BVP for IBC mode
  2 spatial candidates and the last 2 coded block vectors
  The first 2 available ones are used as BV predictors
Currently in WD specification:
  The last 2 coded block vectors are initialized at the beginning of each CTU as (-2*w, 0) and (-w, 0)
  w is the first Intra BC coded CU width in the CTU
  The last 2 coded BVs will then be updated each time a new BV is decoded
  The software implementation for this initialization process does not match the WD

## Slide 4: Problem statement (2)
For the first decoded IBC PU (with CU width W1), the last 2 BVs are set to be (-2*W1, 0) and (-W1, 0), and the decoded BV for this PU is BV1 = ( BV1_x, BV1_y)
  The last 2 BVs will be updated using BV1
For the second decoded IBC PU (with CU width W2):
  In the current WD text, the last coded 2 BVs should be (BV1_x, BV1_y) and (-2*W1, 0), respectively (assuming no duplication in BV values here).
  In the current SCM software, the last 2 coded BVs for the second decoded IBC PU, are set to be (BV1_x, BV1_y) and (-2*W2, 0).

## Slide 5: Problem statement (3)
A mismatch between software and text
The initialization values depend on the first IBC block’s CU size, which is a variable for each CTU

## Slide 6: Proposed methods
Method 1: fix the software to align with text.
Method 2: use a simplified initialization:
  (-2*min_CU_width, 0) and (-4*min_CU_width, 0) are used for the initialization of the last 2 coded BVs, at the begining of each CTU
  No longer CU size dependent
  No need to detect whether the current CU is the first coded IBC CU

## Slide 7: Simulation results
Method 1

## Slide 8: Simulation results
Method 2

## Slide 9: Conclusion
In this contribution, two methods are proposed to change the initialization of block vector predictor
  Method 1: fix the software to match the spec.
  Method 2: simplify the initialization values to be CU size independent and removing the checking for detecting the first coded IBC CU
The impact on coding performance is minimal
Recommend to adopt one method from this proposal

## Slide 11: 420 results for method 1

## Slide 12: 420 results for method 2