## Slide 1: JCTVC-T0082 CE1-related: Syntax fixes for the palette mode
Yao-Jen Chang, Chun-Lung Lin, Ching-Chieh Lin, Jih-Sheng Tu and Chao-Hsiung Hung
Geneva, Switzerland
February, 2015
Notes: <number>

## Slide 2: Issue for zero palette size in the current design
If the stuffing buffer is empty, there are two decoding processes to specify that the palette size is zero:
  Parse palette_share_flag as ‘1’.
  Parse palette_share_flag as ‘0’, and then parse palette_num_signaled_entries as ‘0’.
<number>
Notes: <number>

## Slide 3: Proposed syntax modification
Unify and clean up the syntax for the case of zero palette size:
<number>
Notes: <number>

## Slide 4: Issue for zero palette size in the proposed design
If the stuffing buffer is empty, there is only one decoding process to specify that the palette size is zero:
  Parse palette_share_flag as ‘1’.
  Parse palette_share_flag as ‘0’, and then parse palette_num_signaled_entries as ‘0’.
    Unify the decoding process for the case of zero palette size
    Clean-up
<number>
Notes: <number>

## Slide 5: Results of Lossy for AI/RA/LB
<number>
 | G/Y |  | 
 | AI | RA | LB
RGB, text & graphics with motion, 1080p & 720p | -0.03% | 0.01% | -0.03%
RGB, mixed content, 1440p & 1080p | 0.00% | 0.01% | 0.06%
RGB, Animation, 720p | 0.00% | 0.07% | 0.00%
RGB, camera captured, 1080p | -0.02% | -0.03% | 0.06%
YUV, text & graphics with motion, 1080p & 720p | 0.02% | 0.02% | 0.00%
YUV, mixed content, 1440p & 1080p | -0.01% | 0.10% | -0.09%
YUV, Animation, 720p | 0.03% | -0.05% | -0.01%
YUV, camera captured, 1080p | 0.00% | 0.00% | -0.02%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Notes: <number>

## Slide 6: Results of Lossless in CTC
<number>
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
Version 1 (No updated context models) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 101% |  |  |  | 100% |  |  |  | 100% |  |  | 
Dec Time[%] | 100% |  |  |  | 100% |  |  |  | 100% |  |  | 

## Slide 7: Conclusion
Clean up the syntax for palette_share_flag
Unify the decoding process for the case of zero palette size when the stuffing buffer is empty
Negligible coding loss for the syntax modification
<number>
Notes: <number>

## Slide 8: Recommendation
Recommend to adopt the syntax modification for the Screen Content Coding.
<number>
Notes: <number>

## Slide 9: Acknowledgement
Thank InterDigital for cross check
<number>
Notes: <number>

## Slide 10: Thank you!
<number>

## Slide 11: Appendix
<number>

## Slide 12: Results of Lossy in CTC
<number>
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.2% | -0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | -0.2%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.1% | -0.1% | 0.0% | 0.3%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 0.2% | 0.0% | 0.4% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.0%
Enc Time[%] | 100% |  |  | 100% |  |  | 100% |  | 
Dec Time[%] | 100% |  |  | 101% |  |  | 100% |  |