## Slide 1: JCTVC-T0086 Non-CE1: Parallel processing method for index map coding
Yao-Jen Chang, Chun-Lung Lin, Ching-Chieh Lin, Chao-Hsiung Hung and Jih-Sheng Tu
Geneva, Switzerland
February, 2015
Notes: <number>

## Slide 2: Issue about the palette mode
The current design:
  The palette mode is decoded pixel-by-pixel.
No way to parallelize the decoding process for the reconstruction process of the palette-based CU.
<number>
Notes: <number>

## Slide 3: Proposed design
A 2Nx2N index map is divided into two 2NxN sub-maps during the parsing
Two sub-maps can decode the indexes concurrently
2x system throughput due to parallelization
<number>
8x8 Index map
Two 8x4 sub-maps
Notes: <number>

## Slide 4: One index issue in the proposed sub-map coding
The current design:
  The index map coding with single index case is skipped without signaling
The proposed partition design:
  A new flag “single_index_flag” is used to indicate the single index case for a sub-map
<number>
Notes: <number>

## Slide 5: Results of AI/RA/LB Lossy
<number>
Enabled in 64x64~8x8 CU | G/Y |  | 
 | AI | RA | LB
RGB, text & graphics with motion, 1080p & 720p | 0.3% | 0.2% | 0.1%
RGB, mixed content, 1440p & 1080p | 0.1% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.3% | 0.1% | 0.2%
YUV, mixed content, 1440p & 1080p | 0.1% | 0.1% | 0.0%
YUV, Animation, 720p | 0.0% | -0.1% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | -0.1%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
Coding time is not reliable due to running on different computing clusters.
Anchor: SCM3.0
Notes: <number>

## Slide 6: Results of AI/RA/LB Lossy
<number>
Enabled in 64x64~8x8 CU | G/Y |  | 
 | AI | RA | LB
RGB, text & graphics with motion, 1080p & 720p | 0.2% | 0.2% | 0.1%
RGB, mixed content, 1440p & 1080p | 0.1% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.2% | 0.1% | 0.2%
YUV, mixed content, 1440p & 1080p | 0.1% | 0.1% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 101% |  | 
Coding time is not reliable due to running on different computing clusters.
Anchor: SCM3.0 + JCTVC-T0034 (Run_to_the_End)
Notes: <number>

## Slide 7: Conclusion
  This contribution proposes to partition a 2Nx2N index map into two 2NxN sub-maps for parallelization of the index map coding
  2x system throughput improvement for index map coding
  On top of SCM3.0
    max. of 0.3% loss
  On top of SCM3.0 + JCTVC-T0034
    max. of 0.2% loss
    Run_to_the_End signaling in JCTVC-T0034 can improve the gain of the sub-map index coding
<number>
Notes: <number>

## Slide 8: Recommendation
Recommend to further study the parallel processing in CE for the Screen Content Coding.
<number>
Notes: <number>

## Slide 9: Acknowledgement
Thank Mitsubishi for cross check!
Thank Canon for cross check!
<number>
Notes: <number>

## Slide 10: Thank you!
<number>

## Slide 11: Appendix
<number>

## Slide 12: Results of AI/RA/LB Lossy
<number>
Enabled in 8x8 CU only | G/Y |  | 
 | AI | RA | LB
RGB, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.1%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.1% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.1% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | -0.1%
Enc Time[%] | 107% |  | 
Dec Time[%] | 74% |  | 
Coding time is not reliable due to running on different computing clusters.
Anchor: SCM3.0
Notes: <number>

## Slide 13: Results of AI/RA/LB Lossy
<number>
Enabled in 8x8 CU only | G/Y |  | 
 | AI | RA | LB
RGB, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.1%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.1% | -0.1%
RGB, Animation, 720p | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.0% | 0.1%
YUV, mixed content, 1440p & 1080p | 0.1% | 0.0% | 0.1%
YUV, Animation, 720p | 0.0% | 0.1% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 107% |  | 
Dec Time[%] | 74% |  | 
Coding time is not reliable due to running on different computing clusters.
Anchor: SCM3.0 + JCTVC-T0034 (Run_to_the_End)
Notes: <number>