## Slide 1: Non-CE3: Adaptive PU partitioning for intra block copy JCTVC-T0091
Krishna Rapaka, Marta Karczewicz, Vadim Seregin

## Slide 2: T0091 : Proposed method
IBC fixed PU partitions
Proposed adaptive Intra block copy sub-partitioning

## Slide 3: Proposed changes to Intra BC
The presence of sub-PU’s and the sub-PU split info within the current PU is signalled.
Each Sub-PU has associated block vector in the similar lines to the PU.
The sub-PU splitting is not enabled for NxN PU modes.. The worst case regular bins and MVs for CU does not exceed the HEVC v2 specifications.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -1.1% | -1.0% | -1.0%
RGB, mixed content, 1440p & 1080p | -1.0% | -0.9% | -0.9%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -1.0% | -0.9% | -0.9%
YUV, mixed content, 1440p & 1080p | -1.0% | -0.9% | -0.9%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 120% |  | 
Dec Time[%] | 101% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.7% | -0.6% | -0.7%
RGB, mixed content, 1440p & 1080p | -0.4% | -0.4% | -0.5%
RGB, Animation, 720p | 0.0% | 0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.6% | -0.7% | -0.6%
YUV, mixed content, 1440p & 1080p | -0.5% | -0.3% | -0.3%
YUV, Animation, 720p | 0.0% | -0.2% | 0.1%
YUV, camera captured, 1080p | -0.1% | 0.0% | -0.1%
Enc Time[%] | 103% |  | 
Dec Time[%] | #VALUE! |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.4% | -0.3% | -0.4%
RGB, mixed content, 1440p & 1080p | -0.3% | -0.1% | 0.0%
RGB, Animation, 720p | 0.0% | 0.1% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p & 720p | -0.3% | -0.4% | -0.6%
YUV, mixed content, 1440p & 1080p | -0.4% | -0.2% | -0.2%
YUV, Animation, 720p | 0.0% | -0.2% | -0.1%
YUV, camera captured, 1080p | 0.0% | 0.1% | 0.1%
Enc Time[%] | 94% |  | 
Dec Time[%] | 95% |  |