## Slide 1: Non-CE3: Vector coding for CE3 Test A on Intra line Copy mode JCTVC-T0092
Krishna Rapaka, Marta Karczewicz, Vadim Seregin

## Slide 2: CE3 : Test A : Intra Line copy
*JCTVC-T0105
ILC is a PU based mode.
Every line corresponds to a partition and has a block vector.
The block vector is coded as in SCM 3.0 IBC and RQT is changed to disables explicit RDPCM.

## Slide 3: Proposed solution
First intra line difference vector in the PU are coded using the unified binarization as tested in CE2 Test 5.1
Rest of intra line difference vector in the PU are bypass coded using the above binarization.
Remove the constraints on RDPCM for ILC mode.
Intra line copy is not enabled for NxN.
Prediction Mode (Note: CU Size = 8x8) | 4x8, Uni Prediction (SCM-3.0) | 1x4, IntraLC | 1x4, ILC + RDPCM_OFF | T0092
Number of Context-coded Bins | 488 | 510 | 486 | 485

## Slide 4: Proposed changes to Intra BC
First Line Vector are coded using CE2 : Test 5.1 Binarization.
Rest of the Line Vectors are coded using Bypass flag
Remove the constraints on RDPCM for ILC mode.
Intra line copy is not enabled for NxN.
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -1.9% | -1.7% | -1.7%
RGB, mixed content, 1440p & 1080p | -2.0% | -1.7% | -1.7%
RGB, Animation, 720p | 0.0% | -0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -1.7% | -1.6% | -1.5%
YUV, mixed content, 1440p & 1080p | -1.7% | -1.7% | -1.7%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 109% |  | 
Dec Time[%] | 86% |  | 
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -1.2% | -0.9% | -1.0%
RGB, mixed content, 1440p & 1080p | -1.0% | -0.8% | -0.9%
RGB, Animation, 720p | 0.0% | 0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -1.1% | -1.0% | -1.0%
YUV, mixed content, 1440p & 1080p | -1.0% | -0.9% | -0.9%
YUV, Animation, 720p | 0.0% | -0.1% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | -0.1%
Enc Time[%] | 90% |  | 
Dec Time[%] | 91% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.8% | -0.6% | -0.6%
RGB, mixed content, 1440p & 1080p | -0.5% | -0.3% | -0.4%
RGB, Animation, 720p | 0.0% | 0.0% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.6% | -0.5% | -0.7%
YUV, mixed content, 1440p & 1080p | -0.5% | -0.6% | -0.6%
YUV, Animation, 720p | 0.0% | 0.1% | -0.1%
YUV, camera captured, 1080p | -0.1% | 0.1% | 0.1%
Enc Time[%] | 86% |  | 
Dec Time[%] | 89% |  |