## Slide 1: Non-CE2: Zero merging candidates derivation for Intra BC/Inter signalling unification
Chao Pang, Vadim Seregin, Marta Karczewicz

## Slide 2: Intra BC/Inter signaling unification
In CE2 Test 1, Intra BC/Inter signalling unification is investigated.
Current picture is added to the reference picture list.
Intra BC can be differentiated from the conventional inter by checking whether the reference picture is the current picture.
Zero merging candidates are used in case the merge candidate list is not full; however, zero MVs are always invalid for Intra BC.

## Slide 3: Proposed method
For zero merging candidates, the derivation process for reference indices is kept the same as in HEVC;
When the reference picture is the current picture, predefined MVs, instead of zero MVs, are used;
  5 predefined MVs, {(-4 * CUs, 0), (-8*CUs, 0), (0, -4 * CUs), (0, -8 * CUs), (-4 * CUs, -4 * CUs)}.
The proposed method only changes the MVs in zero merging candidats for Intra BC.

## Slide 4: Experimental results
4:4:4 lossy coding in CE2 Test 1
4:4:4 lossy coding with proposed method

## Slide 5: Discussion on Intra BC constraints
In current SCC, the following constraints applied for Intra BC:
  The reference block should be within the same slice/tile.
  The reference block cannot overlap with current CU.
  The whole reference block should be in the causal neighborhood.
  The reference block should be within a certain region due to the parallelization implementation consideration.
  When constrained intra prediction is enabled, the reference block cannot include any pixel coded with the conventional inter mode.
To avoid nonconforming bitstreams, two possible solutions.
  At decoder side, convert the final BV to a valid BV if possible.
  Replace the unavailable pixels with predefined values, such as 0, or 1 << (B - 1).

## Slide 6: Conclusions
Proposed zero merging candidate derivation method
  Used for Intra BC/Inter signalling unification.
  Use predefined MVs for zero merging candidate when the reference picture is the current picture.
Recommend to be adopted if Intra BC/Inter signalling is unified.