## Slide 1: JCTVC-T0119 Non-CE1: Improved palette run-length coding with palette flipping
Xiaoyu Xiu, Yan Ye, Yuwen He (InterDigital)
Wei Pu, Rajan Joshi, Marta Karczewicz, Feng Zou, Vadim Seregin (Qualcomm)

## Slide 2: Proposal (1)
Modified run-length coding in CE1 Test B.1
  One “run-to-the-end” flag is signaled to indicate the last run of one palette CU.
  It can only be applied to code the last run.
  The proposed palette flipping
  One CU-level flag palette_flipping_flag is proposed to indicate whether or not to flip CU vertically.
  This allows “run-to-the-end” flag to also be applied the first run.
(a) Original palette index map
(b) Flipped palette index map

## Slide 3: Proposal (2)
Encoder method in SCM-3.0
  Derives the possible largest runs for both index mode and copy-above mode, and compares the average bit costs.
  Sub-optimal when one index mode is followed by one copy-above mode, as the index run does not consider future copy-above run.
The proposed encoder improvement
  When index mode is followed by copy-above mode, it is proposed to determine the optimal combination of index run and copy-above run.

## Slide 4: Lossy coding performance
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.6% | -0.7% | -0.6%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.7% | -0.8% | -0.9%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.6% | -0.6%
YUV, Animation, 720p | 0.0% | -0.2% | -0.1%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 
Random Access |  | 
G/Y | B/U | R/V
-0.4% | -0.5% | -0.4%
-0.1% | -0.1% | -0.2%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
-0.4% | -0.6% | -0.7%
-0.2% | -0.3% | -0.5%
-0.1% | -0.1% | 0.1%
0.0% | 0.0% | 0.0%
102% |  | 
99% |  | 
Low delay B |  | 
G/Y | B/U | R/V
-0.3% | -0.4% | -0.4%
-0.3% | -0.2% | -0.3%
0.0% | -0.1% | -0.1%
0.0% | 0.0% | 0.0%
-0.4% | -0.5% | -0.5%
-0.1% | -0.3% | -0.3%
0.0% | -0.1% | 0.0%
0.0% | 0.1% | -0.2%
101% |  | 
101% |  | 
Gain for text & graphics with motion
  AI: {0.7%, 0.7%, 0.8%},
  RA: {0.4%, 0.5%, 0.6%}
  LD: {0.3%, 0.5%, 0.4%}

## Slide 5: Lossless coding performance
text & graphics with motion
  0.3%, 0.2% and 0.1% for AI, RA and LB, respectively
 | All Intra |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.3% | -0.6% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.3% | -0.3% | -0.7% | -0.1%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 98% |  |  | 
Dec Time[%] | 94% |  |  | 
Random Access |  |  | 
Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
-0.1% | -0.2% | -0.5% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
-0.1% | -0.2% | -0.5% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
95% |  |  | 
99% |  |  | 
Low Delay B |  |  | 
Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
-0.1% | -0.1% | -0.3% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
-0.1% | -0.1% | -0.3% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0% | 0.0%
96% |  |  | 
100% |  |  | 
Thanks to MediaTek for the cross-check!

## Slide 6: Closing remarks
The proposed methods
  One CU-level flag is proposed to indicate whether or not flip the CU vertically
  Encoder improvement by determining optimal combination of index run followed by copy-above run.
  Coding performance
  Average BD-rate savings for AI, RA and LB are 0.7%, -0.4% and 0.3%, respectively, for lossy coding.
  Average bit-rate savings for AI, RA and LB are 0.3%, 0.2% and 0.1%, respectively, for lossless coding.
  Little complexity impact.