## Slide 1: JCTVC-T0138: Copy Mode for Static Screen Content Coding
Thorsten Laude

## Slide 2: Copy Mode for Static Screen Content Coding
Screen content with static background
Skip mode: Signal skip flag and merge index
Proposal: Direct copy of corresponding block from closest reference frame
CTU level signaling with a binary flag
Slice level on/off switch

## Slide 3: Copy Mode for Static Screen Content Coding
Coding results (SCC CTC, Anchor: SHM-3.0)
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | -0.4% | -0.3% | -0.3%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.5% | -0.5% | -0.6%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 143% |  | 
Dec Time[%] | 108% |  | 
Runtimes are not accurate
Cross-check: JCT-VC T0150. Thanks to NCTU/ITRI

## Slide 4: Copy Mode for Static Screen Content Coding
Modified encoder with constant compression quality
Same delta QP for all frames
No flickering/pumping over time
High fidelity reference frame for copy mode
Encoding with the modified encoder
Static content: copy mode (no residual)
Moving content without changes: skip mode (no residual)
New/changing content: different mode (with residual)
 Early skip for static CTUs

## Slide 5: Copy Mode for Static Screen Content Coding
Coding results (delta QP = 0)
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.7% | -0.7% | -0.7%
RGB, mixed content, 1440p & 1080p | -0.6% | -1.5% | -1.4%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.6% | -0.8% | -0.7%
YUV, mixed content, 1440p & 1080p | -1.1% | -2.0% | -2.4%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 68% |  | 
Dec Time[%] | 83% |  | 
Runtimes are (to some extend) reliable
Cross-check: JCT-VC T0150. Thanks to NCTU/ITRI