## Slide 1
<number>
Improvements on ISC
JCTVC-T0139
10 Feb. – 18 Feb. 2015
Tao Lin
Notes: <number>

## Slide 2
Motivation
OffsetX
OffsetY
OffsetX
OffsetY
ISC Offset distribution
ABOVE + LEFT strings are less than 30%
ABOVE + LEFT strings are less than 20%
Still have big room of improvement by using ISC
127
-63
-63
63
127
-63
-63
63

## Slide 3
<number>
This Proposal
Lossy matching
  Error Limit is the same as used in CQ of Palette coding
Lossy hash: 4-bit MSB of each color components
travScan in both horizontal and vertical sacns
Redundancy removal in string offset coding
TB coding of string length
Better binarization of offset and length
  1-bit for ABOVE mode
  Other offsets use EG-2 coding
  Lengths are divided into 2 or 3 intervals, each uses FL
Major Improvements

## Slide 4
<number>
This Proposal
Minimum string length: 20 pixels outside of 2CTU
No SRAM or DDR bandwidth issue in ISC
 | Configurations |  |  |  |  |  |  | Memory Bandwidth (P) |  |  |  |  | 
Description | Block Size |  | IF Length |  | Bi Pred | Memory Pattern |  | Y Component |  |  |  |  | 
 |  |  | Y | U/V |  |  | m= | 2 | 2 | 4 | 4 | 8 | 8
 | M | N | L | L | Y or N |  | n= | 2 | 4 | 2 | 8 | 4 | 8
8x8 Bi-prediction | 8 | 8 | 8 | 6 | Y |  |  | 8 | 10 | 10 | 15 | 15 | 18
4x8 Uni-prediction | 4 | 8 | 8 | 6 | N |  |  | 6 | 7.5 | 8 | 12 | 15 | 18
8x4 Uni-prediction | 8 | 4 | 8 | 6 | N |  |  | 6 | 8 | 7.5 | 15 | 12 | 18
4x4 IBC PU | 4 | 4 | 1 | 1 | N |  |  | 2.3 | 3 | 3 | 8 | 8 | 16
1x4 ILC | 1 | 4 | 1 | 1 | N |  |  | 3 | 4 | 6 | 16 | 16 | 32
4x1 ILC | 4 | 1 | 1 | 1 | N |  |  | 3 | 6 | 4 | 16 | 16 | 32
1x1 ISC | 1 | 1 | 1 | 1 | N |  |  | 4 | 8 | 8 |  |  | 
S0139 H scan | 20 | 1 | 1 | 1 | N |  |  |  |  |  | 9.6 | 6.4 | 12.8
S0139 V scan | 1 | 20 | 1 | 1 | N |  |  |  |  |  | 6.4 | 9.6 | 12.8
Memory pattern size in typical SRAM: 2x2 pixels with a memory bus width of 2x2x24=96 bits. P-value = 4
Memory pattern size in typical DDR: 8x8 samples with a bus width of 64 bits and burst size of 8. P-value = 12.8

## Slide 5
ISC memory bandwidth
No CABAC throughput issue in T0139
Prediction Mode | JCTVC-T0139 | 
(Note: CU Size = 8x8) | Syntax Elements | Number
Mode Flag | cu_transquant_bypass_flag | 1
 | cu_skip_flag | 1
 | intra_bc_flag | 1
 | intra_sc_flag | 1
 | isc_srb_mode_flag | 1
 | isc_srb_sharing_flag | 1
Partition | N/A | 
MV or BV | isc_no_ref_pixel_flag | 64
 | isc_offsetX_zero_flag | 64
 | isc_offsetX_sign_flag | 64
 | isc_offsetY_zero_flag | 64
 | isc_offsetY_sign_flag | 64
 | isc_length_prefix | 104
Residual (4 4x4 TBs, 3 Color Components) | N/A | 
Number of Context-coded Bins |  | 430
Bins per Pixel |  | 6.71875

## Slide 6
<number>
Experiments
anchor: SCM30 CTC, 3 test conditions of reference range
 | IBC | ISC
Test condition 1 | Full-frame | 1x2-CTU
Test condition 2 | 1x4-CTU | 1x4-CTU
Test condition 3 | Full-frame | Full-frame

## Slide 7
<number>
Experiments
TC1: FF IBC and 2CTU ISC, lossy
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p |  |  |  | -2.3% | -2.7% | -2.7% | -1.6% | -1.9% | -1.8%
RGB, mixed content, 1440p & 1080p |  |  |  | -0.8% | -1.4% | -1.4% | -0.4% | -1.2% | -1.1%
RGB, Animation, 720p |  |  |  | 0.1% | 0.1% | 0.1% | 0.0% | 0.1% | 0.0%
RGB, camera captured, 1080p |  |  |  | 0.1% | 0.0% | 0.0% | 0.2% | 0.1% | 0.1%
YUV, text & graphics with motion, 1080p & 720p | -3.3% | -3.5% | -3.5% | -2.2% | -2.6% | -2.8% | -1.5% | -1.7% | -2.1%
YUV, mixed content, 1440p & 1080p | -1.3% | -2.7% | -2.6% | -0.9% | -2.2% | -2.2% | -0.3% | -2.5% | -2.3%
YUV, Animation, 720p |  |  |  | 0.0% | -0.2% | 0.1% | 0.1% | 0.3% | 0.0%
YUV, camera captured, 1080p |  |  |  | 0.1% | 0.1% | 0.0% | 0.0% | 0.2% | 0.0%
Enc Time[%] |  |  |  | 156% |  |  | 143% |  | 
Dec Time[%] |  |  |  | 104% |  |  | 105% |  | 

## Slide 8
<number>
Experiments
TC1: FF IBC and 2CTU ISC, lossless
 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Bit-rate saving Total | Bit-rate saving (Avg) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving Total | Bit-rate saving (Avg) | Bit-rate saving (Min) | Bit-rate saving (Max) | Bit-rate saving Total | Bit-rate saving (Avg) | Bit-rate saving (Min) | Bit-rate saving (Max)
RGB, TGM, 1080p & 720p | -4.6% | -5.5% | -15.8% | -0.5% | -2.4% | -3.3% | -10.4% | -0.3% | -2.3% | -2.5% | -6.3% | -0.3%
RGB, MC, 1440p & 1080p | -0.8% | -0.9% | -1.6% | -0.3% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | -4.9% | -5.7% | -16.0% | -0.5% | -2.4% | -3.5% | -10.5% | -0.3% | -2.2% | -2.6% | -6.5% | -0.2%
YUV, MC, 1440p & 1080p | -0.9% | -0.9% | -1.7% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 387% |  |  |  | 148% |  |  |  | 134% |  |  | 
Dec Time[%] | 101% |  |  |  | 102% |  |  |  | 102% |  |  | 

## Slide 9
<number>
Experiments
TC1: 4CTU IBC and 4CTU ISC, lossy
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p |  |  |  |  |  |  |  |  | 
RGB, mixed content, 1440p & 1080p |  |  |  |  |  |  |  |  | 
RGB, Animation, 720p |  |  |  |  |  |  |  |  | 
RGB, camera captured, 1080p |  |  |  |  |  |  |  |  | 
YUV, text & graphics with motion, 1080p & 720p |  |  |  |  |  |  |  |  | 
YUV, mixed content, 1440p & 1080p |  |  |  |  |  |  |  |  | 
YUV, Animation, 720p |  |  |  |  |  |  |  |  | 
YUV, camera captured, 1080p |  |  |  |  |  |  |  |  | 
Enc Time[%] |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  |  |  |  | 

## Slide 10
<number>
Experiments
TC2: 4CTU IBC and 4CTU ISC, lossless

## Slide 11
<number>
Experiments
TC3: FF IBC and FF ISC, lossy
 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p |  |  |  |  |  |  |  |  | 
RGB, mixed content, 1440p & 1080p |  |  |  |  |  |  |  |  | 
RGB, Animation, 720p |  |  |  |  |  |  |  |  | 
RGB, camera captured, 1080p |  |  |  |  |  |  |  |  | 
YUV, text & graphics with motion, 1080p & 720p |  |  |  |  |  |  |  |  | 
YUV, mixed content, 1440p & 1080p |  |  |  |  |  |  |  |  | 
YUV, Animation, 720p |  |  |  |  |  |  |  |  | 
YUV, camera captured, 1080p |  |  |  |  |  |  |  |  | 
Enc Time[%] |  |  |  |  |  |  |  |  | 
Dec Time[%] |  |  |  |  |  |  |  |  | 

## Slide 12
<number>
Experiments
TC3: FF IBC and FF ISC, lossless

## Slide 13
<number>
Conclusions
More than 70% matching strings are not ABOVE/LEFT
  Big room for coding performance improvement by ISC
No SRAM or DDR memory bandwidth issue in ISC
No CABAC throughput issue in ISC
Recommend to adopt T0139 or further study in CE
  Further improving coding performance
  Significantly reducing encoding time w/o performance hit
Notes: <number>

## Slide 14
<number>
THANK YOU
Notes: <number>