## Slide 1: Non-CE3: 2-D Intra String Copy in HEVC SCC
JCTVC – T0193
Huawei USA R&D

## Slide 2: Summary
  For any give location, in addition to the RUN based 1D string search, a 2D string search with flexible width and height is also performed.
  If the area covered by the 2D-match result is bigger than 1D RUN length, the 2D string copy mode is selected and its (mvx, mvy, width, height) is encoded into bit-stream,
  otherwise, the current index map coding mode is selected and its (RUN) is encoded into bit-stream.
  Residual is generated and then coded using the HEVC residual coding method.

## Slide 3: Proposed Method
A one-bit context coded “2D_flag” is added to the syntax to indicate if the 2D-string copy mode is selected.
  If 2D_flag = 1, COPY_ABOVE flag is skipped,
    a one-bit context coded mvx0_flag(mvy0_flag) is added to indicate whether its motion vector mvx(mvy) is equal to zero;
      When a 2D block is a single color block, both mvx and mvy are set to 0 and the quantized version of its pixel values is encoded using TBC method.
    a one-bit context is used to encode the sign of non-zero mvx(mvy), followed by the absolute value of mvx(mvy), which is encoded using truncated binary coding (TBC) method.
    both width and height are encoded using TBC method.
  If 2D_flag = 0, COPY_ABOVE flag is encoded using one context (2 contexts are used in default RUN based 1D search)

## Slide 4: Differences to CE3 Test B.3
CE3 Test-B.3 | Non-CE3
Both 1D and 2D string search operation are done in the quantized version of the original and reconstructed pixels. | Both 1D and 2D string search operation are done in the original pixel domain.
2D string search is limited to CTU level | 2D string search is extended to CU level
In 1D/2D Pixel mode, a frequent color table is used to code pixel, either the quantized version of the original pixel, or a frequent color table index is coded into bit-stream | In 1D/2D Pixel mode, the quantized version of original pixel is coded into bit-stream

## Slide 5: Performance Lossy (the FF case of tested was mistakenly configured using 2 left CTUs instead of 1, we will update the correct result as soon as it become available)
 | 4CTU (Anchor 4CTU) |  |  | FF (Anchor FF) |  | 
 | All Intra |  |  | All Intra |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.7% | -0.9% | -0.9% | -0.7% | -0.8% | -0.8%
RGB, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.1% | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.5% | -0.5% | -0.5% | -0.6% | -0.5% | -0.5%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 118% |  |  | 131% |  | 
Dec Time[%] | 106% |  |  | 113% |  | 
 | Random Access |  |  | Random Access |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.8% | -0.9% | -0.9% | -0.7% | -0.7% | -0.7%
RGB, mixed content, 1440p & 1080p | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.5% | -0.7% | -0.6% | -0.6% | -0.6% | -0.7%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | -0.1% | -0.1% | 0.0% | -0.1%
YUV, Animation, 720p | 0.0% | 0.3% | 0.2% | 0.0% | -0.1% | 0.2%
YUV, camera captured, 1080p | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | -0.1%
Enc Time[%] | 103% |  |  | 105% |  | 
Dec Time[%] | 103% |  |  | 103% |  | 
 | Low delay B |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.6% | -0.6% | -0.5% | -0.5% | -0.6% | -0.4%
RGB, mixed content, 1440p & 1080p | 0.1% | -0.2% | -0.2% | 0.0% | -0.1% | -0.3%
RGB, Animation, 720p | -0.1% | 0.1% | 0.0% | 0.0% | 0.1% | -0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.5% | -0.4% | -0.1% | -0.3% | -0.4% | -0.4%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.3% | -0.2% | -0.3% | -0.4% | -0.1%
YUV, Animation, 720p | -0.1% | 0.1% | 0.0% | 0.0% | 0.2% | 0.1%
YUV, camera captured, 1080p | 0.0% | 0.1% | 0.2% | -0.1% | 0.2% | 0.1%
Enc Time[%] | 102% |  |  | 104% |  | 
Dec Time[%] | 106% |  |  | 108% |  | 

## Slide 6: Performance Lossless (the FF case of tested was mistakenly configured using 2 left CTUs instead of 1, we will update the correct result as soon as it become available)
 | 4CTU (Anchor 4CTU) |  |  |  | FF (Anchor FF) |  |  | 
 | All Intra |  |  |  | All Intra |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | -0.5% | -0.7% | -1.9% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.5% | -0.8% | -2.2% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.1% | -0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 120% |  |  |  | 0% |  |  | 
Dec Time[%] | 104% |  |  |  | 0% |  |  | 
 | Random Access |  |  |  | Random Access |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | -0.5% | -0.6% | -1.9% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.5% | -0.7% | -2.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 103% |  |  |  | 0% |  |  | 
Dec Time[%] | 102% |  |  |  | 0% |  |  | 
 | Low Delay B |  |  |  | Low Delay B |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Average) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, text & graphics with motion, 1080p & 720p | -0.5% | -0.6% | -1.9% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | -0.4% | -0.6% | -2.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 102% |  |  |  | 0% |  |  | 
Dec Time[%] | 103% |  |  |  | 0% |  |  | 

## Slide 7: Conclusion
Recommendation
  Further study 2-D Intra String Copy in CE