## Slide 1
<number>
CE3-related: Worst case SRAM and DDR bandwidth analysis and solutions for ISC
JCTVC-T0224
10 Feb. – 18 Feb. 2015
Tao Lin
Tongji University
Notes: <number>

## Slide 2
SRAM bandwidth analysis
All real-time video decoder chips’ clock frequency
  For full HD (125Mpixel/s): minimum 187MHz (125x1.5)
  No design will use a low frequency
  Pipeline throughput is at least 1.5 cycles per pixel
  This is a basic IC design principle
No SRAM bandwidth problem as long as the decoding operation is simple and needs at most only one SRAM read and write per pixel
ISC decoding operation is just such a simple one
2x2, 2x4, 4x2 memory pattern, P-value is also smaller
From any perspective, no SRAM bandwidth problem

## Slide 3
<number>
2CTU SRAM cost
Option 1: Reuse existing one, no cost
Option 2: Use a dedicated one, cost 0.4 penny
  2CTU SRAM size: 2x64x64x24 = 196608 bits
  Silicon area in 28nm process:0.075mm2
  300mm wafer cost: 3000USD
  Wafer area utilization: 80%
  2CTU cost: 3000*0.075/(3.14*150*150*0.8)=0.00398 USD=0.4 cents
Both SRAM bandwidth and cost are not problem

## Slide 4
Minimum string length of ISC can be limited to and 36 pixels for depth=0~2 outside of 2CTU cost
  20 pixels for depth = 3, 36 pixels for depth = 0~2
P-values: 10.7, 10,7, 14.2 vs 8, 8, 16 for IBC and 12, 15, 18 for inter 4x8 Uni-prediction
<number>
DDR Bandwidth Analysis
8x4
8x4
8x4
8x4
8x4
8x4
8x8
8x8
8x8
8x4
8x4
8x4
8x4
8x4
8x4
4x8
4x8
4x8
4x8
4x8
4x8
8x8
8x8
8x8
8x8
P = 12x8x4/36 = 10.7
P = 12x4x8/36 = 10.7
P = 8x8x8/36 = 14.2
8x8
4x8
4x8
4x8
4x8
4x8
4x8
Depth = 0~2
8x4
8x4
8x4
8x8
8x8
8x4
8x4
8x4
4x8
4x8
4x8
8x8
8x8
P = 6x8x4/20= 9.6
P = 6x4x8/20 = 9.6
P = 4x8x8/20 = 12.8
4x8
4x8
4x8
Depth = 3

## Slide 5
Reuse IBC reconstructed pixel buffer
  No dictionary
  No additional memory
  No additional cost
<number>
DDR cost

## Slide 6
ISC operation is extremely simple
  Only simple and direct copy (memory read and write) is involved
  The complete ISC decoding logic takes less than 10K logic gates
  Cost less than 0.1 penny in 28nm process
<number>
ISC decoding logic

## Slide 7
The new ISC is not old dictionary coding any more
No dictionary, no additional memory
ISC does not have SRAM and DDR bandwidth problem at all
SRAM cost for ISC is either zero or 0.4 penny
ISC decoder operation is extremely simple and costs almost nothing
Using SCM3.0 FF IBC as anchor, ISC can provide
  About -7% BD-rate reduction in lossy coding
  About -10% bit-rate saving in lossless coding
  Total cost less than 0.5 penny in 28nm process
ISC can provide such big gain at almost no cost
<number>
Conclusions

## Slide 8
ISC will not hurt anything
IBC and Palette still play a bigger role than ISC
IBC, Palette, ISC contributions
  IBC: ~30%
  Palette: ~20% on top of IBC
  ISC: ~10% on top of both IBC and Palette
There may be no other single tool can provide such a big gain at almost no cost
<number>
Conclusions

## Slide 9
<number>
THANK YOU
Notes: <number>