## Slide 1: JCTVC-U0021 CE1: Summary report of CE on palette mode improvements
21st JCTVC Meeting, Warsaw, PL. June 2015
PoLin Lai, Vadim Seregin, Xiaoyu Xiu, Christophe Gisquet (CE Coordinators)
<number>

## Slide 2: CE1 Tests and Cross-checks
  Test A.1 - Extended copy above mode to the first line with index adjustment bits
    JCTVC-U0061, cross-check: JCTVC-U0121
Test A.2 – Extended copy above mode to the first line with grouping the palette_run_type_flag in front
    JCTVC-U0062, cross-check: JCTVC-U0147
  Test B – Simplification for index map coding in palette mode
    JCTVC-U0050, cross-check: JCTVC-U0070
  Test C.1 – Improved palette run-length coding with palette reverse scan order
    JCTVC-U0101, cross-check: JCTVC-U0059
  Test C.2 – Palette run-length coding with rotated index scans
    JCTVC-U0088, cross-check: JCTVC-U0108
Test D – Modification of palette run coding
    JCTVC-U0122, cross-check: JCTVC-U0117
<number>
Notes: <number>

## Slide 3: Background: Index adjustment
Current WD:
Number of palette indices [bypass]  Group palette indices [bypass]  pairs { run_type flag [ctx], runs [ctx+bypass] }  Group Escapes [bypass]
For signalling a index:
  If previous is COPY_ABOVE, the current pixel index ≠ above pixel index
  If previous is COPY_INDEX, the current pixel index ≠ previous pixel index
  One less possible value, for current index
Binarization: “truncated binary”, AdjustedMaxPaletteIndex = MaxPaletteIndex – 1
Adjust parsed index: After parsing run_type and run
  “Ref Palette Index” = Above pixel index, if previous is COPY_ABOVE
  = Previous pixel index, if previous is COPY_INDEX
  If parsed current index >= Ref palette index
  Actual current index = Parsed current index + 1
<number>

## Slide 4: Test A.1 (JCTVC-U0061)
Extended COPY_ABOVE_MODE to the first line
Directly copy pixel value from the above CU
If unavailable (slice/tile boundary, CIP), use color value of the first palette entry
How to handle index adjustment?
Always enable, AdjustedMaxPaletteIndex = MaxPaletteIndex – 1
Additional syntax:
  If orange pixels (previous pixel is COPY_ABOVE && above pixel is from above CU)
  If index = MaxPaletteIndex , signal the “MaxPaletteIndex – 1”
  If “MaxPaletteIndex – 1” is signaled, signal index refinement bit to indicate the index is MaxPaletteIndex – 1 or MaxPaletteIndex
Palette index syntaxes separated into two parts:
Number of palette indices [bypass]  Group palette indices [bypass]  { run_type flag [ctx], Palette runs [ctx+bypass], index refinement bit [bypass] (conditionally signalled) }  Group Escape [bypass]
<number>

## Slide 5: Test A.2 (JCTVC-U0062)
Extended COPY_ABOVE_MODE to the first line
Directly copy pixel value from the above CU
If unavailable (slice/tile boundary, CIP), use color value of the first palette entry
How to handle index adjustment?
Group run_type flags in the front:
Number of palette indices [bypass ] Group run_type flags [ctx]  Group palette indices [bypass] Group Palette runs [ctx+bypass]  Group Escapes [bypass]
If previous pixel is COPY_ABOVE: No index adjustment else (previous pixel is COPY_INDEX): Apply index adjustment
<number>

## Slide 6: Test A.1 and A.2, 444 Full-frame IBC
<number>

## Slide 7: Test A.1 and A.2, 444 Full-frame IBC
<number>

## Slide 8: Background for Test B: Index adjustment
<number>
Current WD:
Number of palette indices [bypass]  Group palette indices [bypass]  pairs { run_type flag [ctx], runs [ctx+bypass] }  Group Escapes [bypass]
For signalling a index:
  If previous is COPY_ABOVE, the current pixel index ≠ above pixel index
  If previous is COPY_INDEX, the current pixel index ≠ previous pixel index
  One less possible value, for current index
Adjust parsed index: After parsing run_type and run
  “Ref Palette Index” = Above pixel index, if previous is COPY_ABOVE
  = Previous pixel index, if previous is COPY_INDEX
  If parsed current index >= Ref palette index
  Actual current index = Parsed current index + 1

## Slide 9: Test B (JCTVC-U0050)
1: Group run_type in front, no index adjustment if previous is COPY_ABOVE (No dependency from the above index) Included in Test A.2
2: Group run_type in front, no index adjustment if previous is COPY_INDEX (No dependency from the left index)
3-1: Without grouping run_type in front, completely remove index adjustment.
3-2: Group run_type in front, completely remove index adjustment.
<number>

## Slide 10: Test B (JCTVC-U0050)
<number>

## Slide 11: Test B (JCTVC-U0050)
<number>

## Slide 12: Test C.1 & C.2 (JCTVC-U0101 & U0088)
Add alternative scanning patterns, signalled using one flag
Current Draft Text: Horizontal Traverse scan, vertical Traverse scan
Test C.1: Add Reversed horizontal / vertical traverse scan
Test C.2: Add Rotated horizontal / vertical traverse scan (scan from BR)
<number>

## Slide 13
<number>
C.1: RDO method of CE.1 Test released on May 30, 2015 (encoder only changes compared to the initial C.1 release Apr. 8, 2015)
RD3: RDO method of CE.1 Test C.1 released on May 30, 2015
RD2: RDO method of CE.1 Test C.1 released on Apr. 8, 2015

## Slide 14
<number>
C.1: RDO method of CE.1 Test released on May 30, 2015 (encoder only changes compared to the initial C.1 release Apr. 8, 2015)
RD3: RDO method of CE.1 Test C.1 released on May 30, 2015
RD2: RDO method of CE.1 Test C.1 released on Apr. 8, 2015

## Slide 15
<number>
C.1: RDO method of CE.1 Test released on May 30, 2015 (encoder only changes compared to the initial C.1 release Apr. 8, 2015)
RD3: RDO method of CE.1 Test C.1 released on May 30, 2015
RD2: RDO method of CE.1 Test C.1 released on Apr. 8, 2015

## Slide 16
<number>
C.1: RDO method of CE.1 Test released on May 30, 2015 (encoder only changes compared to the initial C.1 release Apr. 8, 2015)
RD3: RDO method of CE.1 Test C.1 released on May 30, 2015
RD2: RDO method of CE.1 Test C.1 released on Apr. 8, 2015

## Slide 17: Test D (JCTVC-U0122)
Modification of palette run coding
If 1-st pixel in a line: palette_run_end_of_line_flag
If (palette_run_end_of_line_flag)
Signal number of lines L of the run
Code mapped L using xWriteCoefRemainExGolomb with order 0
Else
  Code run length as normal
Else (not 1-st pixel in a line)
Code mapped run length using xWriteCoefRemainExGolomb with order 0
<number>

## Slide 18: Test D (JCTVC-U0122)
<number>