## Slide 1: High dynamic range compatibility SEI message JCTVC-U0033
Matteo Naccari, Andrew Cotton, Sebastian Schwarz, Manish Pindoria, Marta Mrak, Tim Borer

## Slide 2: Overview
Context and motivation
Proposed SEI message
Conclusions

## Slide 3: 1. Context and motivation

## Slide 4: What we really mean by backward compatibility
Anchor
QP=21
HLG
QP=22.5

## Slide 5: Application scenarios for HDR
HEVC Main 10 decoder
New
HDR display
Bitstream
Decoded video
VUI entry
(STD-B67)
HDR service
HDR/SDR service (backwards compatibility case)
Legacy
SDR display
Bitstream
Decoded video
VUI entry
(BT.709)
New
HDR display
Decoded video
VUI entry (BT.709) - SEI message (OETF STD-B67)
New
HLS parser
HEVC Main 10 decoder
Legacy
HLS parser
New
HLS parser
HLS
HLS
HLS

## Slide 6: Enabling HDR services in broadcasting
The Hybrid Log-Gamma Opto-Electronic Transfer Function (OETF) will be used to deliver HDR services in broadcasting
  It is backward compatible
  It does not require dynamic metadata
  It is display independent
By using the Hybrid Log-Gamma (HLG) OETF an HEVC bitstream will serve both Standard Dynamic Range (SDR) and HDR receivers:
  SDR receivers will use the OETF indicated in the VUI (e.g. BT.709 OETF)
  HDR receivers will display the content using the full-dynamic range

## Slide 7: Design issue to be addressed in HDR broadcasting services
Version 1 decoders will be used in HDR services
The solution proposed here is an SEI message:
  Maintains compatibility with Version 1 receivers
  Allows frame accurate switching should it be required

## Slide 8: 2. Proposed SEI message

## Slide 9: SEI message syntax
hdr_compatibility_info( payloadSize ) { | Descriptor
hdr_compatibility_cancel_flag | u(1)
if( !hdr_compatibility_cancel_flag ) { | 
hdr_transfer_characteristics_idc | u(4)
} | 
} | 
Indicates when new HDR data are coming
Indicates which OETF is used

## Slide 10: SEI message semantics
hdr_transfer_characteristics_idc specifies which OETF should be used to display the decoded content
  0 = Use the VUI entry (for backwards compatibility)
  1 = HLG OETF
  > 1 = Reserved for future use

## Slide 11: 3. Conclusions

## Slide 12: To summarise
Backward compatibility with legacy receivers and delivery of HDR services in broadcasting is guaranteed by using the HLG OETF
HEVC Version 1 receivers can be used and HDR is enabled by using an SEI message