## Slide 1: On unification of motion vector resolution for screen content coding
Xiaozhong Xu, Shan Liu and Shawmin Lei
JCTVC-U0076

## Slide 2: Introduction
In last meeting IBC is unified to HEVC inter coding
One thing not yet unified is the adaptive MV resolution on block vectors
This proposal provides a solution to unify the adaptive MV resolution process for all vectors
  Indicated by “use_integer_mv_flag”

## Slide 3: Proposed method
It is proposed to determine the resolution of all vectors in a slice by “use_integer_mv_flag”.
  When this flag is true, all vectors use integer-pel resolution
  When this flag is false, all vectors use quarter-pel resolution
  If current picture is the only reference picture, use_integer_mv_flag is inferred or enforced to be true

## Slide 4: Current Spec (SCM4)
When predFlagLX is equal to 1 and the picture with index refIdx from reference picture list LX of the slice is not the current picture, the luma motion vector mvLX is derived as follows:
  uLX[ 0 ] = ( mvpLX[ 0 ] + mvdLX[ 0 ] + 216 ) % 216 (8‑75)
  mvLX[ 0 ] = ( uLX[ 0 ] >= 215 ) ? ( uLX[ 0 ] − 216 ) : uLX[ 0 ] (8‑76)
  uLX[ 1 ] = ( mvpLX[ 1 ] + mvdLX[ 1 ] + 216 ) % 216 (8‑77)
  mvLX[ 1 ] = ( uLX[ 1 ] >= 215 ) ? ( uLX[ 1 ] − 216 ) : uLX[ 1 ] (8‑78)
When predFlagLX is equal to 1 and the reference picture is the current picture, the luma motion vector mvLX is derived as follows:
  uLX[ 0 ] = ( ( ( mvpLX[ 0 ] >> 2 ) + mvdLX[ 0 ] ) << 2 + 216 ) % 216 (8‑xx)
  mvLX[ 0 ] = ( uLX[ 0 ] >= 215 ) ? ( uLX[ 0 ] − 216 ) : uLX[ 0 ] (8‑xx)
  uLX[ 1 ] = ( ( mvpLX[ 0 ] >> 2 ) + mvdLX[ 0 ] ) << 2 + 216 ) % 216 (8‑xx)
  mvLX[ 1 ] = ( uLX[ 1 ] >= 215 ) ? ( uLX[ 1 ] − 216 ) : uLX[ 1 ] (8-xx)

## Slide 5: Proposed method
When predFlagLX is equal to 1 and the picture with index refIdx from reference picture list LX of the slice is not the current picture, the luma motion vector mvLX is derived as follows:
  uLX[ 0 ] = ( mvpLX[ 0 ] + mvdLX[ 0 ] + 216 ) % 216 (8‑75)
  mvLX[ 0 ] = ( uLX[ 0 ] >= 215 ) ? ( uLX[ 0 ] − 216 ) : uLX[ 0 ] (8‑76)
  uLX[ 1 ] = ( mvpLX[ 1 ] + mvdLX[ 1 ] + 216 ) % 216 (8‑77)
  mvLX[ 1 ] = ( uLX[ 1 ] >= 215 ) ? ( uLX[ 1 ] − 216 ) : uLX[ 1 ] (8‑78)
When predFlagLX is equal to 1 and the reference picture is the current picture, the luma motion vector mvLX is derived as follows:
  uLX[ 0 ] = ( ( ( mvpLX[ 0 ] >> 2 ) + mvdLX[ 0 ] ) << 2 + 216 ) % 216 (8‑xx)
  mvLX[ 0 ] = ( uLX[ 0 ] >= 215 ) ? ( uLX[ 0 ] − 216 ) : uLX[ 0 ] (8‑xx)
  uLX[ 1 ] = ( ( mvpLX[ 0 ] >> 2 ) + mvdLX[ 0 ] ) << 2 + 216 ) % 216 (8‑xx)
  mvLX[ 1 ] = ( uLX[ 1 ] >= 215 ) ? ( uLX[ 1 ] − 216 ) : uLX[ 1 ] (8-xx)

## Slide 6: Simulation results
M.1: if current picture is the only reference picture, infer “use_integer_mv_flag” to be 1 (runtime not accurate)
M.2: if current picture is the only reference picture, always signal “use_integer_mv_flag” to be 1

## Slide 7: Conclusion
This proposal provides a solution to unify the adaptive MV resolution process for all vectors
  Indicated by “use_integer_mv_flag”
This unification simplified the spec (and decoding process)
  Align with HEVC v1
It is recommended to include this unification in the next version spec.
We thank Intel for cross-checking