## Slide 1: On chroma motion vector derivation for intra block copy
Xiaozhong Xu, Shan Liu and Shawmin Lei
JCTVC-U0077

## Slide 2: Proposal Summary
BV is a motion vector pointing to current reference picture
MV is a motion vector pointing to other reference picture
A difference in the chroma MV and BV derivation
  Vector pointing to temporal reference can point to fractional positions; vector pointing to current picture is clipped to be integer
  The chroma BV derivation is different from chroma MV, to keep chroma BV as integer
It is proposed unify the BV chroma vector derivation to MV in HEVC

## Slide 3: Introduction (1)
One small issue when IBC is unified with HEVC inter coding
  In HEVC, for non-4:4:4 formats, chroma motion vector could be fractional even luma moiton vector is integer
  The chroma vector derivation for IBC is different from that for HEVC inter
    If the picture with index refIdx from reference picture list LX of the slice is not the current picture,
      mvCLX[ 0 ] = mvLX[ 0 ] * 2 / SubWidthC
      mvCLX[ 1 ] = mvLX[ 1 ] * 2 / SubHeightC
    Otherwise,
      mvCLX[ 0 ] = ( ( mvLX[ 0 ] >> ( 1 + SubWidthC ) ) * 8
      mvCLX[ 1 ] = ( ( mvLX[ 1 ] >> ( 1 + SubHeightC ) ) * 8

## Slide 4: Introduction (2)
Propose to unify the chroma vector derivation for IBC to that for HEVC inter
Issue to be resolved
  When luma block vector is an odd integer, in non-4:4:4 formats, the chroma BV may be in fractional-pel position
  At the reference area boundary, the supporting neighbour pixels for interpolation may not be available

## Slide 5: Proposed method A
Encoder constraint in non-4:4:4 formats for IBC search area
  Constrain extra 2 luma lines for chroma interpolation
  A1: apply to all BVs
  A2: apply to fractional BVs
Unavailable for IBC reference
Available for IBC reference
Current block

## Slide 6: Proposed method B
Padding some pixel values for unavailable pixels near boundary
  B1: extending boundary pixels
  B2: Padding with constant value
    1<<(BitDepthc- 1)
Sub-pel to be interpolated
Window of nearby integer pixels needed for interpolation
Horizontal padding from right most column
Vertical padding from bottom most row
Available integer pixels from reference block
Padded integer pixels from available pixels
Available reference area

## Slide 7: Simulation results (method A)
Encoder constraints (with chroma interpolation)
  Apply to all BVs (A.1)
  Apply to BVs only when derived chroma BV is fractional (A.2)

## Slide 8: Simulation results (method B)
Padding unavailable pixels for interpolation
  Padding with extending boundary pixels (B.1)
  Padding with extending pixels at picture boundary and constant value (128) inside picture (B.2)

## Slide 9: Conclusion
It is proposed in this contribution that
  Chroma BV derivation for IBC is unified with that for HEVC inter
Two solutions are provided:
  Extra encoder constraints (2.8/1.6/0.9% gain for TGM)
  Padding unavailable pixels (3.2/1.9/1.0% gain for TGM)
In addition to further unification of IBC and HEVC inter, some coding gain is observed for non-4:4:4 formats