## Slide 1: JCTVC-U0081 : On unification of adaptive motion vector resolution
Presenter : Krishna Rapaka

## Slide 2: Motivation
There are two cases when integer MV is used
  IntraBC mode
  inter mode with use_integer_mv_flag equal to 1.
For these cases, we have the following different design approaches
  MV left shifted by 2 for motion compensation when use_integer_mv_flag is equal to 1.
  Rounding of AMVP predictor for IntraBC mode.
  Different MV storage accuracy, which has impact on TMVP accuracy and deblocking threshold when use_integer_mv_flag is equal 1. During the deblocking process, MV is compared against the threshold in quarter luma samples.
  Clipping of integer MV to guarantee the HEVC MV range when use_integer_mv_flag is equal 1, and wrap-around of MV for IntraBC mode

## Slide 3: AMVR unification methods
Method 2.1.1
When use_integer_mv_flag is equal to 1, use IntraBC MV derivation process and MV storage accuracy for inter mode. That is, MV = (MVP >> 2 + MVD) << 2 and no rounding of MV (<<2) before MC.
Method 2.1.2
When use_integer_mv_flag is equal to 1, use inter MV derivation process and MV storage for IntraBC. That is BV = (MVP + BVD) and upscale BV (<< 2) at MC stage. However, it may still have inconsistent deblocking threshold and TMVP accuracy.
Method 2.1.3
Regardless of use_integer_mv_flag value, use inter MV derivation process and MV storage of use_integer_mv_flag equal to 1 for IntraBC. That is BV = (MVP + BVD) and upscale BV (<< 2) at MC stage. However, it may still have inconsistent deblocking threshold and TMVP accuracy.

## Slide 4
SCM Method | Method 1 | Method 2 | Method 3
For AMVR = 0, BV=(P>>2+BVD) << 2 MV= (P + MVD) Storage : BV = Q, MV = Q Shift for MC : None for BV None for MV | For AMVR = 0, BV=(P>>2+BVD) << 2 MV=(P + MVD) Storage : BV = Q, MV = Q Shift for MC : None for BV None for MV | For AMVR = 0, BV=(P>>2+BVD) <<2 MV = (P + MVD) Storage : BV = Q, MV = Q Shift for MC : None for BV None for MV | For AMVR = 0, BV = (P + BVD) MV = (P + MVD) Storage : BV = Int, MV = Q Shift for MC : <<2 for BV None for MV
For AMVR = 1, BV=(P>>2+BVD)<< 2 MV = (P + MVD) Storage : BV = Q, MV = Int Shift for MC : None for BV <<2 for MV | For AMVR = 1, BV=(P>>2+BVD)<< 2 MV=(P>>2+MVD)<<2 Storage : BV = Q, MV = Q Shift for MC : None for BV None for MV | For AMVR = 1, BV = (P + BVD) MV = (P + MVD) Storage : BV = Int, MV = Int Shift for MC : <<2 for BV <<2 for MV | For AMVR = 1, BV = (P+ BVD) MV = (P+MVD) Storage : BV = Int, MV = Int Shift for MC : <<2 for BV <<2 for MV
Summary of Test Methods

## Slide 5: Results of AMVR Test methods
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 99% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.1% | 0.1%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
99% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.1% | 0.1% | 0.1%
-0.1% | 0.1% | -0.1%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.1% | 0.2% | 0.2%
0.1% | 0.1% | 0.2%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
99% |  | 
Results of Test 2.1.1
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
100% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | -0.2% | 0.1%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
100% |  | 
100% |  | 
Results of Test 2.1.2

## Slide 6: Results of Test 2.1.3
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% |  | 
Dec Time[%] | 100% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | -0.1%
0.0% | 0.0% | 0.1%
0.0% | 0.0% | 0.0%
100% |  | 
100% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | -0.1% | 0.1%
0.0% | -0.1% | 0.1%
0.0% | 0.1% | 0.0%
0.0% | 0.0% | 0.1%
100% |  | 
100% |  | 

## Slide 7: Inconsistent MV accuracy for deblocking
In the current WD, MV storage accuracy is different for
  Inter mode with use_integer_mv_flag equal to 1 compared to
  IBC mode and inter mode with use_integer_mv_flag equal to 0.
However, in the de-blocking process MVs are compared against the threshold which is represented in quarter luma samples.
It is proposed to upscale (<<2) MV for inter mode when use_integer_mv_flag is equal 1 for the de-blocking process to match the specification text.

## Slide 8: Results of Test 2.2
 | All Intra |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0%
Enc Time[%] | 99% |  | 
Dec Time[%] | 97% |  | 
Random Access |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
99% |  | 
96% |  | 
Low delay B |  | 
G/Y | B/U | R/V
0.0% | 0.0% | 0.0%
0.0% | 0.1% | 0.1%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.1%
0.0% | -0.3% | 0.0%
0.0% | 0.0% | 0.0%
0.0% | 0.0% | 0.0%
98% |  | 
95% |  | 

## Slide 9: MV accuracy for inter mode with use_integer_mv_flag equal to 1
In the current WD, the luma and chroma MVs are scaled (<<2) and clipped just before motion compensation when use_integer_mv_flag is equal to 1 as below
  mvLX = Clip3( − 215, 215 − 1, mvLX << 2 )
  mvCLX = Clip3( − 215, 215 − 1, mvCLX << 2 )
It is asserted that the scaled motion vectors (luma and chroma) when they are clipped to 215 – 1 result in requiring interpolation. The interpolation is not required for any other cases when use_integer_mv_flag is equal to 1. This special case would add unnecessary complexity for the decoder which it would not have to do otherwise.
When use_integer_mv_flag is equal to 1 and the reference index refIdxLX is not equal to currPic, mvLX and mvCLX (where X equals to 0 or 1) are modified as follows:
  mvLX = Clip3( − 215, 215 – 4, mvLX << 2 )
  mvCLX = Clip3( − 215, 215 − 4, mvCLX << 2 )