## Slide 1: JCTVC-U0095 Non-CE: Encoder modification for intra prediction mode using adaptive colour transform
Yao-Jen Chang, Chun-Lung Lin, Jih-Sheng Tu and Ching-Chieh Lin
Warsaw, Poland
June, 2015
Notes: <number>

## Slide 2: Adaptive colour transform (ACT)
<number>
HEVC-SCC adopts ACT to convert one color-space to another one wherein the correlations among three color components are further reduced, and thus improve the coding efficiency.
Notes: <number>

## Slide 3: Intra prediction using ACT
<number>
ACT can be adaptively enabled/disabled in intra prediction mode, inter prediction mode, intra block copy mode
To evaluate whether to enable the ACT, the intra prediction mode requires to run the process twice for evaluation
  It increases the complexity for evaluation of ACT
Intra
prediction
mode
ACT
CCP,
Transform &
Quantization
Entropy
coder
Notes: <number>

## Slide 4: Ideas for speed-up
<number>
Idea 1: Can the evaluation for the ACT-enabled intra prediction mode be skipped?
Idea 2: Can the evaluation for the sizes of transform unit (TU) be skipped?
  Block size for TU in HEVC can be 32x32, 16x16, 8x8 or 4x4. Evaluation for selecting the best TU size out of 4 block sizes is very time-consuming.
  This idea wants to use the default size for TU block
Intra
prediction
mode
ACT
CCP,
Transform &
Quantization
Entropy
coder
Notes: <number>

## Slide 5: The proposed modification
<number>
Modification 1: If the video is YUV colour space and CU size is 64x64, then skip the ACT-enabled intra prediction
  YUV colour space has no significant correlation among three color components.
  A large CU coded by intra prediction mode usually implies the content in the area is not complex
Modification 2: If the CU size is large enough (≥ NxN, N is set as 32 or 16), then skip the evaluation for smaller sizes of TU in the ACT-enabled intra prediction
  With the help of ACT, the resulting residues in the transform domain may be concentrated into a smaller number of values.
  A large CU coded by intra prediction mode usually implies the content in the area is not complex
Notes: <number>

## Slide 6: Results of AI Lossy, 444, FF-IBC search
<number>
On top of the SCM4.0 CTC
Test 1: Modifications 1 & 2, TU evaluation disabled in CU ≥ NxN = 32x32
Test 2: Modifications 1 & 2, TU evaluation disabled in CU ≥ NxN = 16x16
AI, Lossy | Test 1 |  |  | Test 2 |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.1% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.1%
YUV, text & graphics with motion, 1080p & 720p | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.0% | 0.1% | 0.1% | 0.0% | 0.2% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 95% |  |  | 92% |  | 
Dec Time[%] | 100% |  |  | 100% |  | 
Thank Microsoft (MSRA) for crosscheck!
Notes: <number>

## Slide 7: Results of AI Lossy, 444, FF-IBC search, N = 32
<number>
On top of the SCM4.0 CTC
Modification 2: skipping evaluation of TU sizes only when ACT enabled
Modification 3: skipping evaluation of TU sizes no matter whether ACT is enabled
AI, Lossy | Modification 2 |  |  | Encoding time [%] | Modification 3 |  |  | Encoding time [%]
Skipping evaluation of TU splitting when CU ≥ 32x32 | G/Y | B/U | R/V |  | G/Y | B/U | R/V | 
RGB, TGM, 1080p & 720p | -0.1% | 0.0% | -0.1% | 96% | -0.1% | 0.0% | -0.1% | 95%
RGB, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 96% | 0.0% | 0.0% | 0.0% | 96%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 97% | n/a% | n/a% | n/a% | n/a%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 96% | 0.0% | 0.0% | 0.0% | 96%
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.1% | 95% | 0.0% | -0.2% | 0.0% | 94%
YUV, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 95% | 0.0% | 0.0% | 0.1% | 94%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 96% | n/a% | n/a% | n/a% | n/a%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 94% | 0.1% | 0.0% | 0.0% | 93%
Notes: <number>

## Slide 8: Results of AI Lossy, 420, FF-IBC search, N = 32
<number>
On top of the SCM4.0 CTC
Modification 2: skipping evaluation of TU sizes only when ACT enabled
Modification 3: skipping evaluation of TU sizes no matter whether ACT is enabled
AI, Lossy | Modification 2 |  |  | Encoding time [%] | Modification 3 |  |  | Encoding time [%]
Skipping evaluation of TU splitting when CU ≥ 32x32 | G/Y | B/U | R/V |  | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 100% | 0.0% | 0.0% | 0.0% | 97%
YUV, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 100% | 0.0% | -0.1% | 0.0% | 98%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 100% | 0.0% | 0.0% | 0.1% | 98%
Notes: <number>

## Slide 9: Results of AI Lossy, 444, FF-IBC search
<number>
On top of the SCM4.0 CTC
Modification 2: skipping evaluation of TU sizes with ACT enabled
AI, Lossy | Modification 2 when CU ≥ 32x32 |  |  | Encoding time [%] | Modification 2 when CU ≥ 16x16 |  |  | Encoding time [%]
 | G/Y | B/U | R/V |  | G/Y | B/U | R/V | 
RGB, TGM, 1080p & 720p | -0.1% | 0.0% | -0.1% | 96% | 0.0% | 0.0% | 0.0% | 94%
RGB, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 96% | 0.1% | 0.1% | 0.1% | 94%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 97% | 0.1% | 0.1% | 0.1% | 94%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 96% | 0.1% | 0.0% | 0.1% | 93%
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.1% | 95% | 0.0% | 0.0% | 0.0% | 92%
YUV, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 95% | 0.0% | 0.0% | 0.0% | 92%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 96% | 0.0% | 0.2% | 0.1% | 92%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 94% | 0.0% | 0.0% | 0.0% | 90%
Enc Time[%] | 96% |  |  |  | 93% |  |  | 
Dec Time[%] | 100% |  |  |  | 100% |  |  | 
Notes: <number>

## Slide 10: Conclusion
<number>
Skipping checking of small TU sizes
  ACT-enabled (Modification 2)
  No matter whether ACT is enabled (Modification 3)
Modification 2:
  3~5% improvement on encoding time with 0.1% coding gain
  Disabling when CU ≥ 16 can get 3% additional speed-up than one when CU ≥ 32
Modification 3:
  1~3% additional improvement on encoding time compared to Modification 2
  +0.1~-0.1% coding change compared to SCM4.0
Notes: <number>

## Slide 11: Thank you!
<number>