## Slide 1
<number>
Non-CE1: Enhancement to Palette Coding by Palette with Pixel Copy (PPC) Coding
JCTVC-U0116
19 June – 26 June 2015
Tao Lin
Tongji University
Notes: <number>

## Slide 2
Motivation
Full frame search of either IBC or ISC is not feasible
  During search, all reference pixels have to be in SRAM
  Practically, common maximum search range is 4CTU
  In 4CTU case, half of IBC gain is lost (see JCTVC-U0172)
  A solution of good performance in 4CTU is desperately needed for broader acceptance of HEVC in real world SCC applications
Extending palette coding to neighbor is a natural solution
  Copying pixel out of CU is necessary
  Simply copying pixel in traditional palette mode may break effective “index redundancy removal” mechanism
  Adding another palette mode, specially focusing on pixel copy
  Palette with Pixel Copy (PPC) is such a solution

## Slide 3
A PPC sub-mode is added under traditional palette mode
  Traditional palette mode becomes a sub-mode in parallel with the added PPC sub-mode
  In PPC, a string is either a palette color string or a pixel string
  For a palette color string, an index and a run are coded
  For a pixel string, an offset and a length are coded
  A palette color string is always a LEFT copy string
  An unmatched pixel is coded using max palette index+1
  Search range of pixel string is current CTU + a few left CTUs
  No residual is coded
This Proposal

## Slide 4
Palette with Pixel Copy
CABAC throughput
Prediction Mode | PPC | 
(Note: CU Size = 8x8) | Syntax Elements | Number
Mode Flag | cu_transquant_bypass_flag | 1
 | cu_skip_flag | 1
 | palette_mode_flag | 1
 | ppc_submode_flag ppc_scan_mode_flag | 1 1
 | ppc_palette_color_present_flag | 1
 | ppc_unmatched_pixel_present_flag | 1
Partition |  | 
MV or BV | ppc_pixel_string_flag | 64
 | ppc_above_string_flag | 64
 | ppc_offsetX_zero_flag | 64
 | Ppc_offsetY_zero_flag | 64
 | ppc_length_minus1_prefix | 64
Residual (4 4x4 TBs, 3 Color Components) | N/A | 
Number of Context-coded Bins |  | 327
Bins per Pixel |  | 5.11

## Slide 5
Palette with Pixel Copy
Syntax elements
sps_scc_extension( ) { | Descriptor
curr_pic_as_ref_enabled_flag | u(1)
palette_mode_enabled_flag | u(1)
if( palette_mode_enabled_flag ) { | 
palette_max_size | ue(v)
delta_palette_max_predictor_size | ue(v)
ppc_reference_range_left_ctus | u(2)
} | 
motion_vector_resolution_control_idc | u(2)
intra_boundary_filtering_disabled_flag | u(1)
} | 

## Slide 6
Palette with Pixel Copy
Syntax elements
palette_coding(x0, y0, nCbS) { | Descriptor
ppc_submode_flag | ae(v)
if(ppc_submode_flag) | 
ppc_palette_color_present_flag | ae(v)
if(ppc_palette_color_present_flag ¦ ¦ ! ppc_submode_flag){ | 
palettePredictionFinished = 0 | 
………………………………………………… | 
palette_entry | 
} | 
if(ppc_submode_flag){ | 
ppc_coding(x0, y0, nCbS ) | 
} else{ | 
if( CurrentPaletteSize != 0 ) | 
…… | 
} | 
} | 

## Slide 7
PPC syntax elements
Syntax elements
ppc_coding ( x0, y0, nCbS ) { | Descriptor
ppc_unmatched_pixel_present_flag | ae(v)
ppc_scan_mode_flag | ae(v)
ppcIndexMax = 0 | 
ppcIndexPrev = 0 | 
while(ppcScanPos < nCbS * nCbS ) { | 
if(ppc_palette_color_present_flag ¦ ¦ ppc_unmatched_pixel_present_flag) | 
ppc_pixel_string_flag | ae(v)
if(ppc_pixel_string_flag){ | 
ppc_length_minus1 | ae(v)
ppc_above_string_flag | ae(v)
if(!ppc_above_string_flag){ | 
ppc_offsetY_zero_flag | ae(v)
if(ppc_offsetY_zero_flag){ | 
if(!ppc_scan_mode_flag && 1 == (travScan[pcScanPos][1] & 0x1) ¦ ¦ | 
ppc_scan_mode_flag ) | 
ppc_offsetX_sign | u(1)

## Slide 8
Syntax elements
if(!ppc_palette_color_present_flag){ | 
xR = travScan[ppcScanPos][0] | 
yR = travScan[ppcScanPos][1] | 
ppcParaFlag [xR][yR] = 0 | 
for( cIdx = 0; cIdx < numComps; cIdx++ ){ | 
ppc_unmatched_pixel_val | ae(v)
ppcParaVal [cIdx] [xR][yR] = ppc_unmatched_pixel_val | 
} | 
ppcCopyTypePrev = COPY_NONE | 
ppcScanPos++ | 
ppcIndexPrev = 0 | 
} | 
PPC syntax elements

## Slide 9
Syntax elements
else{ | 
if(ppcScanPos && ppcCopyTypePrev== COPY_LEFT) | 
ppcIndexMax-- | 
if(ppcIndexMax >1) | 
ppc_index_adjusted | ae(v)
if(ppcScanPos && ppcCopyTypePrev== COPY_LEFT) | 
ppcIndexMax++ | 
if( ppc_unmatched_pixel_present_flag&& ((ppcIndexCurrMax <CurrentPaletteSize && ppcIndex==(ppcIndexCurrMax+1)) ¦ ¦ (ppcIndex==CurrentPaletteSize)) ){ | 
xR = travScan[ppcScanPos][0] | 
yR = travScan[ppcScanPos][1] | 
ppcParaFlag [xR][yR] = 0 | 
for( cIdx = 0; cIdx < numComps; cIdx++ ){ | 
ppc_unmatched_pixel_val | ae(v)
ppcParaVal [cIdx] [xR][yR] = ppc_unmatched_pixel_val | 
} | 
ppcCopyTypePrev = COPY_NONE | 
ppcScanPos++ | 
ppcIndexPrev = 0 | 
} else{ | 
PPC syntax elements

## Slide 10
Syntax elements
PPC syntax elements
maxPPCRun = nCbS * nCbS –ppcScanPos– 1 | 
if( maxPPCRun > 0 ) { | 
palette_run_msb_id_plus1 | ae(v)
if( palette_run_msb_id_plus1 > 1 ) | 
palette_run_refinement_bits | ae(v)
} | 
……………………………………………………………………………………………………….. | 
indexCopyPos = 0 | 
while (indexCopyPos <= paletteRun) { | 
xR = travScan[ppcScanPos][0] | 
yR = travScan[ppcScanPos][1] | 
ppcParaFlag [xR][yR] = 0 | 
for( cIdx = 0; cIdx < numComps; cIdx++ ) | 
ppcParaVal [cIdx] [xR][yR] = CurrentPaletteEntries[cIdx][ ppcIndex] | 
indexCopyPos ++ | 
ppcScanPos ++ | 
} | 
ppcIndexPrev = ppcIndex | 
CopyTypePrev = COPY_LEFT | 

## Slide 11
<number>
Experiments
anchor: SCM40 CTC, 2 test conditions of reference range
 | IBC | PPC
Test condition 1 | Full-frame | 1x2-CTU
Test condition 2 | 1x4-CTU | 1x4-CTU

## Slide 12
<number>
Experiments
TC1: FF IBC vs 2CTU PPC, lossy
Anchor_Tested1 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, TGM, 1080p & 720p | -3.8% | -4.1% | -4.1% | -2.5% | -2.7% | -2.7% | -2.0% | -2.0% | -1.9%
RGB, MC, 1440p & 1080p | -1.2% | -1.7% | -1.7% | -0.7% | -1.0% | -1.1% | 0.1% | -0.7% | -0.6%
RGB, Ani, 720p | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | -0.1% | 0.1% | 0.1%
RGB, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | -4.2% | -4.1% | -4.1% | -2.4% | -2.3% | -2.5% | -1.6% | -1.7% | -1.8%
YUV, MC, 1440p & 1080p | -1.5% | -2.0% | -2.3% | -0.9% | -1.4% | -1.9% | -0.3% | -1.2% | -1.6%
YUV, Ani, 720p | 0.0% | 0.0% | -0.1% | -0.1% | -0.3% | 0.1% | 0.0% | 0.2% | 0.0%
YUV, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1% | -0.1% | 0.0% | 0.1%
Enc Time[%] | 105% |  |  | 106% |  |  | 103% |  | 
Dec Time[%] | 99% |  |  | 102% |  |  | 103% |  | 
Encoding time ratio is quite accurate and reliable
Two cross-checkers (Huawei and NCTU) report almost the same numbers

## Slide 13
<number>
Experiments
TC1: 4CTU IBC and 4CTU PPC, lossy
Anchor_Tested1 | All Intra |  |  | Random Access |  |  | Low delay B |  | 
 | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, TGM, 1080p & 720p | -7.4% | -8.0% | -7.9% | -5.1% | -5.4% | -5.3% | -3.1% | -3.3% | -3.3%
RGB, MC, 1440p & 1080p | -2.4% | -3.2% | -3.2% | -1.2% | -1.9% | -1.9% | -0.4% | -1.2% | -1.1%
RGB, Ani, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | -0.1%
RGB, CC, 1080p | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | -7.7% | -7.7% | -7.9% | -5.0% | -4.9% | -5.0% | -2.6% | -2.5% | -2.8%
YUV, MC, 1440p & 1080p | -3.2% | -4.1% | -4.3% | -1.8% | -2.2% | -2.7% | -0.6% | -1.3% | -1.7%
YUV, Ani, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.1% | 0.0% | 0.0% | 0.2%
YUV, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
Enc Time[%] | 106% |  |  | 104% |  |  | 100% |  | 
Dec Time[%] | 98% |  |  | 101% |  |  | 100% |  | 

## Slide 14
<number>
Experiments
TC1: FF IBC and 2CTU PPC, lossless
Anchors_Tested1 | All Intra |  |  |  | Random Access |  |  |  | Low Delay B |  |  | 
 | Bit-rate change (Total) | Bit-rate change (Avg) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Avg) | Bit-rate change (Min) | Bit-rate change (Max) | Bit-rate change (Total) | Bit-rate change (Avg) | Bit-rate change (Min) | Bit-rate change (Max)
RGB, TGM, 1080p & 720p | -4.8% | -5.6% | -14.9% | -0.9% | -2.8% | -3.5% | -10.2% | -0.4% | -2.6% | -2.8% | -6.6% | -0.2%
RGB, MC, 1440p & 1080p | -0.8% | -0.9% | -1.6% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
RGB, A, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | -5.2% | -6.0% | -15.4% | -1.0% | -2.8% | -3.9% | -10.5% | -0.3% | -2.6% | -3.1% | -7.5% | -0.2%
YUV, MC, 1440p & 1080p | -0.9% | -1.0% | -1.7% | -0.2% | -0.1% | -0.1% | -0.2% | -0.1% | -0.1% | -0.1% | -0.1% | -0.1%
YUV, A, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, CC, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 118% |  |  |  | 106% |  |  |  | 104% |  |  | 
Dec Time[%] | 100% |  |  |  | 103% |  |  |  | 102% |  |  | 

## Slide 15
<number>
This Proposal
Does PPC decoder have memory bandwidth problem?
  No at all
  The entire reference pixel range is in SRAM
  The worst case SRAM BW and throughput is 1.25cycles/pixel
  1.25cycles/pixel is way below any decoder does due to many other restrictions in a decoder, e.g. cabac
  Inter pred. mode seems have more than 7 bins per pixels
  Practically, the best a decoder can do is 3-4 bins per cycles
  MC, Inv-trans/Dequan, etc. also need at least 1.5cycles/pixel
U0171 provides a PPC HW decoder reference design
  System clock is 330MHz for 4K decoding (249Mpixels/sec)
A few questions one may ask on PPC decoder

## Slide 16
<number>
This Proposal
Does PPC have extra SRAM cost?
  No at all
  IBC also needs the same reference pixel SRAM to reduce DDR bandwidth and power consumption
  Why? 4CTU SRAM (4x64x64x24=384 kbits) has a silicon area of 0.08217mm2 at 28nm high performance CMOS IC process
  At $3000 per 12 inch wafer and 80% utilization, the cost of one mm2 silicon area is 0.05142 US$.
  4CTU SRAM costs 0.004225 US$ = 0.4225 US penny
  A typical 4K decoder has 2Million gates = 35 mm2 silicon area and costs 1.8 US$
  4CTU is 0.23% of a decoder, and really negligible
  One 4K FF is 2025CTU, FF SARM will cost 2.14 US$
A few questions one may ask on PPC decoder

## Slide 17
<number>
This Proposal
Is PPC decoder complicated and hard to design
  Not at all
  JCTVC-U0171 provides a PPC decoder reference design
  The major module is Address Generator to copy pixels from one location of SRAM to another location of SRAM
  Total PPC decoder gate count is 6.2K.
  This is 0.31% of a 4K decoder
  Less than one thousand lines of verilog code
  It takes one man-week to complete the design
  This is probably the simplest module in HEVC decoder
A few questions one may ask on PPC decoder

## Slide 18
<number>
This Proposal
What is the challenge to design a PPC encoder
  To design any high-performance and commercially competitive HEVC encoder is always extremely challenging
  But designing a 4K high performance PPC encoder is feasible
  The most challenging part is String Search Engine
  The most critical bottleneck is pixel read bandwidth
  Fortunately, these are all common design challenges
  There are plenty of solutions to deal with them
  A String Search Engine Architecture Ref. Design will be done
  PPC encoder is estimated to be 2-3% of entire HEVC encoder
  Hopefully we will be able to submit a document about it in the next few days if people are really interested in it and PPC
A few questions one may ask on PPC encoder

## Slide 19
<number>
Conclusions
PPC is a natural extension of palette coding to bring back some of the big loss due to the infeasibility of FF IBC real-time encoder
BD-rate reduction is 4.2% in FF IBC vs 2CTU PPC case
BD-rate reduction is close to 8% in both 4CTU case
PPC decoder has no memory bandwidth issue
PPC decoder is simple and costs 0.31% of a 4K decoder
PPC decoder design can be done with very little effort
PPC encoder is doable and costs 2-3% of a 4K encoder
Strongly recommend to adopt U0116 and PPC. It is really a no-brainer
Notes: <number>

## Slide 20
<number>
THANK Huawei and NCTU for cross-checking
Notes: <number>

## Slide 21
<number>
THANK YOU
Notes: <number>