## Slide 1: JCTVC-U0118 On intra block copy bitstream constraints
V. Seregin, K. Rapaka, R. Joshi, M. Karczewicz, Y.-K. Wang

## Slide 2: 1. Collocated picture constraint
Current picture shall not be used as a collocated picture:
  It is a requirement of bitstream conformance that the picture referred to by collocated_ref_idx shall be the same for all slices of a coded picture and shall not be the current picture itself.
It is proposed to exclude current picture from being addressed by collocated_ref_idx with the following steps:
  Count the number NumCurrRef0 of reference pictures equal to the current picture
  If num_ref_idx_l0_active_minus1 − NumCurrRef0 > 0 signal collocated_ref_idx
  Exclude current picture from the range of possible collocated reference indices

## Slide 3: 2. RPLM signalling modification (1)
If IBC SPS flag is equal to 1, the following constraints is applied:
  It is a requirement of bistream conformance that when nal_unit_type has a value in the range of BLA_W_LP to RSV_IRAP_VCL23, inclusive (i.e. the picture is an IRAP picture) and curr_pic_as_ref_enabled_flag is equal to 1, RefPicList0 shall contain one or more entries that refer to the current picture only.
To satisfy this constraint, RPLM shall be signalled is some cases to put the current picture into the reference picture list

## Slide 4: 2. RPLM signalling modification (2)
However, when only one picture is used in the slice, RPLM signaling is redundant and current picture can be inferred being included into the reference picture list, and the following is proposed:
for( rIdx = 0; rIdx <= num_ref_idx_l0_active_minus1; rIdx++) { (8‑9) rIdxTemp = ( num_ref_idx_l0_active_minus1 = = 0 && curr_pic_as_ref_enabled_flag ) ? NumPicTotalCurr – 1 : rIdx RefPicList0[ rIdx ] = ref_pic_list_modification_flag_l0 ? RefPicListTemp0[ list_entry_l0[ rIdx ] ] : RefPicListTemp0[ rIdxTemp ]
}
ref_pic_lists_modification( ) { | Descriptor
if( num_ref_idx_l0_active_minus1 > 0 ¦ ¦ !curr_pic_as_ref_enabled_flag ) | 
ref_pic_list_modification_flag_l0 | u(1)
if( ref_pic_list_modification_flag_l0 ) | 
for( i = 0; i <= num_ref_idx_l0_active_minus1; i++ ) | 
list_entry_l0[ i ] | u(v)
if( slice_type = = B ) { | 
ref_pic_list_modification_flag_l1 | u(1)
if( ref_pic_list_modification_flag_l1 ) | 
for( i = 0; i <= num_ref_idx_l1_active_minus1; i++ ) | 
list_entry_l1[ i ] | u(v)
} | 
} | 

## Slide 5: 3. IBC predictor constraint
In the current IBC design, IBC predictor is constrained to be within the picture, this restrictions makes it different from the inter mode:
  In the clause 6.4.1, if one or more of the following conditions are true, minBlockAddrN is set equal to −1:
    xNbY is less than 0
    yNbY is less than 0
    xNbY is greater than or equal to pic_width_in_luma_samples
    yNbY is greater than or equal to pic_height_in_luma_samples
It is proposed to remove predictor constraint for IBC, which will be aligned with inter mode

## Slide 6: 4. IBC search range constraints (1)
In the current WD, IBC search range is constrained as follows:
  IBC predictor shall be located inside the current picture, and shall belong to the same tile and slice as the current block
  IBC predictor cannot overlap with the current CU
  IBC predictor shall follow WPP boundaries
To avoid bitstream restrictions which potentially can be broken by some encoders, it is proposed to clip the IBC predictor to the valid IBC area in the decoder when the predictor is outside of that region.

## Slide 7: 4. IBC search range constraints (2)
For the predictor located outside of the valid region the following steps are performed:
  Predictor is moved into the IBC valid search area by clipping the bottom right corner of the predictor block
  If the clipped predictor is still not valid, the predictor samples are replaced with 1 << ( BitDepthY − 1 ) for luma and 1 << ( BitDepthC − 1 ) for chroma