## Slide 1: JCTVC-U0119: On slice segment freeze signalling for screen content coding
Thorsten Laude

## Slide 2
High level syntax for freezing slice segments
Goal: low complexity and efficient coding of static SC
SC often static for several seconds/minutes
Example: 1500 static pictures per minute (25 fps)
Avoid unnecessary computation for encoder and decoder
Low delay constraints: Analysis of future pictures not desired
Proposal: Analysis of already coded pictures and freeze slice segments which have been static

## Slide 3
Slice segment freeze process
Signal for a slice segment of the current picture that it will be frozen for subsequent picture(s)
Copy samples from frozen slice segment to subsequent pictures

## Slide 4
Slice segment header syntax
Binary flag slice_freeze_mode_flag
slice_segment_header( ) { | Descriptor
[…] | 
slice_freeze_mode_flag | u(1)
byte_alignment( ) | 
} | 

## Slide 5
Termination of slice segment freeze mode
Avoid analysis of future pictures (low delay)
End freeze process when a new slice segment is coded at the corresponding location
Frozen slice segments

## Slide 6
Constraints with respect to the partitioning of subsequent pictures
No partial overlap with locations of frozen slice segments
Complete coverage of remaining picture parts

## Slide 7
Conclusions
HLS signalling to freeze slice segments
Benefit: Frozen slice segments avoid unnecessary computation for encoders and decoders