## Slide 1: Range Extension Verification Test
Vittorio Baroncini
Guillaume Barroux
Chris Rosewarne

## Slide 2: Test Method
DSIS Variant I
SRC vs PVS
  SRC is uncompressed reference
  PVS is compressed by Proponents and Anchor
Professional Monitor EIZO CGW302 (2560x1600)
Set to HD resolution @ 60fps 10 bits
MUP player
21 valid viewers (out of 24)
6 girls 15 boys (pre and post screened)

## Slide 3: Test design
Four test sessions
3 dummy BTCs (Basic Test Cell) each session
SRC vs. SRC (also to check viewers consistency)
Two viewers seated at 2,5 H
Low light behind monitor
0 to 10 scoring impairment scale
Accurate viewers training focusing on the meaning of the scale and of the kind of impairment expected
Training made of 10 BTC using wide range of quality from actual test content

## Slide 4: EBUHorse (4:2:2)
Chart: Bit-rate
| 13921.19 | 8761.98 | 5707.36 | 2762.07
AVC | 7.6 | 7.2667 | 6.2667 | 6.2667
HEVC | 8 | 7.8667 | 7.6667 | 7.2667

## Slide 5: EBUKidsSoccer (4:2:2)
Chart: Bit-rate
| 15177.65 | 8713.2000000000007 | 5387.76 | 2645.91
AVC | 7.3333 | 7.1333 | 6.8667 | 4.2
HEVC | 8.5333 | 8.2667 | 7.0667 | 4.2

## Slide 6: EBUWaterRocksClose (4:2:2)
Chart: Bit-rate
| 13338.01 | 8769.24 | 5748.69 | 2997.91
AVC | 6.6667 | 4.0667 | 3 | 1.1333
HEVC | 6.4667 | 4.6 | 4.5333 | 1.4667

## Slide 7: BirdsInCage (4:4:4)
Chart: Bit-rate
| 21087.89 | 17317.23 | 11039.36 | 5741.45
AVC | 7.6 | 7.2667 | 7.1333 | 7.2
HEVC | 7.9333 | 7.8667 | 7.6 | 7.4

## Slide 8: CrowdRun (4:4:4)
Chart: Bit-rate
| 23419.15 | 18369.3 | 10232.68 | 5463.21
AVC | 7.8667 | 7.5333 | 7.4 | 7.2
HEVC | 8.4 | 7.7333 | 7.4667 | 7.1333

## Slide 9: EBULupoCandlelight (4:4:4)
Chart: Bit-rate
| 22322.81 | 18948.86 | 11051.63 | 5104.96
AVC | 7.3333 | 6.2 | 4.2 | 2
HEVC | 6.7333 | 6.2 | 4.5333 | 3.0667

## Slide 10: Acknowledgement
The authors would like to thank Canon for encoding all bit-streams for this activity.
Great appreciation is also shown toward the work of Alexis Tourapis (Apple) who helped defining the test scope but also provided great insight concerning the JM settings and the deinterlacing tools which should be used.
Finally, the authors would also like to thank Test & Write for preparing and realizing all the subjective viewing tests.