## Slide 1: JCTVC-V0037: On SCC Level Limits
Sachin Deshpande, Seung-Hwan Kim

## Slide 2
Introduction
The current HEVC Screen Content Coding draft 4 defines the calculation of MaxDpbSize in Annex A.
  Different MaxDpbSize is calculated based on PicSizeInSamplesY to take advantage of available memory capacity
  However the MaxDpbSize is not calculated based on the bit-depth or chroma format
In this contribution MaxDpbSize calculation which accounts for memory use due to bit-depth and/or chroma components is proposed for Screen-Extended Main 10 profile and Screen-Extended Main 10 4:4:4 profile.
In addition, a bug-fix is proposed to Table A.4 for Screen-Extended Main 4:4:4 and Screen-Extended Main 4:4:4 10 profiles.

## Slide 3
Proposal
The existing process for computing MaxDpbSize is extended by introducing a scaling factor (SFactor)
  SFactor accounts for bit-depth and chroma subsampling for Screen-Extended Main 10 profile and Screen-Extended Main 10 4:4:4 profile.
  The scaling factor (SFactor) is set equal to 1 for profiles other than Screen-Extended Main 10 profile and Screen-Extended Main 10 4:4:4 profile

## Slide 4
Proposed Text Changes
A.4.2 Profile-specific level limits for the video profiles
…
The variable BrNalFactor, which represents the NAL bit rate scale factor, is set equal to CpbNalFactor * HbrFactor.
The variable SFactor is defined as follows:
- If the bitstream or sub-layer representation is indicated to conform to the Screen-Extended Main 10
profile, SFactor is set equal to SFactor =((4*BitDepthY + 2*BitDepthC)  (6*10)
- Otherwise, if the bitstream or sub-layer representation is indicated to conform to the Screen-Extended
Main 10 4:4:4 profile, SFactor is set as follows:
  If chroma_format_idc is equal to 1, SFactor =((4*BitDepthY + 2*BitDepthC)  (12*10)
  If chroma_format_idc is equal to 3, SFactor =((4*BitDepthY + 8*BitDepthC)  (12*10)
- Otherwise, SFactor is set equal to 1.
The variable MinCr is set equal to MinCrBase * MinCrScaleFactor ÷ HbrFactor.
When the specified level is not level 8.5, the value of
sps_max_dec_pic_buffering_minus1[ HighestTid ] + 1 shall be less than or equal to MaxDpbSize, which
is derived as follows:
if( PicSizeInSamplesY <= ( MaxLumaPs >> 2 ) ) MaxDpbSize = Min( 4 * maxDpbPicBuf/SFactor, 16 ) else if( PicSizeInSamplesY <= ( MaxLumaPs >> 1 ) ) MaxDpbSize = Min( 2 * maxDpbPicBuf/SFactor, 16 ) (A‑1) else if( PicSizeInSamplesY <= ( ( 3 * MaxLumaPs ) >> 2 ) ) MaxDpbSize = Min( ( 4 * maxDpbPicBuf/SFactor) / 3, 16 ) else MaxDpbSize = maxDpbPicBuf/SFactor

## Slide 5
Results for MaxDpbSize from our proposal (1/3)
Table 1 - Scale Factors for various bit depth and chroma formats for Screen-Extended Main 10 profile
Profile | Chroma format | BitDepthY | BitDepthC | SFactor
Screen-Extended Main 10 | 4:2:0 | 8 | 8 | 4¸5
Screen-Extended Main 10 | 4:2:0 | 8 | 10 | 13¸15
Screen-Extended Main 10 | 4:2:0 | 10 | 10 | 1
Screen-Extended Main 10 4:4:4 | 4:2:0 | 8 | 8 | 2¸5
Screen-Extended Main 10 4:4:4 | 4:2:0 | 8 | 10 | 13¸30
Screen-Extended Main 10 4:4:4 | 4:2:0 | 10 | 10 | 1¸2
Screen-Extended Main 10 4:4:4 | 4:4:4 | 8 | 8 | 4¸5
Screen-Extended Main 10 4:4:4 | 4:4:4 | 8 | 10 | 14¸15
Screen-Extended Main 10 4:4:4 | 4:4:4 | 10 | 10 | 1

## Slide 6
Results for MaxDpbSize from our proposal (2/3)
Table 2- MaxDpbSize for various Scale Factors when sps_curr_pic_ref_enabled_flag=0
PicSizeInSamplesY | SFactor=1 (HEVC SCC Draft 4) | SFactor=4¸5 | SFactor=13¸15 | SFactor=2¸5 | SFactor=13¸30 | SFactor=14¸15 | SFactor=1¸2
PicSizeInSamplesY ≤ (MaxLumaPS>>2) | 16 | 16 | 16 | 16 | 16 | 16 | 16
(MaxLumaPS>>2) < PicSizeInSamplesY ≤ (MaxLumaPS>>1) | 12 | 15 | 13 | 16 | 16 | 12 | 16
(MaxLumaPS>>1) < PicSizeInSamplesY ≤ ((3*MaxLumaPS)>>2) | 8 | 10 | 9 | 16 | 16 | 8 | 16
((3*MaxLumaPS)>>2) < PicSizeInSamplesY ≤ 1.0 * MaxLumaPS | 6 | 7 | 6 | 15 | 13 | 6 | 12

## Slide 7
Results for MaxDpbSize from our proposal (3/3)
Table 3- MaxDpbSize for various Scale Factors when sps_curr_pic_ref_enabled_flag!=0
PicSizeInSamplesY | SFactor=1 (HEVC SCC Draft 4) | SFactor=4¸5 | SFactor=13¸15 | SFactor=2¸5 | SFactor=13¸30 | SFactor=14¸15 | SFactor=1¸2
PicSizeInSamplesY ≤ (MaxLumaPS>>2) | 16 | 16 | 16 | 16 | 16 | 16 | 16
(MaxLumaPS>>2) < PicSizeInSamplesY ≤ (MaxLumaPS>>1) | 12 | 16 | 16 | 16 | 16 | 15 | 16
(MaxLumaPS>>1) < PicSizeInSamplesY ≤ ((3*MaxLumaPS)>>2) | 8 | 11 | 10 | 16 | 16 | 10 | 16
((3*MaxLumaPS)>>2) < PicSizeInSamplesY ≤ 1.0 * MaxLumaPS | 7 | 8 | 8 | 17 | 13 | 7 | 14

## Slide 8
Bug-fix for Table A.4 of JCTVC-U1005-V2
Table A.1 – Allowed values for syntax elements in the screen content coding extensions profiles
Profile for which constraint is specified | chroma_format_idc | bit_depth_luma_minus8 and bit_depth_chroma_minus8
Screen-Extended Main | 0 | 0
Screen-Extended Main 10 | 0 | 0..2
Screen-Extended Main 4:4:4 | 10 or 32 | 0
Screen-Extended Main 4:4:4 10 | 10 or 32 | 0..2

## Slide 9
Conclusion
Modification is proposed for MaxDpbSize calculation for Screen-Extended Main 10 profile and Screen-Extended Main 10 4:4:4 profile to account for bit-depth and chroma format.
We propose to adopt the proposed approach in HEVC SCC Draft.
Additionally a bug-fix is proposed to Table A.4 for Screen-Extended Main 4:4:4 and Screen-Extended Main 4:4:4 10 profiles.

## Slide 10: Thank You